## Slide 1: Liaison presentation to SC6 regarding Internet Security
Date: 2012-February-13
Authors:

## Slide 2: Requirements for designing Ethernet security
IEEE 802.1 Security Task Force

## Slide 3: Agenda
  Overview
  Ethernet Security Criteria & Threat Analysis
  802.1 Fabric
  802.1 Security Architecture
  Applying Security Criteria to 802.1
  Applying Security Criteria to TLSec
  Conclusions

## Slide 4: Overview
This presentation describes some important items that all Ethernet security features need consider when they are designed
It then shows how this criteria was applied in the development of the current IEEE 802.1 security mechanisms
It also show how this criteria is applied to TLSec as described in N14402, N15083, and N15084
  From the limited available information there seem to be some gaps in how the criteria is met by TLSec, and we mention those.

## Slide 5: Ethernet security criteria
When designing any network security system it is necessary to define strong security methods and protocols.
When develop a security system for Ethernet, there are some additional criteria that are very important to address
  Threat Model/Analysis
  Working with IEEE 802.1 Bridging/Switching
  Fitting into Switching/Bridging Equipment Architectures
  Fitting many Network Architectures

## Slide 6: Threat Model/Analysis
It is important to consider the threats to the security protocols
  Threats of attackers entering the network at any port in the network must be considered
  Threats to the bridged/switched network itself must be considered as well as threats to resources connected to the network
    If protocols running in the links in the network are not protected, then protected data traffic is still vulnerable to attack

## Slide 7: IEEE 802.1 Bridging/Switching
Ethernet technologies change rapidly, and new methods of bridging/switching are frequently introduced to adapt to the new technologies
Ethernet security features must fit carefully into the IEEE 802.1 Architecture in order to be accommodate current and future bridging/switching technologies
  This requires a thorough understanding of this architecture in order to build security technologies that will be relevant in the future
  It is also necessary to understand the boundaries of the architecture and to know which problems are within and without the scope of the architecture

## Slide 8: Switching/Bridging Equipment Architecture
It is important to design security features that do not add significant latency to the throughput of data
  Note that link speeds of 40Gbps and 100Gbps are being designed today
It is important to understand the capabilities and limitations of Ethernet MAC chips
  Cost effective chips have limited capabilities for storing cryptographic keys and policy, and limited capability for switching between keys

## Slide 9: Network Architectures
It is important to recognize that there are many ways to configure Ethernet networks
  It is also important to handle point to point, multicast, and broadcast frames
Designing one set of security methods that work in each of the configurations and with all frame types is vital in order for it to be effective.

## Slide 10: IEEE 802.1 Security
Following is an overview of the current security features. An explanation of these features are available in N14793.
Then we apply the criteria mentioned in the previous slides to the IEEE 802.1 security features.

## Slide 11: IEEE 802.1 Security Architecture
The IEEE 802.1 Security Architecture for Bridged/Switched networks includes
  IEEE 802.1X-2010 – Port-Based Network Access Control & Key Management
  IEEE 802.1AE-2006 - MACsec
  IEEE 802.1AR-2009 – Secure DevID
These three standards work together to provide a consistent security architecture that works in today’s networks
  They have been designed to work in tomorrows networks as well
  They are the result of several iterations of security solutions, and so have the benefit of many lessons learned. We are mentioning some of those lessons learned today for you to consider.

## Slide 12: Applying the criteria to the IEEE 802.1 Security Architecture
Threat Model: Protects against threats to both the network edge and the core. The security features can be automatically applied at each link according to the risks facing that link.
  The same security features are are suitable to be applied at all ports and using the same policy, whether they be at the edge and/or ports in the core.
  Or, a network administrator can choose which ports in the network have threats and just apply security on those ports
Compatibility with IEEE 802.1 Bridging/Switching: Protects bridging/switching protocols as well as user data on each link where security is required

## Slide 13: IEEE 802.1 Security Architecture
Switching/Bridging Equipment Architecture: Fits within the capabilities of bridged/switched equipment designs up including 40Gbps and 100Gbps links with low latency
  This is done using state of the art, internationally reviewed, adaptable, and conventional cryptography. This is very important in order to achieve broad acceptance in the marketplace
  Ethernet ports supporting MACsec and software supporting IEEE 802.1X is available, and new network devices are supporting these security features today
Network Architectures: Is designed to fit into the IEEE 802.1 Architecture, and so can be used by all conforming bridged/switched networks

## Slide 14: TLSec
TLSec is described in N14402, N15083, and N15084.
From these descriptions there seem to be some gaps between the TLSec method and the criteria mentioned earlier, and the next slides mention those gaps.
  Many of them are related to the generation, distribution, and storage of cryptographic keys, which are crucial to having a secure and scalable system

## Slide 15: Applying the criteria to TLSec
Threat Model: Focuses on inside threats between selected devices, which may cross one or more bridges/switches
  Because of key management and storage issues it may not be suitable for network edge ports.
Compatibility with IEEE 802.1 Bridging/Switching: The encrypted frames cross bridges/switches, and so they cannot protect the bridging/switching protocols underlying the network
  This leaves the network open to a wider a wider variety of denial of service attacks

## Slide 16: Applying the criteria to TLSec
  Switching/Bridging Equipment Architecture: TLSec seems to be designed to use many keys for many destinations
    This can require a large key store (e.g., at least one key for each destination), and keys have to be referenced and used without introducing network latency.
    Most encryption systems compute and store the key schedules for cipher keys rather than the keys themselves. Each key requires Kilobytes of memory that must be available to the MAC level function performing encryption. This is commonly a serious constraint to designers.
    TLSec requires many more resources than is available in switches/bridges, and will be a substantial architectural hurdle as link speeds and network sizes increase.

## Slide 17: Applying the criteria to TLSec
  Network Architectures: To be successful, TLSec must support more than peer to peer traffic with pair-wise keys
    Keys generated from TePA must be shared with multiple peers in order to protect multicast or broadcast
    Sharing keys between devices on different networks leads to additional threats and key management complexity

## Slide 18: Conclusions
When designing security for Ethernet networks, it is important to take into consideration both the architecture of that network and the network configurations that can be used
IEEE 802.1 security and TLSec are addressing the same architectures and network configurations, so the same requirements apply to both
IEEE 802.1 security was carefully designed to maximize the value and level of security for a diverse variety of bridged/switched networks
As always, IEEE 802 would encourage open discussion on security criteria, architectures and alternative solutions in the interests of developing and standardizing the most commercially relevant and robust security standards.