## Slide 1: ELLA: Proposed Aspects of IEEE Std 802 Revision
Roger Marks (EthAirNet Associates)
roger@ethair.net
+1 802 capable
7 October 2021
Mentor DCN 802.1-21-0060-00-ICne

## Slide 2: IEEE Std 802 - History
IEEE Std 802-1990
IEEE Std 802-2001
  IEEE Std 802a-2003: Playpen EtherTypes
  IEEE Std 802b-2004: OID hierarchy
IEEE Std 802-2014
  IEEE Std 802c-2017: Local MAC Address Usage
  IEEE Std 802d-2017: URN allocation
  P802f: YANG Data Model for EtherTypes
    WG ballot opened, June 2021
Procedurally, revision should follow before further amendments

## Slide 3: IEEE Std 802 - Contents
Overview, Scope, Purpose
Normative references
Definitions
Family of IEEE 802 standards
Reference models (RMs)
General requirements for an IEEE 802 network
IEEE 802 network management
MAC addresses
Protocol identifiers
Allocation of OID values
Allocation of URN values
Annex A (informative) Bibliography
Annex B (informative) Reference models for IEEE 802 standards
Annex C (informative) Examples of bit ordering for addresses
Annex D (informative) List of IEEE 802 standards
Annex E (informative) History
[Annex F: (informative) YANG representation example (P802f)]

## Slide 4: Proposal on how to revise
4. Family of IEEE 802 standards (pp 7-10)
  4.1 High-level view of IEEE 802 networks: revise; explain the commonality
  4.2 List of applications: delete
  4.3 Internationalization: minimize
  4.4 List of standards and projects: delete
5. Reference models (RMs) (pp 11-18): replace with LL Service & Architecture
  5.1 Describes Link Layer (LL) as one LLC over various MACs: replace
    Describes media-independent handover: delete
  5.2 Reference model for end stations (LLC/MAC/PHY): replace
  5.3 Interconnection: replace
    Barely mentions VLANs or priority; no reference to their role in architecture
6. General requirements for an IEEE 802 network (p 19)
  Replace with conformance-related description of LL service provided to client
7. IEEE 802 network management (pp 20-21): replace
8. MAC Addresses (pp 22-27, plus pp 12-19 of 802c)
  Revise; merge with LL Service and Architecture
9. Protocol identifiers (pp 28-34)
  Lists many 802.3 MAC frame formats, without assigning fields to layers
    Who’s responsible for adding and stripping those fields?
  Replace; merge with LL Service and Architecture

## Slide 5: IEEE Std 802 – Proposed Revision
Overview, Scope, Purpose
Normative references
Definitions
Family of IEEE 802 standards
Network and application scenarios served by IEEE 802
IEEE 802 Link Layer Service and Architecture
General requirements for an IEEE 802 network
IEEE 802 network management
Allocation of OID values
Allocation of URN values
Annex A (informative) Bibliography
Annex B (informative) Reference models for IEEE 802 standards
Annex C (informative) Examples of bit ordering for addresses
Annex D (informative) List of IEEE 802 standards
Annex E (informative) History
Annex F: (informative) YANG representation example

## Slide 6: Link Layer Service and Architecture
Layers, sublayers, and SAPs
  LLC & LSAP
  MAC & MSAP
  PHY
  VLAN-aware end station
Link Layer (LL) service speciﬁcation
  LL Service User and LL Service Provider
  LL modes
    Service Characteristics
      Transparency
      Data loss, data insertion, data duplication, misordering, priority, QoS, time-sensitivity, flow control,…
  LL Service primitives
  LL Service parameters
  LL Service sequences of actions and events
MAC service specification
  Refer to IEEE Std 802.1AC
LSAP addresses and protocol discrimination
MAC address
Bridging and relay architecture