## Slide 1: Elastic Ethernet based on Converged Switch
Huajie Bao (baohuajie@huawei.com, Huawei)
Jiang Li (lijiang3@huawei.com, Huawei)
Kaiyun Qin (qinkaiyun@baosight.com, BAOSIGHT)
2022-6-2
Notes: https://www.ieee802.org/1/files/public/docs2022/new-Schlechter-Common-TSN-0222-v01.pdf

## Slide 2: Background
Regarding Elastic Ethernet, several presentations were discussed:
  2021-05-26 Elastic Ethernet based on Converged Switch
    Converged switch
  2021-05-16 Industrial Network based on Convergent & Elastic Ethernet (presented to 60802 Task Group)
    Weak determinism
    Centralized management
    Extreme low latency / jitter
  2021-05-06 Convergent & Elastic Ethernet Networking for Industry (presented to 60802 Task Group)
    Convergent industrial network based on Ethernet
  2021-04-07 Elastic Ethernet Networking for Industry
    Elastic Ethernet framework
  2021-11-18 Low Latency Discussion for Ethernet Networking
    Extreme low latency / jitter analysis
This presentation further discusses the Converged Switch including a refined study item proposal.

## Slide 3: An Example of EtherCAT Network with Star Topology
EtherCAT uses a logical ring topology but can be deployed with a physical star topology.
The basic principle is that internally the EtherCAT frames continue to be transported in a logical ring:
  the EtherCAT master sends the frame on the port 0 of the EtherCAT junction
  this frame passes each port & each slave once,
  and is returned to the master through port 4 & port 0.
But the EtherCAT junction cannot be used as an Ethernet bridge.
Is it possible to forward EtherCAT frames & standard Ethernet frames simultaneously in a converged forwarding device?
EtherCAT
Junction
Master
Slave
Slave
Slave
Slave
Port 0
Port 1
Port 2
Port 3
Port 4

## Slide 4: More Complicated Scenarios
Different production line use different industrial networks via different industrial frame forwarding devices.
Each switch node connect the devices as star topology.
Nearby some switch nodes, there are some Ethernet switches / stations or devices of other industrial network.
Is it possible to forward EtherCAT frames, PROFINET frames & standard Ethernet frames simultaneously in a converged forwarding device?
EtherCAT
Junction
Master
Slave
Slave
Production Line 1
Production Line 2
Slave
Slave
PROFINET
Switch
PLC
Device
Device
Device
PROFINET
Switch
Device
Ethernet Switch
EtherCAT
Junction
Slave
Device
PROFINET
Switch
Ethernet Switch
Ethernet station
Ethernet station
Ethernet station
Ethernet station
Slave
Device
EtherCAT
Junction

## Slide 5: Converged Switch in Isolated Networks
The converged switch simultaneously forwards standard Ethernet frames, connects all EtherCAT devices in EtherCAT domain, and connects PROFINET devices I PROFINET domain.
The appropriate forwarding method is based only on the port, and the converged switch is configured based on the network attached there.
Production Line 1
Production Line 2
EtherCAT
Junction
Master
Slave
Slave
Slave
Slave
PROFINET
Switch
PLC
Device
Device
Device
Device
Converged Switch
Slave
Device
Ethernet station
Ethernet station
Ethernet station
Ethernet station
Slave
Device
EtherCAT
Junction
PROFINET
Switch
Ethernet Switch
PROFINET domain
EtherCAT domain

## Slide 6: Converged Switch in Mixed Networks
The converged switch may need to support mixed networks.
Each access port (to a station) only carries a single frame type for a specific network according the station connected.
The (red) inter-switch link between the converged switches carries a mix of frame types.
The appropriate forwarding method is not determined by the port only; the frame type should be considered to select the forwarding rule.
The inter-switch link is a shared resource, and the Converged Switch may need to allocate the resource to assure the QoS for each network.
Future end stations may need to support mixed networks; e.g. Ethernet control messaging to an EtherCAT slave.
Production Line 1
Production Line 2
EtherCAT
Junction
Master
Slave
Slave
Slave
Slave
PROFINET
Switch
PLC
Device
Device
Device
Device
Converged Switch
Slave
Device
Converged Switch
Ethernet station
Ethernet station
Ethernet station
Ethernet station
Slave
Device
Forwarding Policy
Traffic type identification
Forwarding table
Forwarding
Forwarding Policy
Traffic type identification
Forwarding table
Forwarding

## Slide 7: QoS of Traffic Through the Inter-Switch Link
As the network scales out, it’s important to manage the resources to assure the QoS.
Centralized Management
  Collect attributes and QoS request
  Compute resource utilization, deadline, path routing etc. for each request
  Allocate resources for each request
  Distribute the result of allocation to each converged switch
  Adjust quickly as the network scales out or is updated
Improve the forwarding delay
  Cut-through forwarding (required for EtherCAT)

## Slide 8: The Pros & the Cons of Converged Switch
Category | Pros | Cons | Potential Solution
Forwarding | One category of switch supports multiple scenarios | Challenge to support forwarding modes different from standard Ethernet Extra switching may increase latency in comparison to physical ring Challenge to assure QoS, to avoid the shared resource conflict between different kinds of traffic | To support different forwarding modes based on converged switch with new designed forwarding table Unified to scheduling timeline and allocate bandwidth resources for different kinds of traffic
Management | Centralized management based on converged switch leads to the overall effectiveness (e.g. proper traffic routing) | Challenge to improve the management process and corresponding tool to mitigate complication of management | To provide unified tool to implement the management & extension functionality
Extension | To plan from the whole viewpoint, and to be good to get the optimal extension solution | Challenge with network reconfiguration | 
Future evolution | To be ease to implement communication across different networks, e.g. Ethernet control message from IT application to PLC, or PLC to PLC of different industrial network for coordination across production line | - | -

## Slide 9: Proposal for Nendica Study Item
For Nendica to initiate a study item on Converged Elastic Ethernet Network
To be studied | Industrial requirements for elastic topology / forwarding. Feasibility of assuring QoS for all devices connected by the converged switch. Feasibility of scheduling. Feasibility of centralized & effective management / scheduling. Other related aspects (high available, security, etc.) requested by industrial scenarios.
Deliverable | An informal report documenting Summary requirements of industrial scenarios unsatisfied by current industrial networks Potential benefits from Converged Elastic Ethernet Network Impact & optimization of evolving technologies Possible standardization needs Possible recommendation to initiate a work item
Leader | Huajie Bao (Huawei), or other volunteers
Timeline | Start in June 2022, finish in Nov 2022 Draft version Aug 2022 Call for comments Sept 2022 Complete Study Item Report Nov 2022
Work schema | Weekly meeting or on-demand meeting Encourage all contributions