## Slide 1: Updates of 1-24-0031-02-ICne
Presenter: Yuehua Wei
(wei.yuehua@zte.com.cn)

## Slide 2: Updates
Addressed comments collected from the Nendica meeting held on 2024-07-18：the benefits of Link Layer Retransmission（LLR） should be quantified.
  Replace RS(544,514) with light weighted FEC and LLR
Added one more co-author：Lv Yong
Added more references.
Ver02：https://mentor.ieee.org/802.1/dcn/24/1-24-0031-02-ICne-availability-challenges-and-requirements-of-aicn.docx

## Slide 3: Recap
https://mentor.ieee.org/802.1/dcn/24/1-24-0043-01-ICne-brief-introduction-of-updates-to-1-24-0031-00-icne.pdf

## Slide 4: The benefit quantization of light weighted FEC and LLR——parameters(1)
Take IEEE802.3 400GE as an example
  The pre-FEC BER is 2.4e-4[8]
  It is based on PAM-4 signaling with RS(544,514) as its FEC scheme
Suppose transit N 64-octet frames on a 150 meters 400 Gb/s Ethernet optical fiber link
  1 frame loss every N frames, N = 1/FLR
  RTT ≈ 2*（Link latency + (Transmitter + Receiver Latencies)） ≈ 2000 ns

## Slide 5: The benefit quantization of Light-weighted FEC and LLR——parameters(2)
Replace RS(544,514) with RS(274,258) plus link-layer retransmission mechanism
The latency of a frame equals the latency of a codeword，including codeword encoding time，decoding time， correction time and codeword storage time
Latency of LLR including the latency of a frame and a RTT
Chart: BER-IN
| 2.8E-3 | 1.5E-3 | 8.9999999999999998E-4 | 5.5000000000000003E-4 | 3.6000000000000002E-4 | 2.4000000000000001E-4 | 1.7000000000000001E-4 | 1.2E-4 | 9.0000000000000006E-5 | 6.0000000000000002E-5 | 4.0000000000000003E-5
RS(272,258,t=7) | 0.0018 | 0.00017075 | 1.0763e-05 | 4.6253e-07 | 2.4098e-08 | 1.2406e-09 | 9.2475e-11 | 6.4026e-12 | 6.8734e-13 | 2.8761e-14 | 1.1758e-15
Pre-FEC BER | 5.50E-04 | 3.60E-04 | 2.40E-04 | 1.70E-04 | 1.20E-04
Post-FEC BER | 4.63E-07 | 2.41E-08 | 1.24E-09 | 9.25E-11 | 6.40E-12

## Slide 6: Calculation process and result
 | RS(544,514) | RS(274,258) + LLR
Latency of a codeword/frame | Tcwa = 3+3+31+25.6 = 62.6ns[7] | Tcwb = 3+3+31/2+25.6/2 = 34.3ns[7]
Post-FEC frame loss rate | FLRa =1.7*10-12[8] | FLRb = 64*8*1.24*10-9= 6.35*10-7
Frame numbers | N = 1/(FLRb-FLRa) = 1.57*106 | 
Retransmitted frame numbers | Nra = 0 | Nrb = 1
Latency cost of N frames | Ta = Tcwa*N = 9.83*107 | Tb = Tcwb*(N+1) + RTT*1 = 34.3*(1.57*106 +1) + 2*103= 5.39*107 LLR time cost is about 2us per 1.57*106 frames.
Latency benefit per N frames | Tn = Ta - Tb = 4.44*107 ns | 

## Slide 7: Conclusion
Light weighted FEC significantly save latency of frame transmission
  The frame loss rate increasing accordingly could be fixed by LLR
    The latency cost of LLR is insignificant
Use light weighted FEC plus LLR is a reasonable solution

## Slide 8: References
https://www.ieee802.org/3/dj/public/adhoc/optics/0423_OPTX/brown_3dj_optx_01b_230413.pdf
IEEE802.3-2022
https://www.ieee802.org/3/bs/Objectives_16_0317.pdf

## Slide 9: Thank You!