## Slide 1: What Should Be in an IAPP?
Bob O’Hara
Informed Technology, Inc.

## Slide 2: Previous Submission on IAPP
94/17 – The Provisions Required for Handoff, Wim Diepstraten
95/188 - How Far Should an ESS Extend?, Michael Fischer
96/108 - Draft Inter Access Point Protocol (IAPP) Specification, Wim Diepstraten and Mike Trompower

## Slide 3: 94/17 – Provisions for Handoff
New AP must inform old AP when a station reassociates
New AP must inform DS of the new location of the station
Old AP may forward buffered frames for reassociating station to new AP

## Slide 4: 95/188 ESS Extent
Deals mostly with the definition of and extended service set
  Proposes that an ESS comprise only layer 2 devices
Introduces “More Extended Service Set (MESS)”
  Proposes that this be used for any ESS including items above layer 2
Indicates that an IAPP would be a fruitful area to standardize

## Slide 5: 96/108 Draft IAPP Specification
Defines two protocols
  Announce protocol provides
    Identification of active APs
    AP announcement of capabilities and configuration
    AP “heartbeat”
    Coordinated management and configuration of APs
  Handover protocol provides
    Notification of old AP that a station is reassociating with a new AP
    Update of layer 2 DS devices to properly forward frames to reassociating station
Allows proprietary extensions

## Slide 6: 96/108 Draft IAPP Specification
Announce and handover protocol parameters
  SSID
  BSSID
  Old BSSID
  Mobile station address
  IAPP capabilities and status
  Periodic announce interval
  Station stale-out time
  Handover timeout
  PHY type
  Regulatory domain
  Channel
  Beacon interval

## Slide 7: What Should Be In Today’s IAPP?
A handover protocol
  Terminates association with old AP
  Updates layer 2 DS devices
  Provides for optional forwarding of buffered frames

## Slide 8: What Might Be In Today’s IAPP?
Standardized AP configuration/management
  Enumeration of APs in an ESS
    Layer 2 only?
  Configuration of basic AP capabilities
  Goal of “no touch” out-of-box experience
    After configuration of one AP?
  AP “heartbeat”
    Could be useful if there is a way to integrate it with standard network management consoles