## Slide 1: Collision Avoidance in Overlapping BSSs of 802.11 WLAN
Gerard G. Cervello and Sunghyun Choi
Philips Research
Briarcliff Manor, New York

## Slide 2: Overlapping BSS Issue
Independent from core .11e MAC proposals
  As long as they are based on PCF
Desired/proposed mechanisms
  Dynamic channel selection (00/195r2)
  Channel sharing among overlapping BSSs
  Error correction/control and scheduling
Channel sharing with feedback system
  Based on Philips (00/108) and NWN (00/113) proposals presented in May

## Slide 3: Three Overlapping Situations
Situation A: STA1,1 is not reachable from AP2

## Slide 4: Thee Overlapping Situations
Situation B: STA1,1 is reachable from AP2

## Slide 5: Three Overlapping Situations
Situation C: both APs are reachable to each other

## Slide 6: Recapture of NWN Proposal
Contention-Free Burst (CFB) for situation C
  Enhancement of Clause 9.3.3.2
  Modified Duration/ID field of CF frames
CFP
Beacon or CF-End
Contention Free Burst
CFB Backoff
deferred backoff
CFP
BSS 1
BSS 2
CP
RTS/CTS during CFP for situation A
  Philips proposed the same in May

## Slide 7: Problems of NWN Proposals
RTS/CTS
  Will not update NAV of STAs in overlapping BSSs in CFP
Possible collision after deferral
  After a CFB, BSSs can end back-off at the same time
Channel sharing fairness
  A BSS may never grab the channel: blank CFP

## Slide 8: Enhanced CFB Mechanism
Overlapping Network Allocation Vector (ONAV)
Physical channel sensing during CFPs
Channel sharing fairness

## Slide 9: Overlapping NAV (ONAV)
Two NAVs
  Legacy STAs w/ only NAV
  Enhanced STAs (ESTAs) w/ both NAV and ONAV
ONAV updated w/ same rule for NAV by
  All frames from neighboring BSSs
ESTA does not transmit/respond
  Not even with (CF-)ACK and CTS
  If ONAV is not ZERO
Enhanced PC (EPC) will contend for a CFB
  With zero ONAV, even with non-zero NAV

## Slide 10: Usage of ONAV (Situation C)

## Slide 11: Physical Channel Sensing
Channel sensing by PC in CFP after
  First frame (e.g., beacon) transmitted in CFB/CFP
  Every CF-poll (+data+…)

## Slide 12: Fair Channel Sharing
Different contention window size for channel-releasing PC
Blank CFB: need to adjust CFBMaxDuration

## Slide 13: RTS/CTS during CFP
Complement to CFB for situations A
  When APs cannot hear to each other
Can work as a channel probing mechanism
  To prevent collisions due to bursty errors

## Slide 14: Operations of RTS/CTS
Data + CF-Ack + CF-Poll: not used
RTS actually not updating ONAV
STA1,1 calculates actual “Duration” per RTS
dfd
gfgf

## Slide 15: Feedback System
ESTA reports existence of other BSSs and frame reception statistics to its AP
  Number of frames received (in error)
  “To DS” and/or “From DS” frames received
  Used to determine whether to use RTS/CTS and more
  Used also to initiate a dynamic channel selection (00/195r2)

## Slide 16: Summary of Proposal
Mechanism of RTS/CTS in CFP
  Idea about when to use and its limitations
Introduction of Overlapping NAV (ONAV)
  Also with how to use it
Physical channel sensing during CFP
  After first frame (of a CFB) and CF-poll frames
Consideration on channel sharing fairness issue

## Slide 17: Open Questions
How to handle situation B?
  Neither CFB nor RTS/CTS works well
  Avoid situation B via Dynamic Channel Selection!!!
Fairness issue?
  How to handle the fairness without explicit communication between APs?