## Slide 1: Suggested Phase Noise Model for 802.11 HRb
Mark Webster and Mike Seals
Intersil Corporation
September, 2000

## Slide 2: Overview
This presentation recommends a phase-noise model for 802.11 HRb proposals.
Phase noise impacts packet-error-rate.
The model is a fair representation of phase noise behavior and “ideal” carrier recovery loops.
The model is easy to use.
Used by 802.11a.

## Slide 3: VCO Phase Noise and Ideal 2nd-order Carrier Recovery Loops
2nd-order
PLL
VCO
-20 dB/dec
VCO
dBc/Hz
freq
+20 dB/dec
PLL
Trk
Resp.
freq
-20 dB/dec
Output
Composite
freq
Assumes Ideal
Phase Detector
F3dB
F3dB

## Slide 4
Equivalent Phase Noise Model
1st-order
LPF
AWGN
-20 dB/dec
Output
Composite
freq
F3dB
-20 dB/dec
1st-
order
LPF
freq
F3dB
AWGN
PSD
freq
Matches Composite
Hardware Effect
Startup
Transient

## Slide 5: Two Free Parameters
-20 dB/dec
Composite
Phase Noise
freq
F3dB
Pssb dB
Free Parameters
1. 3 dB bandwidth
2. SSB Phase noise level at 0 Hz (or RMS Phase noise)

## Slide 6
Equivalent Noise Bandwidth of 1-pole Butterworth Filter used for phase noise shaping.
R
C

## Slide 7
Compute RMS Phase Noise as Function of Flat SSB Power Pssb dB
-20 dB/dec
Phase
Noise
freq
F3dB
Pssb dB

## Slide 8
Matlab Code Usage
% Settable parameters.
vcoPnDegRms = 1; % Desired RMS phase error in degree.
vcoPnBwHz = 10e3; % LPF 3 dB bandwidth in Hz.
nSamples = 1e6; % Length of transmit signal (packet).
chanSampRateMHz = 44; % Signal (packet) sample rate.
%------------------------------------------------------------------*
% Monte-Carlo simulation to verify model.
% Note, the 1-pole filter has a start-up transient.
% But, that is OK for examining effects of phase deviations.
% Output samples have the form exp(j*radian_deviation).
%------------------------------------------------------------------*
% Generate a VCO sample waveform.
vcoPnPhasor = PhzNoiseGen( vcoPnDegRms, vcoPnBwHz, ...
nSamples, chanSampRateMHz);
% Phase-noise distort signal
outSig = inSig .* phzNoise.

## Slide 9: Matlab Code for Generator (page 1 of 2)
%**********************************************************************
% PhzNoiseGen.m
%
% VCO Phase Noise modeled using a 1-pole Butterworth filter to
% give 20 dB/dec slope. Gaussian white noise is passed
% through the Butterworth filter, with the correct level
% to generate the radian variation. Output samples have
% the form exp(j*radian_deviation).
%
% Input parameters:
%
% vcoPnDegRms % Desired RMS phase error in degrees.
% vcoPnBwHz % LPF 3 dB bandwidth in Hz.
% nSamples % Size of output vector.
% chanSampRateMHz % Simulation sample rate.
%
% Output parameters:
%
% phzNoise % nSamples length complex vector.
% % Each sample has abs() equal to 1;
% % Example usage:
% % outSig = inSig .* phzNoise.
%
%
% Mark Webster September 19, 2000
%**********************************************************************
function phzNoise = PhzNoiseGen( vcoPnDegRms, vcoPnBwHz, nSamples, chanSampRateMHz)

## Slide 10
% Design VCO phz noise filter.
% 1-pole Butterworth.
vcoPnNPoles = 1; % Gives 20 dB/dec phase-noise roll-off.
chanSampRateHz = chanSampRateMHz * 1e6;
Wn = 2 * vcoPnBwHz / chanSampRateHz;
[vcoPnB,vcoPnA] = butter( vcoPnNPoles, Wn);
% Compute the resulting RMS phz noise in dBc/Hz.
vcoPnRadiansRms = vcoPnDegRms * pi/180;
vcoPnVar = vcoPnRadiansRms ^ 2;
excessBw1PoleButter = pi/2; % Relative excess bandwith of 1-pole filter.
vcoPnPwrPerHzOneSided = vcoPnVar / (vcoPnBwHz * excessBw1PoleButter) ;
vcoPnPwrPerHzSsb = vcoPnPwrPerHzOneSided / 2;
vcoPnLvldBcPerHzSsb = 10 * log10( vcoPnPwrPerHzSsb );
% Compute AWGN source level feeding Butterworth filter.
awgnPnPwr = vcoPnPwrPerHzSsb * chanSampRateHz;
awgnPnRms = sqrt(awgnPnPwr);
% Generate a VCO phase-noise sample waveform.
nPnSamps = 100000;
awgnPn = awgnPnRms * randn(nSamples,1);
coloredGaussianPn = filter(vcoPnB,vcoPnA, awgnPn);
phzNoise = exp(j*coloredGaussianPn);
Matlab Code for Generator (page 2 of 2)

## Slide 11
Matlab Code for Test Shell (page 1 of 3)
%**********************************************************************
% MainPhzNoiseTest.m
%
% This routine tests the procedure for simulating phase noise
% using 1-pole LPF spectral shaping. In this routine, the user
% sets
%
% (1) The 3 dB bandwidth of the LPF filter
% (2) The desired RMS phase noise in degrees.
% (3) The number of phase noise samples desired.
% (4) The simulation channel sample rate.
%
% Simulation verifies the model.
%
% Mark Webster September 9, 2000
%**********************************************************************
clear all
close all
% Settable parameters.
vcoPnDegRms = 1; % Desired RMS phase error in degree.
vcoPnBwHz = 10e3; % LPF 3 dB bandwidth in Hz.
nSamples = 1e6; % Length of transmit signal (packet).
chanSampRateMHz = 44; % Signal (packet) sample rate.

## Slide 12
%------------------------------------------------------------------*
% Monte-Carlo simulation to verify model.
% Note, the 1-pole filter has a start-up transient.
% But, that is OK for examining effects of phase deviations.
% Output samples have the form exp(j*radian_deviation).
%------------------------------------------------------------------*
% Generate a VCO sample waveform.
vcoPnPhasor = PhzNoiseGen( vcoPnDegRms, vcoPnBwHz, ...
nSamples, chanSampRateMHz);
% Estimate the VCO's output phz noise in degrees RMS.
degRx = angle(vcoPnPhasor) * 180/pi;
degRmsEst = sqrt(mean(degRx.^2));
Matlab Code for Test Shell (page 2 of 3)

## Slide 13
%--------------------------------------*
% Plot and print stochastic results.
%--------------------------------------*
figure
plot(degRx)
grid
xlabel('sample #')
ylabel('Degrees')
str = sprintf('Phz Noise Sample: %2.2f degrees', degRmsEst);
title(str)
disp(' ')
disp('*********************')
str = sprintf('Target RMS phz error (degrees): %d', vcoPnDegRms);
disp(str)
str = sprintf('Estimated RMS phz error (deg) using %d samples: %d', ...
nSamples, degRmsEst);
disp(str)
disp('*******************')
disp(' ')
Matlab Code for Test Shell (page 3 of 3)

## Slide 14
*********************
Target RMS phz error (degrees): 1
Estimated RMS phz error (deg) using 1000000 samples: 1.005964e+000
*******************
Example Test Shell Output
Startup Transient
is OK because we
seek phase deviations

## Slide 15: Summary
Recommend 1-pole phase noise shaping.
Use 3 dB bandwidth of 20 KHz.
Sweep RMS phase noise in degrees.
Show influence on Carrier Degradation in AWGN.
Start-up transient is OK, since deviation.
Caveat: assumes “ideal” carrier recovery loop.