## Slide 1: Texas Instruments Proposal for IEEE 802.11g High-Rate Standard
Texas Instruments
141 Stony Circle, Suite 130
Santa Rosa California 95401
(707) 521-3060, heegard@ti.com
Chris Heegard, PhD, Eric Rossin, PhD,
Matthew Shoemake , PhD, Sean Coffey , PhD
and Anuj Batra , PhD

## Slide 2: Outline
Introduction
  Improved utilization of the 2.4 GHz ISM band for wireless Ethernet
The TI/Alantro 22 Mbps solution
  How it works
  Why it is good
Certification Issues
  Processing Gain
  Jamming Requirements
The ACX101 Baseband Processor
Summary

## Slide 3: Introduction
“Double the Data Rate” Wireless Ethernet

## Slide 4: TI Offers 2x, “Double the Data Rate”
Noise, Multipath Distortion
Data Rate, Mbps
0
5
10
15
20
25
Others
T I
22 Mbps
11 Mbps
5.5 Mbps
2 Mbps
IEEE 802.11b
Additive White Gaussian Noise
  The TI FEC has a “3db” coding gain advantage
Multipath Distortion
  The TI “joint equalizer/decoder” can process much more distortion
  The TI “CCK” solution takes advantage of the receiver

## Slide 5: Why Increase Performance?
Spectrum is rare and valuable
  In order to be efficient it demands the most aggressive practical technical solution
  History: as progress is made, more throughput is achieved
  Example: Telephone modem technology
    Fixed 3 kHz channel
    Initial progress: 300 -> 1,200 -> 2,400 -> 4,800 bits/second
    Progress was stalled until:
      Trellis coding, a form of FEC based on convolutional coding, was developed
      Adaptive signal processing was developed
    Inspired new wave: 9,600 -> 14,400 -> 28,800 bits/second
The Alantro/TI technology provides the next wave in wireless Ethernet performance

## Slide 6: How to Increase Performance?
Shannon
Shannon ( = 11)
Barker 1
Barker 2
CCK 11
PBCC 11
PBCC 22
-2
0
2
4
6
8
10
0
5
10
15
20
25
30
Rate versus SNR
Es/No (dB)
Rate (Mbps)
Increase
Robustness
Increase
Data
Rate
PER = 10-2

## Slide 7: Packet Binary Convolutional Coding
Combines Binary Convolutional Coding with Codeword Scrambling
For 11 (and 5.5) Mbps
  Rate k=1, n = 2 encoder
  64 state
  QPSK (BPSK) modulation
  Dfree^2/Es = 9/2 = 6.5 dB
For 22 Mbps
  Rate k=2, n=3 encoder
  256 state
  8PSK modulation
  Dfree^2/Es = 704/98 = 8.6 dB

## Slide 8: PBCC Components

## Slide 9: BCC Encoder
PBCC-11:
PBCC-22:

## Slide 10: “Symbol Scrambler”
QPSK
Mode
(1 bit per
symbol)
s = 0
s = 1
8PSK Mode
(2 bit per
symbol)
00
00
01
11
10
01
11
10
s = 0
s = 1
000
001
010
011
100
101
110
111
011
000
001
010
111
100
101
110
(y1,y0)
(y2,y1,y0)

## Slide 11: The “s” Sequence
A length 256 sequence generated from a length 16 sequence
  [c0,c1,…,c15] = [0011001110001011]
Periodically extended for >256

## Slide 12: AWGN Performance

## Slide 13: Throughput

## Slide 14: Throughput (cont.)

## Slide 15: Certification Issues
PBCC-22 should be certified under existing rules

## Slide 16: 2 Principle Aspects to Certification
Transmission: The nature of the transmitted signal
  What is the power level?
    Power Spectrum
Reception: Robustness at the receiver
  Depends on the character of the transmitted signal and the sophistication of the receiver
  Processing Gain
    Measured with respect to a reference
    Comparison of Shannon Limits
  Interference Rejection
    CW Jamming Margin
    Narrow Band Gaussian
    Noise

## Slide 17: The Transmitted Signal
Barker 2
CCK 11
PBCC 11
PBCC 22

## Slide 18: The Definition of Spread Spectrum
“I Don’t Know How to Define It, But I Know It When I See It”
  This ignores the long history to the science of digital communications
    Morse, Nyquist, Shannon, Weiner, Hamming, Elias,…
Although one does need to make logical definitions, similar difficulties exist with other important communications parameters
  Signal-to-Noise ratio
  Bandwidth
  Power Spectrum, etc.
Reasonable Definitions Exist (examples to follow)
Is the definition important? NO
  A means to an end --> robust communications

## Slide 19: Massey’s Definition
“Towards an Information Theory of Spread- Spectrum Systems” ,
  Code Division Multiple Access Communications (Eds. S. G. Glisic and P. A. Leppanen) , 1995, James L. Massey.
Defined 2 notions of Bandwidth
  “Fourier” or “Nyquest” Bandwidth
    Relates to Spectrum Occupancy
  “Shannon” Bandwidth
    Relates to Signal Space Dimension
  Spreading Ratio 
    A system is “spread spectrum” if  is large
This definition is mathematically precise and intuitive
  This definition argues that high rate (bits/sec/Hz) systems cannot have significant spreading
A Theorem

## Slide 20: Massey’s Definition Applied to Wireless Ethernet

## Slide 21: Other Notions of Signal “Spreading”
Uncoded Modulation:
Break data stream into small pieces
  map onto independent dimensions
  Noise occasionally causes symbol error ==> data error
Data:
Symbols:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: In FEC Systems, Information is Spread
Coded Modulation:
Have each bit of data affect many symbols
Average out the noise with the decoding
Lesson of Shannon:
  If you are willing to work (compute) then more throughput is possible
Data:
Symbols:
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: PBCC-11 Pathmemory Requirements
To perform within 0.5 dB of optimal requires the decoder to observe received symbols in a window that is > 28 QPSK symbols long
  > 2.5 sec
    @ 11Msps

## Slide 24: PBCC-22 Pathmemory Requirements
To perform within 0.5 dB of optimal requires the decoder to observe received symbols in a window that is > 40 8PSK symbols long
  > 3.6 sec
    @ 11Msps

## Slide 25: Processing Gain
Gain is respect to a reference, an uncoded signal
  CCK-11, PBCC-11 --> QPSK
  PBCC-22 --> 8PSK
Processing gain
  is defined as the difference between the SNR (Es/ No) required to achieve a threshold BER or PER with the reference scheme and the SNR (Es/ No) required to achieve the same threshold BER or PER when the signal is processed.
Processing
  of the signal includes error control coding and de-spreading of the signal.
Repetition or Rate reduction gain
  is the energy gain achieved from the reduction of data rate relative to the reference.

## Slide 26: Processing Gain (cont.)
Coding gain
  is measured on an Eb/ No scale rather than an Es/ No scale. This prevents the apparent increase in performance that has been gained as a tradeoff between Es/ No and rate.
  it is the excess gain from a repetition gain
Bandwidth expansion factor gain
  With ideal pulse shaping, the TI system which operates at 11 Msps, would occupy 11 MHz of bandwidth. However, the signal is spread to a bandwidth of ~20 MHz. This yields a waveform spreading gain of
    ~10 log( 20/ 11)= 2.6 dB.

## Slide 27: P. G. Comparison
Processing Gain = Coding Gain + Rate/Spreading Gain + Waveform/Spreading Gain

## Slide 28: The CW Jamming Margin Test
The ACX101 will pass the existing test in all modes
  Including PBCC-22
This test is useful for eliminating poorly designed systems
  Shows some degree of robustness
Other measures of robustness: (e.g., narrow band Gaussian)
  The PBCC-22 mode is as robust as the CCK-11
  Any reasonable test that CCK-11 passes will be passed by PBCC-22

## Slide 29: The ACX101 Baseband Processor

## Slide 30: The ACX 101 Baseband Processor

## Slide 31: Summary
Alantro/TI has built an extension to the existing IEEE 802.11b standard that is fully backward compatible
The solution will pass the existing FCC rules
  The spectrum is the same as the existing standard
  The ACX101, with PBCC-22, is as robust as existing CCK-11 products
    Will deliver twice the data rate in the same environment
  The 22 Mbps achieves better performance through
    Sophisticated signal and FEC design
    Advanced digital communications signal processing algorithms
The TI solution is the leading contender for the new IEEE 802.11g wireless Ethernet standard