## Slide 1: E-DCF with Backoff Adaptation to Traffic
Mathilde Benveniste
AT&T Labs, Research
Relevant submissions: IEEE 802.11-00/375 (.ppt and .doc); -00/456; -00/457; -01/002; -01/004;
-01/019; -01/117r1; -01/135r1; -01/144

## Slide 2: Backoff Adaptation to Traffic (BAT) - General
Backoff adaptation involves changes in the values in response to traffic congestion
It uses feedback on traffic fluctuations to avoid collisions and reduce idle time
Window Adaptation
Changes the contention window for random backoff values for new packet arrivals or retransmissions
 BAT helps determine the number of active sessions
Residual Adaptation
The residual backoff value of a backlogged station is changed
  ‘Backlogged’ stations are stations with packets pending transmission
 BAT helps avoid collisions and reduces delay during traffic bursts

## Slide 3: Role of the ESTA
Upon joining a BSS or IBSS, or whenever they detect any change in the advertised values of CWSizei, ESTAs set their CWSizei to the value in the EDCF Element.
ESTAs engage in FAT and adjust their CWSizei and residual backoff values mi
ESTAs send one of their CWSizei to the AP in any new frame type under consideration; the CWSizei of any class conveys the same scaling information
Role of the AP
Using CWSizei in the EDCF element, the AP may adjust the contention window in response to traffic conditions.
The new window is used when a new packet arrives or upon retrial of a failed transmission.
The AP may adjust the CWSizei in response to information received from the ESTAs in the BSS on their backoff adjustments

## Slide 4: Scaling Factors
The ‘scaling factor’ C is the coefficient of expansion or compression
C > 1 when scaling up
C < 1 when scaling down
For efficiency scaling occurs at discrete adjustment steps
CR = 1 + R = 1.5 when scaling up with the step R = 1/2
CD = 1/(1+D) = 0.75 when scaling down with the step D = 1/3

## Slide 5: Window Adaptation
Given the scaling up factor CR, the new contention window size becomes
aCurrentCWSize  trunc[CR x aCurrentCWSize + 0.5]
Given the scaling down with factor CD, the new contention window size becomes
aCurrentCWSize  max { trunc[CD x (aCurrentCWSize + D)] , 2 }
Residual Adaptation
When adjusting residual backoff values by fractional adjustment steps
new backoff values must be integer
the ordering of the backoff values must be preserved
new backoff values must be distributed uniformly

## Slide 6: Scaling Up
Given the scaling up factor CR= 1.5
e + f = m x CR
if f = 1/2, m’ = e with prob 1/2
m’ = e + 1 with prob 1/2
if f = 0, m’ = e - 1 with prob 1/6
m’ = e with prob 2/3
m’ = e + 1 with prob 1/6
m
m’
1
2
3
1
2
3
4
5
R=1/2

## Slide 7: Scaling Down
Given the scaling up factor CD= 3/4
e + f = m x CD
if f = 3/4, m’ = e with prob 1/6
m’ = e + 1 with prob 5/6
if f = 1/2, m’ = e with prob 1/2
m’ = e + 1 with prob 1/2
if f = 1/4, m’ = e with prob 5/6
m’ = e + 1 with prob 1/6
if f = 0, m’ = e with prob 1
m
m’
1
2
3
D=1/3
1
2
3
4
5
4

## Slide 8: When to scale
Scaling occurs when deviation from ‘ideal’ conditions exceeds tolerance level indicated by adjustment step.
An estimate of the expected number b1 of backlogged stations with backoff value =1 is maintained
Ideally, we want
b1 = n . p1 = 1
where n is the expected number of backlogged stations
p1 is the probability of having a backoff value =1
Given an estimate of b1,
scale up if b1 is too large n . p1 >= CR
scale down if b1 is too small n . p1 <= CD , n >=2
After scaling, the probability p1 is adjusted
p1  p1 /CR decreases for scaling up
p1  p1 /CD increases for scaling down

## Slide 9: Estimating n
The expected number n of backlogged stations is estimated by monitoring
idle slots, and
successful or failed Contention-Based Transmissions (CBTs)
  [A CBT is a transmission not protected by a NAV]
A new estimate is obtained for each period between two instances of TAT, the end of deferred access
T is the end of idle and start of deferred access

## Slide 10: Basic Scaling Algorithm
Scale up; and
adjust p1
At new TAT,
estimate
b1 = n p1
Scale down; and
adjust p1
Is b1 > = CR ?
Is b1 < = CD ?
YES
YES
New TAT
New TAT

## Slide 11: Estimating n
An estimate of the CBT arrival rate  is maintained for time periods outside PCF
 = N /(T0 - TN )
where N is 4, and (T0 - TN ) time for the last N successful CBTs
Idle period
Using the length of the idle period (TAT - T ), compute the number t of idle slots and
apply the following t times
n0 = n1 ; n1 = n0 . q +  
where  is the slot time and q = 1 - p1
CBT - ‘Success’
When a good CRC is received, or an ACK or CTS follows, update n1 as follows
n1 = n0 . q +  .( +  )
CBT - ‘Failure’
Otherwise, update n1 as follows
n1 = n0 + 2 +  .( +  )

## Slide 12: QoS Differentiation
BAT is compatible with TCMA
All classes are scaled by the same factor
Distributed vs Centralized Monitoring
The stations perform channel monitoring and determine the scaling factors, instead of just the AP
This eliminates the need to transmit a ‘management’ frame for periods as short as necessary for residual backoff adaptation (~5 millisec)
This way, capacity is not lost to ‘management’ overhead, which is incurred at inconvenient times; as at the start of a traffic burst
Backoff adaptation can benefit from knowledge of local conditions in the BSS through distributed monitoring
Distributed monitoring provides BAT in IBSS

## Slide 13: Comparison of BAT to p-Persistent CSMA
BAT can be compared to p-persistent CSMA (the ‘permission probability’ approach)
Similarities:
  They both control the probability of transmission,
  They both use the expected number of backlogged stations
  They both use pseudo-Bayesian stabilisation
Differences:
Upon adjustment of the permission probability, p-persistent CSMA treats all packets the same, independent of age
  Delay jitter is introduced
Upon scaling, Backoff Adaptation to Traffic preserves the ordering of the backoff values, thus older packets are more likely to transmit first
  No added delay jitter

## Slide 14: Conclusions
Backoff Adaptation to Traffic, BAT, increases channel utilisation efficiency and reduces delays without causing delay jitter
It is performed by the stations, thus reducing the channel capacity overhead for that purpose
It utilises information on local conditions in the BSS
It provides adaptation to traffic to an IBSS
It is compatible with TCMA