## Slide 1: Dynamic Frequency Selection (DFS) and Transmit Power Control (TPC) Joint Proposal for 802.11h
S. Choi1, S. Gray2, M. Kasslin2, S. Mangold3 and A. Soomro1 Philips Research1, Nokia Research Center2
and ComNets Aachen University3

## Slide 2: Outline
Dynamic Frequency Selection
Transmit Power Control

## Slide 3: Part I
Dynamic Frequency Selection

## Slide 4: Motivation for DFS
Yes, we need it for ERC
Additionally,…
  DFS can enhance QoS when there exist overlapping BSSs
  DFS can enhance QoS when there exists alien systems in the proximity

## Slide 5: DFS Procedure
Initiation of a new channel selection
Request of a channel measurement by AP
Channel measurement process of STAs
Measurement report from STAs to AP
Decision making by AP
Channel switch announcement by AP
Switch into the new channel

## Slide 6: 1. Initiation of Channel Selection
Four cases of channel selection initiation
  A new BSS is formed by an AP
  BSS w/ no associated STA
  Experience bad channel condition persistently
  Overlapping BSSs detected
Determined by the AP’s measurement and STAs’ voluntary measurement reports
When to initiate will be up to implementation

## Slide 7: 2. Channel Measurement Request
AP requests channel measurements to some STAs to find the best channel to run its BSS
  AP should buffer the downlink traffic for the STAs
New Channel Measurement Request management frame
  Using generic action request frame format
  When, how, and which channel(s) to measure
  Two channel measurement method information elements

## Slide 8: Channel Measurement Request Management Frame
Using generic action management frame from TGe

## Slide 9: Two Channel Measurement Method Information Elements
Basic channel measurement method information
CF channel measurement method information

## Slide 10: 3. Channel Measurement Process
AP measurement should minimize the service disruption
  Measurement during a CFP or after RTS possible
STA moves to channel(s) to measure as requested by AP
Three types of channel measurements
  Detection of other BSSs running in the channel
  CCA Busy fraction
  MSSRI statistics

## Slide 11: Channel Measurement Report Management Frame
Using generic action management frame from TGe

## Slide 12: Channel Measurement Report Information Element
To report results about n channels

## Slide 13: Channel Measurement Report Information (Cont.)
Measurement Summary field
Each octet in Received Signal Strength Range Indicator (RSSRI) Statistics Field

## Slide 14: 4. Measurement Report to AP
Measurement report of STA(s) to AP
May be reported during CP or CFP (per being polled)
Report time limit as specified in the report request frame

## Slide 15: 5. Decision Making by AP
AP make a decision per hearing the measurement reports from STAs
  Whether to move or not
  To which channel if decided to move
  When to move, i.e., in which TBTT
Need to consider sleeping STAs to determine when to move

## Slide 16: 6. Announce of Channel Switch
Need to announce the channel move decision
The decision announced via beacon frames
Announced several times to ensure the decision reception
New channel switch announcement element information

## Slide 17: 7. Switch into New Channel
At the scheduled moment, i.e., TBTT, all STAs including AP change their channel
Can be done by changing PHY MIB using PLME SET
  dot11CurrentFrequency in .11a

## Slide 18: Part II
Transmit Power Control

## Slide 19: Motivation for TPC
Yes, we need it for ERC
Additionally,…
  TPC can extend battery life
  TPC can increase network capacity
  TPC can improve SNR (on a short term basis)

## Slide 20: Overview of TPC Methodology
DCF
  Transmit power for all is sent in the Beacon
  Same power setting is “fair” for STAs using CSMA/CA (i.e., CCA mechanism is key)
PCF, EPCF and HCF
  Transmit power may be different for all STAs where transmit power information is contained in the poll
  Lowering power on a per STA basis will
    Improve battery life
    Improve network capacity
  Increasing power on a per STA basis for a short time can improve frame error rate

## Slide 21: TPC with DCF
New beacon orders are added to accommodate TPC
If STA is incapable of decoding new elements, then TPC commands are ignored (obviously)

## Slide 22: TPC with DCF (2)
New Beacon Orders

## Slide 23: TPC with DCF (3)
First Channel Number: first channel where power setting is valid
Number of Channels: self explanatory
Maximum Transmit Power Level: EIRP in dBm
AP has the discretion to determine how much information to send (minimum requirement is one set of First Channel Number, Number of Channels, and Maximum Transmit Power Level)
Domain Information Element

## Slide 24: TPC with DCF (4)
Maximum Transmit Power Level Field
First Channel Number Field

## Slide 25: TPC with DCF (5)
Power Level Adjustment Information Element
Power Setting Relative to Maximum Field

## Slide 26: TPC with PCF, EPCF and HCF
Power is changed on a per STA basis
Transmit power used by the STA is defined by min(TxPoll, Maximum Transmit Power Level ) where
  TxPoll = MaxTxP+ PwrSetRelMax + TxP
MaxTxP is Maximum Transmit Power Level from the Domain Information Element
PwrSetRelMax is the Power Setting Relative to Maximum from the Power Level Adjustment Information Element
TxP is the delta change in power per STA

## Slide 27: TPC with PCF, EPCF and HCF(2)
New proposed MAC frame format by TGe (shown below)
  PCF: TCID is gone and TxP can be conveyed in the Duration/ ID field
  EPCF: many bits are currently available in TCID field for TxP
  HCF: a little bit of a problem because only 2 bits are currently available in TCID for TxP

## Slide 28: TPC with PCF, EPCF and HCF(3)
TxP: Delta Power Change Setting

## Slide 29: DFS Summary
Basic DFS mechanism proposed for infrastructure BSS of 802.11
Three types of channel measurements
Two new management frames:
  Using {generic} action frames
Four new information elements:
  Channel switching announcement
  Two channel measurement method
  Channel measurement report

## Slide 30: TPC Summary
Meets the minimum requirements of the ERC for transmit power control
DCF
  Flexible solution allowing AP to inform BSS of power setting
(E)PCF and HCF
  Improve network capacity
  Improve battery life
  Improve QoS