## Slide 1: Using the Host Identity Payload for WLAN authentication
Robert Moskowitz
Trusecure Corporation

## Slide 2: Goals
To Introduce HIP
How it works
How is ESP used with HIP
To recommend potential usage scenarios

## Slide 3: What is HIP?
A new, complete Namespace
  A cryptograpically based Host Identity
    DSA the default
    Just a string of bits will add DOS attacks
  ‘Statistically’ Global scope
Support for Anonymity
A payload
A protocol, complete with a state machine
A compressed header for every packet -- ESP Transport
  The ESP Security Parameter Index (SPI) points to the Host Identity

## Slide 4: More on HIP
A 4 packet exchange
  Complete with a state machine
  packets 3 and 4 can carry a datagram
Packets 2 - 4 are signed
Initiator MIGHT be anonymous
  Defends from Man-in-the-middle by ‘knowing’ the responder
    Initiator learns responder’s Identity from HIP B0 packet, DNS, PKI, or out-of-band distribution
Diffie-Hellman exchange to create keying material

## Slide 5: How HIP provides Authentication
Host needs to initiate communication with another
  Access point or peer
Host requests an authentication challenge
  Can be pre-computed and reused over a time delta
Host computes challenge response and sends it
  Can include an authenticated and private datagram
Host receives challenge met response
  Can also include an authenticated and private datagram

## Slide 6: The Host Identity Tag (HIT)
Provides constancy in protocols regardless of asymmetric crypto used
128 bits
Address space segmented similar to RFC 2373
Host Assigning Authority (HAA) field
  22 bits Registered Assigning Authority (RAA)
  40 bits Registered Identity (RI, commonly a company).

## Slide 7: ESP (RFC 1406) Usage
Provides Authentication of every packet back to HIP exchange
  Security Parameter Index (SPI) is 32 bit pointer to 128 bit HIT
ESP header smaller than a HIP header in every packet
  10 bytes minimum for header (depending on padding requirements)
  16 bytes for 32 bit IV and 96 bit HMAC if using DES-HMAC-96 or equivalent ESP transform

## Slide 8: More ESP (RFC 1406) Usage
ESP header smaller than a HIP header in every packet
  ESP is larger than WEP’s 8 bytes
  Close to size of WEP2
ESP usage is ‘Transport mode’
Full strength IPsec privacy with proven security behavior

## Slide 9: Special HIP packets
The HIP bootstrap
  announces system’s HIT and HI to potential Initiators
The HIP Rekey
  Allows unilateral rekeying by sending a new DH key
The HIP new SPI
  Sends a new SPI; needed when the ESP sequence number rolls over

## Slide 10: HIP usage scenarios
Corporate usage
  Repository for Access Point His and HITs
  Repository for mobile node HIs and HITs
Public usage
  Repository for Access Point HIs and HITs
  Either
    Anonymous HIs for mobile nodes (anyone securely in)
    Repository for mobile node HIs (fine-level access control)
SoHo usage
  Out-of-band exchange of HIs and HITs

## Slide 11: Work to be done
HIP uses ICMP messages in an IP world. Need an alternative
Develop reference implementation

## Slide 12: HIP State Machine
Ioo, Roo
Ioo, Roo
Ioo, Roo
I1o, Ro1
I11, R11
Inm, Rmn
Ioo, Rmn
Ioo, Rmn
Ioo, Rmn
Inm, Roo
Inm, Roo
In1, R1n
I1m, Rm1
I1  R
R1  I
I2  R
R2  I
I2  R
R1  I
I1  R
ESP
Packets
I reboots
or times out
R reboots
or times out
Iesp  R
Ricmp  I
After I receives
x ICMPs
NES  R
NES  I
Rrky  I
Irky
 R
Rekeying states
Ioo Initiator at no data packets sent,
none received
Roo Responder at no data packets sent,
none received
I1 or R1 Initial HIP packet from Host
I2 or R2 Second HIP packet from Host
Inm or Rmn Host sent n packets and received
m packets