## Slide 1: Serial Authentication Using EAP-TLS and EAP-MD5
Using EAP-TLS without client-side certificates and EAP-MD5 to distribute 802.11 session keys and mutually authenticate a user and RADIUS server(s)
July 10, 2001, IEEE 802.11 TGi
Albert Young 3Com Corporation Phone: 408-326-6435 e-Mail: albert_young@3com.com
Dan Nessett 3Com Corporation Phone: 408-326-1169 e-Mail: dan_nessett@3com.com
Simon Blake-Wilson Certicom Phone: +1 905 501 3786 e-Mail : sblake-wilson@certicom.com

## Slide 2: Content
Objectives
Overview
State Machines
Protocol
Implementation details
Summary

## Slide 3: Overview of Serial Authentication
Serial Authentication Scheme General Configuration

## Slide 4: Objectives of the Serial Authentication
Flexible
  1st Phase – Network Authentication and Dynamic Key Distribution
  2nd Phase – Protected User authentication
  Server uses user identity to choose EAP method e.g. EAP-MD5, EAP-OTP
  Support future authentication protocols, e.g. DIAMETER, in the 2nd Phase
Secure
  Mutual authentication
  Tx/Rx key pairs for confidentiality and message integrity
  Keys for protecting traffic between WC and AP after the 1st Phase
  Resist to offline dictionary attacks, active and passive attacks
  Graceful disaster recovery in case of compromise

## Slide 5: Objectives of the Serial Authentication
Easy to deploy
  Use standard protocols 802.1x, TLS, RADIUS.
  Compatible with legacy authentication databases
  Can support a common user authentication database for wired/wireless LAN and remote access
  No client-side certificates required
  Quick time-to-market
Light weight on AP and client
Support fast hand-off in roaming
Support anonymity of the user

## Slide 6: Overview of the Serial Authentication
Advertise as authentication suite in Associate Request/Response ..
Cipher suite selection
  1st Phase
  UCSE NOT in .11 management frames
  Utilizes secure cipher suite negotiation mechanisms of TLS
1st Phase
  EAP-TLS protocol
  Authenticates a RADIUS-EAP-TLS server to wireless clients
  Distributes keying material used to protect the wireless side
2nd Phase
  EAP-MD5 as default
  Authenticates the user using a RADIUS-EAP-2ndPhase server
  User identity sent to RADIUS, choose specific EAP protocol associated with the user identity

## Slide 7: Overview
RADIUS-EAP-TLS server and RADIUS-EAP-2ndPhase server can be in a single server
  Can deploy with additional software in existing RADIUS server
For standalone networks, AP emulate the two servers w/o RADIUS protocol

## Slide 8: Overview
Subports allow the serial authentication scheme to use 802.1x unchanged
In AP, 802.1x PAE controls access to an authenticator port using two associated subports.
On successful 1st Phase, the EAP-TLS subport “switch” moves from open to close
On successful 2nd Phase, the EAP-2ndPhase subport “switch” moves from open to close.
Now data can flow between the point-of-attachment and the encrypted controlled port.

## Slide 9: Overview

## Slide 10: State Machines
Wireless Client State Machine
  Refer to Section 4.2 of the proposal
AP State Machine
  Refer to Section 4.3 of the proposal

## Slide 11: Protocol
Refer to section 5 of the proposal

## Slide 12: Protocol and Implementation details
RADIUS attributes used to move info between AP and RADIUS-EAP-TLS server
  802.11-UCSE
  802.11-Keying-Material
TLS ciphersuite identifiers used during 802.11 cipher suite negotiation
Key material derivation from the master secret for each 802.11 cipher suite
Distribution of the identifiers of trusted RADIUS-EAP-TLS servers to wireless clients
  Trusted web site, manual configuration …

## Slide 13: Summary
Secure with well-understood technologies
Quite simple
Easy to deploy – compatible with legacy authentication databases
Quick time-to-market
Flexible
Support fast hand-off
Need more comments to make it perfect!

## Slide 14: Back up slides

## Slide 15: Fast Hand-off and re-authenticate in roaming
Cluster Key concept for compromise containment control of APs that share the same key
Utilizes IAPP
  Registration server return a “cluster” attribute to the new AP s.t. the AP can decide whether this is an Intra-cluster roam or Inter-cluster roam
  Transfer of Context Blob (CB) from old AP to new AP
Intra-Cluster roaming
  CB contains keying material etc used to protect the traffic between the Wireless client and old AP
  CB protected with shared key between APs in the same cluster
Inter- Cluster roaming
  Re-authenticate with Serial Authentication

## Slide 16: Fast Hand-off and re-authenticate in roaming