## Slide 1: Supplementary Functional Requirements for Tgi ESS Networks
Submitted to IEEE802.11 TGi
July 2001
Albert Young, Dan Nessett, 3Com
H. Haverinen, J.P. Edney, Nokia
Simon Blake-Wilson, Certicom

## Slide 2: Reason for this submission
May Meeting issued call for “new technical proposals”
We need a basis on which to compare technical proposals and also evaluate the existing technical decisions
There is confusion over which requirements were adopted previously. Document 00/245r1 has general requirements - but little substantive detail
This document adds a number of additional requirements which are felt to be important for the adopted method

## Slide 3: Structure of requirements
It is assumed that one method will be specified as “mandatory to support”
Might be different mandatory method for ESS and IBSS. These requirements relate to ESS
Requirements presented in three sections:
    All methods must meet some requirements
    Mandatory method must meet additional requirements
    Desirable (but not required) attributes for all methods

## Slide 4: Requirements for all methods
All methods must provide one or more session master key(s) from which other session keys required by packet security methods can be derived.
Fast handoff (<?? ms) must be supported, either inherently by the method or via context transfer to be specified in TGf.
  Subject to further technical discussion.
All methods should conform to current RFC2284 (EAP) & 802.1X
All methods must support mutual authentication between supplicant and network authentication server/s (for example upon association and re-association). For re-association context transfer method may be use to inherit previous mutual authentication.

## Slide 5: Requirements for mandatory method(1)
1. The mandatory method must be resistant to all known active and passive attacks, including dictionary attacks, man-in-the-middle attacks, replay attacks, and interleaving attacks.
2. The mandatory method shall not require a certificate on the client side
3. The mandatory method must conform to IEEE intellectual property policy
4. The mandatory method should allow deployment using a common authentication database for wireless LAN, wireline LAN and remote network access.

## Slide 6: Requirements for mandatory method(2)
1. The mandatory method must be suitable for a range of deployment scenarios such as:
  Mobile device to network in corporate environment
  Mobile device to internet gateway in home environment
  Mobile device to public infrastructure network
2. The mandatory method must be suitable for implementation in access points and client which have low or moderate computational resources. “Low or moderate” computational resources means a class of device for which the following example is indicative:
  On initial association, a 40MIPS access point or mobile terminal with limited RAM must be able to execute the method in 5 seconds or less.

## Slide 7: Requirements for mandatory method(3)
3. The Security capabilities of the mandatory method shall meet or exceed that the required to maintain integrity against both active and passive attacks of 280 work factor and probability of successful bogus authentication (in the absence of 280 work) of at most 2-32
4. The mandatory method must allow the client to roam among access points without advance knowledge of all potential access points available.
5. The protocol used by the mandatory method must be capable of implementation in conjunction with legacy network access databases.

## Slide 8: Desirable Attributes (1)
1. A method should be specified for use in IBSS (ad hoc) networks but this method need not necessarily be the same as the mandatory method for ESS networks
2. In the event that two candidates for the mandatory method offer similar security capabilities, the method with lowest computational resources should be chosen.
3. If it is necessary to reference technical specifications or standards which are outside the scope of control of the IEEE802 exec, such references should not include draft versions or "work in progress"

## Slide 9: Desirable Attributes (2)
4. The method should provide simple disaster recovery in face of various possible compromises including:
      compromise of a client's "credentials"
      compromise of any access point's credentials
      compromise of any authentication server
5. The method should provide anonymity from standpoint of an attacker. In other words the identity of the supplicant should not be available to a third party wireless observer.

## Slide 10: Conclusion
After suitable discussion we propose that the additional requirements be adopted by the Tgi group