## Slide 1: Tgi/Tge Cross-Group MAC Issues
Simon Black, Nokia simon.a.black@nokia.com
Jesse Walker, Intel
jesse.walker@intel.com

## Slide 2: Scope & Purpose
A number of issues have been identified during the letter ballots that span TGi and TGe work
Purpose of this paper is to identify issues for discussion
  some analysis and recommendations given
  no normative text at this stage
Some issues also apply to TGh

## Slide 3: Order of Operations in the MAC Architecture
Where do the new security functions sit with respect to the QoS functions in the enhanced MAC architecture?
Placing security functions above QoS raises issue of reordering
  replay protection designed to cope with worst case reordering, or
  limit maximum reordering in QoS functions, or
  assign replay window to each traffic category.
  Disadvantages of state storage and complexity

## Slide 4: Order of Operations in the MAC Architecture
Placing security functions below QoS raises issue of delay introduced by the cryptographic functions
  May force the use of hardware acceleration
  Hardware may be required for high rate PHYs regardless
  AES timing characteristics probably preferable to WEP
Overall, placing security below QoS would seem to be preferable

## Slide 5: MSDU, or MPDU Encryption
Should the new cryptographic protections be applied to MSDUs, or MPDUs?
Linked to position of the security functions in the MAC architecture
Security functions placed below QoS means MPDU encryption

## Slide 6: MPDU Expansion
New cryptographic protections introduce additional MPDU expansion when compared to WEP protection. Do we expand the maximum MPDU size, or reduce the MSDU payload?
Individual length related issues outlined in main paper
Compatibility with existing implementations suggests keeping service definition constant is the correct approach so the maximum MPDU size will expand
Need to update MIB and clause 7.1.3.5.

## Slide 7: One Level of Cryptographic Protection per Association
The current TGi draft makes provision for one level of cryptographic protection for the entire association and does not permit separate cryptographic protections for each traffic category. Is this acceptable?
It is highly desirable to keep the enhanced security model simple and avoid having to store separate keys and other state for each traffic category.

## Slide 8: Protection of Management Frames
At this stage, TGi is proposing to not to protect the 802.11 header, or MMPDUs. Is protection of other MMPDUs, or header fields required?
Possible that protection may be extended to Disassociate MMPDU and MAC address fields as part of letter ballot comment resolution
Effect of modifying other fields is probably denial of service. There are simpler ways to deny service, so specific protection probably not required.

## Slide 9: Direct STA-STA Communication
The concept of direct communication between stations in a BSS breaks the assumption that the AP can be used to enforce security policy.
Direct communication is limited to that using multicast keys, or not having protection.
A scheme would be possible whereby the AP authorized specific direct STA-STA communication. Would require extension of the key derivation protocol, which is a very significant piece of work.

## Slide 10: Beacon/Probe Response Issues (1)
The Beacon management frame is becoming increasingly overloaded. How should this be addressed?
Include only essential information in the beacon frame (look to use probe and association exchanges for bulk communication).
Separate the beacon and probe request-response mechanisms in the base MAC protocol. Passive scan may not return all BSS information.

## Slide 11: Beacon/Probe Response Issues (2)
Add current channel information to probe request to overcome the problem of APs on adjacent channels responding leading to excessive probe response retries

## Slide 12: Co-ordination of Field Usage and Numbering
Separate working groups are extending the existing MAC field encoding, therefore some co-ordination is required between the groups to avoid conflicts. How should this be addressed?
Some items that require careful co-ordination are:
  Capability sub-fields
  Element identity numbering
  Status and reason codes