## Slide 1: Proposed Changes for Ad Hoc QBSSs
John M. Kowalski
Sharp Laboratories of America, Inc.
Camas, WA
E-mail: kowalskj@sharplabs.com

## Slide 2: What We Need for Consumer AV
For AV Applications QoS needs:
  Low Cost
  Tight Control of TXOP Allocations
  Ability to interoperate with either infrastructure LANS or in a QoS enabled ad hoc mode.
  Ability to connect with AV/1394 .
We DON’T need
  TCP/IP Integration in every STA.

## Slide 3: The Answer: The Ad Hoc QBSS
NO AP that supports Power Save, Integration services
But there is an HC that supports Association/Reassociation/Disassociation.
Intra-Ad Hoc QBSS functionality is supported.

## Slide 4: Summary of Ad Hoc QBSS Features (1)
Straightforward changes to functionality from QBSS- only integration functions disappear.
Beacons are as in QBSSs
Capability Information changes: ESS=0, IBSS=0 for HC.
“Election” mechanism can be simply, “whoever comes up first within range gets to be HC.”

## Slide 5: Summary of Ad Hoc QBSS Features (2)
This allows manufacturers to develop an ESTA that:
  Functions as a STA in an IBSS
  Functions as a ESTA in a QBSS
  Can become (or not become) the hybrid coordinator in an ad hoc QBSS.
That’s what consumer AV manufacturers need.

## Slide 6: Summary
Proposed changes solve the quandary: “Can an infrastructureless network provide hybrid-coordinated QoS???”
Simple extension to what we’ve already discussed.
Normative text changes in
“11-01-474r1-E-Proposed Changes to Normative Text for Ad Hoc QBSSs”

## Slide 8: Acknowledgement Services for Multicast Frames (1 of 2)
Multicasting in IEEE 802.11:
Multicasting is an unacknowledged service.
If acknowledgement is desired, it needs to be done through a higher layer.
Why is Multicast acknowledging not supported in 802.11?
Only one station can get access to the channel at a given time.
No mechanism to allow access of the channel by all the stations.
The data rates were considerably low in the earlier PHYs and the relatively high packet error rate made it highly inefficient channel utilization even for a medium number of multicast receivers.

## Slide 9: Acknowledgement Services for Multicast Frames (2 of 2)
In 802.11e,
There is a centralized point coordinator (or the hybrid coordinator).
The coordinator can control access to all the stations.
ESTAs would register (during the admission of a stream) through the TSPEC expressing their desire to send an Ack.
The coordinator can poll each of the stations, one at a time, to allow each of the receiving STAs to send an Ack.
Provide the ability to Ack multicast frames when there are small number of receivers thus increasing the reliability.
Even though the above concept can be used for all acknowledgements, we limit it only to delayed Acks.

## Slide 10: Concept of Acknowledgement for Multicast Frames
The delayed acknowledgement frames from a receiver to the sender will themselves form a stream.
ESTA 0
ESTA 1
ESTA 2
ESTA 3
Sender
Receivers
Multicast Stream
Delayed Ack Stream
1 Multicast and 3 D-Ack Streams
Every Multicast stream implicitly defines a number of delayed Ack streams.
The number of delayed Ack streams is same as the number of recipients.

## Slide 11: Operation of ack to Multicast Frames
Operation
  AP grants a TXOP to the ESTA that has the multicast MPDUs by polling.
  ESTA transmits multicast MPDUs.
  After the TXOP, HC polls a ESTA on the multicast DA for acknowledgement.
  The ESTA responds with the delayed Ack.
  Repeat the above two steps for the remaining ESTA on the multicast DA.
  Delayed Ack may be sent in the EDCF as well.
QoS
Data
Poll
QoS Data
from
ESTA #0
DAck
CF-
Poll
DAck
from
ESTA
#1
Ack
from
ESTA
#-0
AP/HC
STA
DAck
CF-
Poll
DAck
from
ESTA
#2
Ack
from
ESTA
#-0
DAck
CF-
Poll
DAck
from
ESTA
#3
Ack
from
ESTA
#-0
Sender : #0
Receivers : #1, #2 & #3

## Slide 12: Polling for acknowledgement
The polling is done by using the DlyAck CF-Poll (a new frame) by the HC.
Frame Format:
Set the type value (b3b2) to 01 (control frame) and subtype value (b7b6b5b4) to 0111.
The receivers are given a TXOP to send their acknowledgement. They may choose to acknowledge multiple streams in the provided TXOP. However, the total duration of all the acknowledgements may not be greater than the duration it takes to transmit 2304 bytes at the highest rate.

## Slide 13: TSPEC for the Delayed Ack streams
Delayed Ack CF-poll is sent at the end of the TXOP to the source.
If there is not enough time for the transmission of the sequence of a DlyAck CF-Poll before the next DTIM, the polling frame may be sent subsequently.
  The DlyAck poll should be sent within the retry period specified in the TSPEC.
It is the responsibility of the HC to provide the delayed Ack transmission opportunity.
It is also the responsibility of the HC to keep the TXOP small enough. If a longer TXOP is desired, split it into two, poll for delayed ACK and then re-assign the rest of the TXOP.

## Slide 14: Set up for Multicast Ack ( 1 of 2)
The acknowledgement policy will be signaled by the receiver during the setup of the stream through the TSPEC.
HC can determine if the stream is multicast based on the destination address.
Bits 2 and 3 of TS Info field will be used for encoding the policy. Ack policy should be set to 2.

## Slide 15: Set up for Multicast Ack (2 of 2)
Thus,
If the destination address is of multicast and the Ack Policy is set to 2, then HC shall schedule polls to each of the receiving STAs after the end of the TXOP.
Only a subset of ESTAs may wish to Ack while the others may set the Ack Policy to 3 in TS Info field. Conversely, based on the admission policy, bandwidth availability and the link characteristics, the HC may allow acknowledgement of a frame by only a subset of the receiving ESTAs in the multicast group.

## Slide 16: Conclusions
Presented a mechanism to allow acknowledgement of multicast frames.
The mechanism is highly efficient if there are small number of multicast stream recipients.
The presented mechanism may also be used for unicast frames, if delayed Ack is desired (unicast is a special case of multicast).
  Expecting the receiver to generate the delayed Ack using DCF rules may increase the latency and may be unacceptable.
  Autonomous burst may be used, but does not scale well if more stations decide to receive the stream.
A variation of CF-Multi-poll may also be used. But, for small number of recipients, the channel efficiency gained may not be substantial.