## Slide 1
Burst Transmission and Acknowledgment
Jin-Meng Ho, Jie Liang, Sid Schrum
Yasuo Harada, Isaac Lim Wei Lih
Yoshihiro Ohtani, Srinivas Kandala
Maarten Hoeben
Duncan Kitchin

## Slide 2
802.11e/D2.0 Burst Request/Ack Issues
Buffer resource issue:
  How large should a burst be before the transmitting station requests a burst ack from the receiving station?
    A large burst may exceed the buffer capacity at the receiving station, resulting in the loss of some frames that were received correctly.
Re-ordering and delay issue:
  How long should the receiving station hold correctly received higher sequence number frames to wait for missing lower sequence number frames?
    Some missing frames may have been discarded by the transmitting station and unnecessarily delay the delivery of frames correctly received by the receiving station to the upper layer.

## Slide 3
Burst Ack Request Frame (1)
Burst Ack Starting Sequence Control:
  Indicating the sequence number for the starting MPDU from which the transmitter is requesting ACK status. This number can not be decreasing (sequence number may wrap around 4096) for the subsequent Burst Ack Request frame for the same TID. This number shall not be offset by more than 128 from the latest sequence number for the same traffic stream, and shall also be limited by the receiver buffer size. MSDUs of sequence number smaller than this number have been discarded by the transmitting MAC entity and are not to be awaited by the receiving MAC entity.

## Slide 4
Burst Ack Request Frame (2)
TID (4 bits):
TID of the traffic stream for which the burst Ack request is intended.
Burst Ack Stop (1 bit):
  When set to 1, indicates that the transmitter is terminating burst ack for this TID and the receiver can release relevant resources.
  When set to 0, indicates that the transmitter will continue burst ack for this TID

## Slide 5
Burst Ack Request/Response Sequence
A QSTA must respond to a Burst Ack Request frame addressed to itself after SIFS. It can respond either with a BurstAck response frame or with a regular Ack frame. If the QSTA has the capability of responding with a BurstAck frame after SIFS, it is recommended to do so.
When a QSTA responds to a BurstAck Request frame with an Ack frame, it means the BurstAck Response frame will be delivered in subsequent available TXOP. The receiver shall set the delivery priority of the pending BurstAck frame to the highest, and put it to the head of the current delivery queue as soon as the BurstAck frame is available.
When the QSTA responds with a Burst Ack Response frame and the Wait subfield is 1, the BurstAck bitmap in the BurstAck Response frame is reserved and set to 0, however the Re-ordering buffer size is valid.
When the transmitter is to initiate a Burst transmission for a TS, it shall first use Burst Ack Request to get the resource constraint from the receiver.

## Slide 6
Burst Acknowledgment (BurstAck) Frame (1)
The Duration field is set to the value obtained from the duration field of the immediately previous frame, subtracted by a SIFS period and the time required to transmit a BurstAck frame.
  If the calculated duration includes a fractional microsecond, that value is rounded up to the next higher integer.
The RA field is copied from the TA field of the immediately previous Burst Ack Request frame:
  This frame acknowledges the frames belonging to the same TID as contained in this frame.

## Slide 7
Burst Acknowledgment (BurstAck) Frame (2)
The Burst Control field is 2-octet field that contains a Buffer subfield in bits 0-7 , a Wait subfield in bit 8, a Fragmentation subfield in Bit 9, and TID in bit 12-15.
  The Buffer indicates the buffer space, in units of MSDUs, that the acknowledging station has, at the time of transmitting this BurstAck frame, for receiving MPDUs belonging to the same TID as contained in this frame.
  The Wait subfield, if set to 0, indicates that this frame contains a valid Burst Ack Bitmap, and if set to 1, indicates that a valid Burst Ack Bitmap cannot be sent with this Burst Ack frame. The value of the Wait subfield does not affect the meaning of the Buffer subfield.
  The maximum number of MSDUs that are acknowledged by the frame are given by Bitmap Size/2.
  Each bit in the Burst Ack Bitmap indicates the status for each fragmentation of a MSDU.
  TID: TID of the traffic stream for which the burst Ack request is intended.

## Slide 8
Burst Acknowledgment (BurstAck) Frame (3)
The Burst Ack Bitmap is a variable field that indicates sequentially the reception status of MSDUs with consecutive sequence numbers and with the TID as contained in this frame.
  A bit in this bitmap is set to 1 if the corresponding fragment of MSDU is received correctly (after FEC decoding if appropriate), or otherwise the bit is set to 0. Some bits in the bitmap may correspond to fragments that did not exist or have not been transmitted; these bits are set to 0.
Starting Sequence Control corresponds to the first MPDU/MSDU that is Acked in the Burst Ack Bitmap.

## Slide 9
Normative Text
Contained in 02/004r4a.doc

## Slide 10
Motion
To replace the frame formats, figures, and text pertaining to the Burst Acknowledgment mechanism in Draft 2.0 with those provided in this document.