## Slide 1: Enabling direct WSTA-WSTA transmissions in a QBSS
Srinivas Kandala
Sharp Laboratories of America, Inc.
E-Mail: srini@sharplabs.com

## Slide 2: Introduction
Direct WSTA-WSTA transmission is allowed in IEEE 802.11e
What is not yet specified is how it will be initiated/used.
We propose two tools:
  The first based on the pending traffic queued.
  The other based on management primitives received.

## Slide 3: Tool 1
The WSTA maintains a Connectivity table containing the MAC address and if the traffic is to be sent directly or through the AP.
Typical Connectivity table as shown below:
When a packet arrives to the head of the queue, it determines if the destination address (DA) has an entry in the table.
If there is an entry, it transmits the packet based on that entry.

## Slide 4: Tool 1
If there is no such entry, then it transmits a directed probe request at the highest rate to the DA.
  If the DA is in the range, the DA shall send a directed probe response. The WSTA will make an entry “direct” into the table and send the packet to the DA. The WSTA whose MAC address shall also make an entry “direct” for the sending WSTA MAC into its own table.
  If there is no response, the DA shall retransmit the probe request at the next highest rate and will repeat the process until it gets a response or the rate that it has to send falls below half the highest rate in the BSSBasicRateSet.
  If the WSTA does not receive the probe response for any rate, it will make an entry of “distribution” into the table and will transmit the packet to the AP for forwarding.

## Slide 5: Tool 2
Sometimes a higher layer protocol (or application) might want to determine if direct transmission is possible:
  To formulate an appropriate bandwidth request.
It causes the SME to generate a MLME-CONNECTIVITY. request with the destination address as the parameter.
The MAC will first check its Connectivity table. If there is an entry for the MAC address it will generate a MLME-CONNECTIVITY.response with the MAC address, Connection Type and PHY rate as the arguments. The Connection Type will be either “direct” or “distributed”.
If there is no entry, the MAC will initiate a probe request /response exchange as described in mechanism 1. After completing the exchange it will update its Connectivity table and generate the MLME-CONNECTIVITY.response

## Slide 6: Motion
Move to incorporate the text in 02/018r0