## Slide 1
Fixing Some EDCF Problems
Sunghyun Choi, Javier del Prado, and Sai Shankar
Philips Research USA
Briarcliff Manor, New York
sunghyun.choi@philips.com

## Slide 2: AIFS[TC] or AIFS[UP]
D2.0 defines user priority (UP), and its mapping from TID.
TS is mapped into a UP.
Accordingly, all the instances of xxx[TC] should be replaced by xxx[UP].

## Slide 3: Mapping per D2.0a

## Slide 4: Motion I
Motion: empower the editor to change all xxx[TC], including AIFS[TC], CWmin[TC], and Cwmax[TC], to xxx[UP] after defining the acronym UP, and to change wording to make the revised draft to be consistent with the above changes.

## Slide 5: Which EDCF Parameters to Use?
Problem with QSTA with less than 8 output queues.
Per D2.0, AIFS[TC], where TC is the traffic category of the highest priority mapped to the queue, is used.
This concerns many voters as it will make implementing fewer queues better, and essentially EDCF useless.

## Slide 6: Frame at the Head of Queue
Let’s use the EDCF parameters corresponding to the frame at the head of the queue.
If the queue is empty (i.e., in case of post-backoff), the EDCF parameters corresponding to the latest frame which was in the queue.
“When multiple user priorities are mapped into a output queue, the dot11AIFS[UP], aCWmin[UP], and aCWmax[UP] are used for the contention of the queue, where UP is the user priority of the frame at the head of the queue[i] or the latest frame which was in queue[i] in the queue is empty.”

## Slide 7: Motion II
Empower the editor to incorporate the normative text changes found in the word document 01/xxxr0, and to change wording to make the revised draft to be consistent with the above changes.

## Slide 8: At Least 4 Queues in QAP?
It seems that QAP will not rely on EDCF as it has highest prioritized channel access.
Not clear why “9.1.3.1 HCF contention-based channel access” states that QAP shall provide at least 4 physical queues.
This requirement should be removed
Or moved to a relevant clause if 4 queue requirement is not for EDCF contention.

## Slide 9: Motion III
Instruct the editor to remove the sentence “A QAP shall provide at least 4 physical queues.” in Clause 9.1.3.1.

## Slide 10: Minimum Value of AIFS?
The note in 9.2.10 states that the default value of AIFS[.] is DIFS.
Seems that the minimum value of AIFS also should be DIFS in order to give the prioritized channel access to HC.

## Slide 11: Motion IV
Instruct the editor to add the following after the last sentence of the note at the end of 9.2.10:
“The minimum value for dot11AIFS[UP] is also 2 for each user priority (UP). The minimum value enables the prioritized channel access by HC.”