## Slide 1
Fixing Some EDCF Problems
Sunghyun Choi, Jin-Meng Ho*, Javier del Prado, and Sai Shankar
Philips Research USA
Briarcliff Manor, New York
sunghyun.choi@philips.com
*Texas Instruments
Dallas, Texas
Jinmengho@ti.com

## Slide 2: AIFS[TC] or AIFS[UP]
D2.0a defines user priority (UP), and its mapping from TID.
TS is mapped into a UP.
Accordingly, all the instances of xxx[TC] should be replaced by xxx[UP].

## Slide 3: Mapping per D2.0a

## Slide 4: Motion I
Motion: empower the editor to change all xxx[TC], including AIFS[TC], CWmin[TC], and Cwmax[TC], to xxx[UP] after defining the acronym UP, and to change wording to make the revised draft to be consistent with the above changes.

## Slide 5: Which EDCF Parameters to Use?
Problem with QSTA with less than 8 output queues.
Per D2.0, AIFS[TC], where TC is the traffic category of the highest priority mapped to the queue, is used.
This concerns many voters as it will make implementing fewer queues better, and essentially EDCF useless.

## Slide 6: Frame at the Head of Queue
Let’s use the EDCF parameters corresponding to the frame at the head of the queue.
If the queue is empty (i.e., in case of post-backoff), the EDCF parameters corresponding to the latest frame that was in the queue.
“When multiple user priorities are placed into queue[i], the dot11AIFS[UP], aCWmin[UP], and aCWmax[UP] are used for the contention of the queue, where UP is the user priority of the frame at the head of the queue[i] or the latest frame that was in queue[i] if the queue is empty.”

## Slide 7: Motion II
Empower the editor to incorporate the normative text changes found in the word document 01/112r2, and to change wording to make the revised draft to be consistent with the above changes.

## Slide 8: dot11PriorityMapping MIB?
dot11PriorityMapping MIB ties the backoff procedure to the queue, rather than to each frame.
  The EDCF behavior is sensitive to the number of queues implemented.
Our proposed remedy ties the backoff procedure directly to the frame to be transmitted (at head of the queue).
  This makes the EDCF behavior normative (no longer dependent on the number of physical queues).
  This also removes the need for defining and implementing the dot11PriorityMapping.

## Slide 9: Motion III
Instruct the editor the replace
“The EDCF provides differentiated, distributed access to the WM for 8 user priorities. EDCF channel access will use at most 8 prioritized output queues, one for each delivery priority. A QSTA or QAP may implement fewer than 8 physical queues and shall provide a mapping from user priorities to the available queues by means of the dot11PriorityMapping table in the MAC MIB.”

## Slide 10
With
“The EDCF provides differentiated, distributed access to the WM for eight user priorities. EDCF channel access shall use at most eight prioritized output queues for up to eight user priorities.”
In Clause 9.1.3.1.

## Slide 11: At Least 4 Queues in QAP?
It seems that QAP will not rely on EDCF as it has highest prioritized channel access.
Not clear why “9.1.3.1 HCF contention-based channel access” states that QAP shall provide at least 4 physical queues.
This requirement should be removed
Or moved to a relevant clause if 4 queue requirement is not for EDCF contention.

## Slide 12: Motion IV
Instruct the editor to remove the sentence “A QAP shall provide at least 4 physical queues.” in Clause 9.1.3.1.

## Slide 13: Minimum Value of AIFS?
The note in 9.2.10 states that the default value of AIFS[.] is DIFS.
Seems that the minimum value of AIFS also should be DIFS in order to give the prioritized channel access to HC.

## Slide 14: Motion V
Instruct the editor to add the following after the last sentence of the note at the end of 9.2.10:
“The minimum value for dot11AIFS[UP] shall be 2 for each user priority (UP). This restriction enables prioritized channel access by the HC.”