## Slide 1: Burst Ack Recommendations
Srinivas Kandala,
Sharp Laboratories
TGe Burst Ack ad hoc group

## Slide 2: Changes from Dallas Meeting
Introduce a capability bit element.
Establish the handshaking through management frames.
Replace a Burst Ack Request frame with a QoS Data frame.
Introduce two bits, No Ack and Burst Ack in frame control.
  Removed No Ack bit from QoS control
Get the Wait functionality by reinterpreting one of the unused bits of the ACK frame.
Clarify the Buffer size statement.
Issues to be resolved

## Slide 3: Two types of Burst Ack
Immediate
  The Burst Ack shall be sent immediately after being solicited.
  If not ready, the receiver shall send an ACK (to be expanded later) seeking further action from the transmitter.
Delayed
  The Burst Ack shall be sent when the receiver has finished processing all the frames.

## Slide 4: Handshaking
Designate QoS Action codes and use QoS Action management frames:
Newly
introduced

## Slide 5: Define Burst Ack Request
Frame body format:
Dialog token can be of any value but the same value should be used in all future exchanges.
ACK policy = 1 means immediate, 0 means delayed.
TID is the value of the TC or TS of the traffic.
Starting Sequence Control has the sequence number and the fragment number of the first frame.
  How does the transmitter predict its value? Jump to a particular number?

## Slide 6: Define Burst Ack Response
Frame Format:
Dialog Token & TID shall be same as the request frame.
When Reject bit is set to 1, the burst Ack is not allowed.
ACK policy may be same as the request frame or may be changed depending on the capabilities of the receiver.
Re-ordering buffer size is the number of 2312 buffers that are available.
  Each MPDU (or MSDU) uses one buffer irrespective of the size of the MPDU.
A receiver may send the frame unsolicited if it desires to change parameters

## Slide 7: Delete Burst Ack request
Frame Format:
Dialog token same as in the Define Burst Ack request.
This frame could be sent by the originator of the burst or the recipient.
TAID is used to identify the traffic to indicate the source.
  We can also use a bit to indicate the same information. Don’t feel very strongly about either.

## Slide 8: No Ack and Burst Ack bits in Frame Control
Editor has indicated that two bits - retry and More Data will not be used in IEEE 802.11e and suggested using them.
Frame Control Format:
Retry bit and More Data will have meaning only for legacy.
For QoS Data type frames, when No Ack = 1, then there will not be an ACK or QoS (+)CF-Ack after SIFS duration. However, there could be some other frame as explained in the next slide. When No Ack = 0, the recipient shall respond with either ACK or QoS (+)CF-Ack.
No Ack is reserved for all other frames and set to 0.

## Slide 9: Burst Ack bit in Frame Control
For QoS Data frames, the interpretation depends on No Ack bit as shown in the following table:

## Slide 10: Burst Ack bit in Frame Control
Continued from the previous slide:

## Slide 11: Burst Ack bit for ACK frames
In ACK frames, the Burst Ack bit can be set to 1 to indicate to the recipient to re-send the immediate burst ack frame (usually in the form of a QoS Null with No Ack bit and Burst Ack bit both set to 1).

## Slide 12: Burst Ack frame
The frame which actually sends the acknowledgements.
Frame Format:
Bitmap size works as before.

## Slide 13: Data transfer and acknowledgements
All QoS Data frames in the burst except for the last one are sent with No Ack bit set to 1 and Burst Ack bit set to 0.
Immediate Burst ACK:
  The final frame shall be sent with No Ack bit set to 1 and Burst Ack bit set to 1.
  The receiver shall respond with a Burst Ack or with an ACK frame with Burst Ack bit set to 1.
  If the receiver responds with ACK frame with Burst Ack bit set to 1, then the transmitter will transmit a QoS Null frame with same TID, and No Ack bit set to 1 and Burst Ack bit set to 1.
  If there is no response from the receiver, the transmitter may retry later.

## Slide 14: Data transfer and acknowledgements
Delayed Burst ACK:
  The final frame shall be sent with No Ack bit set to 0 and Burst Ack bit set to 1.
  The receiver shall respond with a ACK or a QoS(+) CF-Ack frame.
  The receiver shall send the Burst Ack subsequently to which the transmitter shall acknowledge with a ACK or a QoS(+)CF-Ack.
Unsolicited Burst Ack:
  Due to transmission failures or lack of TXOPs, it is possible that the final frame never gets received at the receiver.
  Then the receiver may send the Burst Ack frame unsolicited.

## Slide 15
QoS
CF-Poll
QoS
Data
QoS
Data
QoS
Data
QoS
Data
ACK
QoS
Null
Burst
Ack
HC
Originator
Recipient
No Ack =1
Burst Ack = 1
No Ack =1
Burst Ack = 0
Burst Ack = 1
Data Burst
Burst Ack
Exchange
TXOP Limit
NAV Reservations
Typical Burst Sequence with Immediate Burst Ack Policy

## Slide 16
QoS
CF-Poll
QoS
Data
QoS
Data
QoS
Data
QoS
Data
ACK
QoS
Null
Burst
Ack
HC
Originator
Recipient
No Ack =1
Burst Ack = 1
No Ack =1
Burst Ack = 0
Burst Ack = 1
Data Burst
Burst Ack
Exchange
TXOP Limit
NAV Reservations
Typical Burst Sequence with Delayed Burst Ack Policy

## Slide 17: Issues
Re-ordering Buffer Size in Burst Ack
Clarification on Capability Information
Need for a quicker update of Starting Sequence Control in request?
  Perhaps re-use bits in QoS Control ?
Timeouts?
Others?