## Slide 1: Burst Ack Recommendations
Srinivas Kandala,
Sharp Laboratories
E-Mail: srini@sharplabs.com
TGe Burst Ack ad hoc group

## Slide 2: Changes from Dallas Meeting
Introduce a capability bit element.
Establish the handshaking through management frames.
Replace the No Ack bit in QoS Control with a 2-bit Ack Policy.
Get the Wait functionality by reinterpreting one of the unused bits of the ACK frame.
Clarify the Buffer size statement.
Allow BurstAckReq and BurstAck control frames be sent at the same rates as Data MPDUs.
Remove the restriction of “Retransmitted burst data MPDUs shall preserve their original relative order”
  Removed because some non-hardware implementations may need time to search for the earliest frame that needs to be sent.

## Slide 3: Two types of Burst Ack
Immediate
  The Burst Ack shall be sent immediately after being solicited.
  If not ready, the receiver shall send an ACK (to be expanded later) seeking further action from the transmitter.
Delayed
  The Burst Ack shall be sent when the receiver has finished processing all the frames.

## Slide 4: Handshaking
Set up and tear down of Burst Ack is through QoS Action management frames.
Designate QoS Action codes and use QoS Action management frames:
Newly
introduced

## Slide 5: Define Burst Ack Request
Frame body format:
Dialog token can be of any value but the same value should be used in all future exchanges.
Burst Ack policy = 1 means immediate, 0 means delayed.
TID is the value of the TC or TS of the traffic.

## Slide 6: Define Burst Ack Response
Frame body Format:
Dialog Token & TID shall be same as the request frame.
When Reject bit is set to 1, the burst Ack is not allowed.
Burst Ack policy may be same as the request frame or may be changed depending on the capabilities of the receiver.
Re-ordering buffer size is the number of 2304 octet buffers that are available.
  Each MPDU (or MSDU) uses one buffer irrespective of the size of the MPDU.
A receiver may send the frame unsolicited if it desires to change parameters or to terminate its participation in Burst Ack.

## Slide 7: Delete Burst Ack request
Frame Body Format:
Dialog token and TID shall be same as in the associated Define Burst Ack request.
This frame is sent only by the originator.
If the recipient desires to end the participation in the burst, it sends a Define Burst Ack response QoS Action frame with Reject field set to 1.

## Slide 8: Ack Policy in QoS Control
Replace a single-bit No Ack bit with the two-bit Ack Policy in QoS Control in QoS data frame.
  Non-Final bit has no normative behavior and is being recommended to be removed by other ad hoc groups.
Field format of QoS Control
Ack policy subfield interpretations are given in next slide.

## Slide 9: Ack Policy in QoS Control

## Slide 10: Wait bit in Frame Control for ACK frames
The retry bit will never be used in ACK frames.
  We propose to use this for indicating Wait functionality.
Frame Control Format:
In ACK frames, the Wait bit is set to 1 to indicate to the recipient to re-send the immediate burst Ack frame (in the form of a QoS Null with Ack Policy in QoS Control set to 10).

## Slide 11: BurstAckReq frame
The frame used for requesting Burst Ack.
Frame Format:
Burst Ack Policy is set to 1 for immediate and 0 for delayed.

## Slide 12: BurstAck frame
The frame which actually sends the acknowledgements.
Frame Format:
Decided to use a constant bitmap size as a variable bitmap size will raise questions on how to set the duration.
Bitmap works as before.

## Slide 13: Multirate support for BurstAckReq and BurstAck
Control frames are restricted to the use of the rates in BSSBasicRateSet.
  No reason to have the same restriction on BurstAckReq and BurstAck frames as they are more like the Data frames in nature.
Allow transmitting BurstAckReq and BurstAck frames at the same rate as Data MPDUs.

## Slide 14: Data transfer and acknowledgements
Immediate Burst ACK:
  All QoS Data frames shall be sent with the Ack Policy of 10.
  After transmitting the burst, the transmitter shall send a Burst Ack Request frame.
  The receiver shall respond with a Burst Ack or with an ACK frame with Wait bit set to 1.
  If the receiver responds with ACK frame with Wait bit set to 1, then the transmitter will retransmit the Burst Ack Request frame.
  If there is no response from the receiver, the transmitter may retry later.

## Slide 15: Data transfer and acknowledgements
Delayed Burst ACK:
  All Data frames shall be sent with Ack Policy set to 01.
  The transmitter seeks the Burst Ack through a Burst Ack Request frame.
  The receiver shall respond with a ACK or a QoS(+) CF-Ack frame.
  The receiver shall send the Burst Ack subsequently to which the transmitter shall acknowledge with a ACK or a QoS(+)CF-Ack.
  Upon reception of a request, the receiver shall endeavor to expedite the delivery of the burst Ack by placing it at the head of the queue of the highest priority.

## Slide 16: Data transfer and acknowledgements
Unsolicited Burst Ack:
  Due to transmission failures or lack of TXOPs, it is possible that the final frame never gets received at the receiver.
  Then the receiver may send the Burst Ack frame unsolicited.

## Slide 17
QoS
CF-Poll
QoS
Data
QoS
Data
QoS
Data
BurstAck
Req
ACK
BurstAck
Req
BurstAck
HC
Originator
Recipient
Ack Policy = 10
Wait = 1
Data Burst
Burst Ack
Exchange
TXOP Limit
NAV Reservations
Typical Burst Sequence with Immediate Burst Ack Policy

## Slide 18
QoS
CF-Poll
QoS
Data
QoS
Data
QoS
Data
BurstAck
Req
ACK
BurstAck
HC
Originator
Recipient
Ack Policy = 01
Wait = 0
Data Burst
Burst Ack
Exchange
TXOP Limit
NAV Reservations
ACK
Typical Burst Sequence with Delayed Burst Ack Policy
Wait = 0

## Slide 19: Issues
Bitmap Size
Retry Limit for BurstAckReq
Wait functionality in ACK
Allowing Unsolicited Burst Ack with Immediate Burst Ack policy
Timeouts?
Others?