## Slide 1: 1394 Clock Synchronization over 802.11
Javier del Prado, Sunghyun Choi, Sai Shankar, Takashi Sato, and Jeff Bennett
Philips Research-USA
Briarcliff Manor, New York
sunghyun.choi@philips.com

## Slide 2: Introduction
1394 Clock Synchronization is critical for Wireless 1394 and required for the virtual 1394 bus
No mechanism has been yet defined for the 1394 clock synchronization over 802.11 WLAN
In this submission we present a mechanism for stringent clock synchronization, and define a set of new 802.11 primitives needed to support it

## Slide 3: Scenario
(Virtual 1394 Bus)
CM

## Slide 4: Our Solution
<= 10 ms
a(n)
n
n'
802.11 synchronization frame from CM
Cycle Master
CTR
a(n)
Cycle Slave
CTR
b(n)
a(n)

adjust
Last_Symbol_on_Air
Last_Symbol_on_Air
PHY_TXEND.confirm
PHY_RXEND.indication
802.11 synchronization frame from CM
n
Frame
Sequence
Number

## Slide 5: How It Works
At Cycle Master
  a(n) = CTR_Value (at observed Last_Symbol_On_Air event) – offset
  Multicasts a(n) and n in synchronization frame at a semi-regular interval (e.g. 10 ms)
At Cycle Slave
  b(n) = CTR_Value (at observed Last_Symbol_On_Air event) – offset
  Receive synchronization frames and retrieve a(n) and n
  Compare b(n) and a(n) and use  to adjust CTR appropriately
offset: delay from the end of the last symbol on the air to when capturing of the CTR value takes place

## Slide 6: Changes required in 802.11
No major change required!
Only three new primitives need to be defined to support the synchronization
The primitives will pass the synchronization information from the MAC to the SME
The communication between the SME and the 1394 PAL Layer is out of the scope of this submission

## Slide 7: Synchronization Primitives
MLME-HL-SYNC.request
MLME-HL-SYNC.confirm
MLME-HL-SYNC.indication

## Slide 8: MLME-HL-SYNC.request
This primitive requests activating the synchronization support mechanism
It is generated by the SME when a higher layer protocol, which requires a stringent synchronization, such as the 1394 PAL, is active in the STA
Semantics:
  MLME-HL-SYNC.request (
  RxAddress
  )

## Slide 9: MLME-HL-SYNC.confirm
This primitive confirms the activation of the higher layer synchronization support mechanism
It is generated by the MLME as a result of an MLME-HL-SYNC.request to activate the mechanism for the higher layer synchronization support
Semantics:
  MLME-HL-SYNC.confirm (
  ResultCode
  )

## Slide 10: MLME-HL-SYNC.indication
This primitive reports completed transmission or reception of a synchronization frame
This primitive is generated by the MLME when the successful reception/transmission of a synchronization frame is detected. The synchronization frame is identified by the multicast MAC address indicated by the MLME-HL-SYNC.request primitive
Semantics:
  MLME-HL-SYNC.indication (
  TxAddress
  SequenceNumber
  ProcDelay
  )

## Slide 11: MLME-HL-SYNC.indication (II)
Parameters:
Name
Type
Valid Range
Description
TxAddress
MACAddress
Any valid individual MAC address
Specifies the address of the MAC entity that sent the synchronization frame. In the case of the STA sending the frame, it will be its own MAC address.
SequenceNumber
Enumeration
As defined in the frame format
Specifies the sequence number of the synchronization frame received/transmitted.
ProcDelay
Enumeration
[0, 65535]
Specifies the estimated time between the generation of this primitive and the time at which the end of the last symbol of the frame that generated this primitive was detected on the air.
 |  |  0 | 

## Slide 12: Summary (I)
A new clock synchronization mechanism defined for timing critical applications such as Wireless 1394
  Relies on a higher-layer clock in each node and the Last_Symbol_On_Air timing that occurs simultaneously across 802.11 WLAN
  Does not rely on TSF Timer, which may not be accessible, reliable, or accurate enough
Any node can become the Cycle Master!!!
Not require any significant change in 802.11
    PHY_TXEND & PHY_RXEND are readily available
    Only three new primitives need to be defined

## Slide 13: Summary (II)
The MAC change is essentially optional !!!
    Look at MLME-HL-SYNC.confirm (Not Supported)
    E.g., no need to implement it if no plan to support timing-critical applications
Can be used for any higher layer protocol that requires stringent clock synchronization!!!