## Slide 1: Suggested Changes to RSN
Tim Moore

## Slide 2: Some implementation experience
Took TGi draft 2
Added 48bit IV TKIP change
Deleted 1X rekeying for Pairwise key
Attempted to implement
  Editing document as ran into problems

## Slide 3: General comments
Difficult to follow
  Rewrote large pieces of document
  Added clarifications for questions
Legacy support
  Needed to specify what combinations of legacy/RSN support

## Slide 4: Authentication
Went back to 802.11 open authentication
  Reverted 802.11 state machine back
Did 1X as an authenticated key management protocol over a 802.11 data link
  Some issues in 1X state machine
  Some issues in the way eapol-key message was used
  Encrypt 1X with key mapping key only
    Can’t start a 2nd association otherwise

## Slide 5: Information element
Difficult to work out valid combinations
  Add table of combinations and reference code
Found pre-shared key is a special case for users
  Needed to add an auth type to make this easy for users

## Slide 6: PRF
Needed reference code and test vectors

## Slide 7: TKIP
Used 48 bit IV
Used frame format

## Slide 8: Michael
Assumes unicast keys with a different integrity in each direction
Broadcast key
  What integrity key since can’t use different integrity keys for broadcast in IBSS
Counter measures
  Trying to stop handling out new keys for the attacker to attack
  Rather than stopping the MAC, stop handing out keys.
    If attacker is attacking one station doesn’t affect others