## Slide 1: Suggested Changes to RSN
Tim Moore

## Slide 2: Some implementation experience
Took TGi draft 2
Added 48bit IV TKIP change
Deleted 1X rekeying for Pairwise key
Attempted to implement
  Editing document as ran into problems

## Slide 3: General comments
Difficult to follow
  Rewrote large pieces of document
  Added clarifications for questions
Legacy support
  Needed to specify what combinations of legacy/RSN support

## Slide 4: Authentication
Went back to 802.11 open authentication
  Reverted 802.11 state machine back
Did 1X as an authenticated key management protocol over a 802.11 data link
  Some issues in 1X state machine
  Some issues in the way eapol-key message was used
  Encrypt 1X with key mapping key only
    Can’t start a 2nd association otherwise

## Slide 5: Information element
Difficult to work out valid combinations
  Add table of combinations and reference code
Found pre-shared key is a special case for users
  Needed to add an auth type to make this easy for users

## Slide 6: PRF
Needed reference code and test vectors

## Slide 7: TKIP
Used 48 bit IV
Used frame format

## Slide 8: Michael
Assumes unicast keys with a different integrity in each direction
Broadcast key
  What integrity key since can’t use different integrity keys for broadcast in IBSS
Counter measures
  Trying to stop handling out new keys for the attacker to attack
  Rather than stopping the MAC, stop handing out keys.
    If attacker is attacking one station doesn’t affect others

## Slide 9: Additional issues
RSN information element
  Clarify which fields are optional
  Clarify that it is also in the re-association request message.
  Clarify the use of WEP for multicast cipher suite is for legacy support
802.1X keying
  Added ReAuthenticationRequest event to Authenticator key state machine to trigger 4-way handshake on 802.1X re-authenticate.
  Added the RSN IE in the 2nd and 3rd EAPOL-Key message of the 4-way handshake to fix a security issue of attacking security by modifying the RSN IE.
    Also required for pre-authentication so new AP knows the cipher to allow it to send the correct keying information
  Added some text about the checks the Supplicant and Authenticator should carry out as part of the keying state machines.
  Updated Authenticator state machine to correct an error in the handling of the EAPOL-Key message with the Request bit set to 1
  Clarify the use of the secure bit in the EAPOL-Key message
TKIP
  Changed the TKIP frame format to send RC4KEY[0-2] in the WEP IV field and the upper 4 octets of the TSC in the EIV
    Document 02/281 was different than suggested in 02/282 (TKIP 48bit IV)(
  Added text noting the increased data payload length due to the MIC and fragmentation may occur because of this.
Added a table of Required, Recommended, Optional functionality
General editorial clarifications