## Slide 1: Suggested Changes to RSN
Tim Moore

## Slide 2: Updates from r3 to r4
Michael integrity reporting clarifications
  Very confusing, rewrote with help from Dorothy
Group key sequence counter security fix
  Doug/Jesse pointed out problem with Group key for stations associating sometime after GTK generated. Fix to pass sequence counter in Group key update
  Added a parameter to the EAPOL-Key message to pass the Sequence counter
  Add a parameter to SetKeys to pass receive sequence counter
Michael Tx/Rx fix
  The Michael key selection logic didn’t work for Group keys
  Now use supplicant/authenticator to select keys
  Add a parameter to SetKeys to pass supplicant/authenticator

## Slide 3: Updates from r3 to r4
Clarify use of multicast cipher in associate request
  Must be the same as from the AP
Some fixes in the Authenticator state machine
  Error on no key in 802.1X authentication case
Bit/Octet convention issue, 298 referred to 802.11 for one field but one others, 802.1X uses a different convention for other fields
  All fields EAPOL-Key use 802.1X convention
Change EAPOL-Key MIC to HMAC-MD5 for AES case
  Jesse pointed out a problem. When added information element to 4-way handshake to fix the negotiation security problem caused a problem with using AES-CBC for EAPOL-Key MIC. Fix change it to use HMAC-MD5 same as TKIP EAPOL-Key

## Slide 4
Motion to incorporate changes in 02-298r4 into TGi draft