## Slide 1: Dual precoding with FEC packets
Texas Instruments
141 Stony Circle, Suite 130
Santa Rosa California 95401
(707) 521-3060, heegard@ti.com
Chris Heegard, Lior Ophir,
Richard Williams & Sid Schrum
Home and Wireless Networking

## Slide 2: March Submission
Chris Heegard and Richard Williams, A Precoder for Limiting Scrambler Error Propagation, IEEE 802.11: 11-02-221r0, March, 2002.
Issue: The “MAC” header was scrambled
  The system described in March is “non-systematic” on the entire packet, meaning that the output of the pre-coder is a scrambled version of input
Suggested solution: Dual Precoding

## Slide 3: Single Precoding System
Recursive filter before transmission
  After FEC encodder
Moving average filter after receiption
  Before FEC decoder
Non-systematic
  Transmitted MAC header is scrambled by the recursive filter

## Slide 4: Sytematic FEC Encoder
IEEE 802.11e uses a Reed-Solomon code
The output packet agrees with the input packet until the first parity checks
  When initial information, such as a MAC header, is produced at the output before the first parity checks are inserted, then the initial information could be extracted from the output without knowledge of how the ECC parity checks are computed and inserted in the output packet
It is desirable to keep this property with the scrambling function

## Slide 5: Dual pre-coding system