## Slide 1: IEEE 802.1X Pre-Authentication
Bernard Aboba
Microsoft

## Slide 2: Outline
Goals
Conclusions
Overview of pre-authentication
State machine
Threat model
EAP requirements
Management frame protection
Control frame protection
Protected negotiations
Key activation
Summary

## Slide 3: Goals
To present a strawman threat model for IEEE 802.11 Tgi
  Tim Moore to present detailed threat analysis on Thursday
To understand the implications of IEEE 802.1X pre-authentication
  Pre-authentication supported in 802.11i Draft 2.2
To analyze solutions to potential threats
  Protected capabilities negotiation
  Key activation
  Management frame authentication
  Control frame authentication

## Slide 4: Conclusions
IEEE 802.11i needs a threat model.
  Without a threat model, you never know when you’re done!
  IEEE 802.1X could use a formal threat model too (to avoid misunderstandings).
IEEE 802.1X pre-authentication with 802.11 introduces some new wrinkles
  Supplicant-only initiation
  Station authenticated to multiple Authenticators simultaneously
  No controlled and uncontrolled ports
  802.11 state machine controls access, not 802.1X state machine
  IEEE 802.1X frames have a unicast DA and may be forwarded
IEEE 802.1X pre-authentication has substantial advantages for 802.11
  Pre-authentication enables a station to authenticate to multiple APs, which is not possible when 802.1X occurs after Association.
    Minimizes connectivity loss during roaming
  IEEE 802.1X pre-auth makes it possible to authenticate and derive keys early on, use keys to protect as many messages as possible
  Most management and control frames can be protected, with the exception of Beacon and Probe Request/Response

## Slide 5: 802.1X Pre-Authentication
Channel 6
Channel 11
AP A
AP B
STA authenticates and associates to AP A on Channel 6
  802.1X data frames with “From DS” and “To DS” set to false (Class 1)
STA does passive or active scan, moves, selects AP B as “potential roam”
STA authenticates to AP B before connectivity is lost to AP A (if T < c/v)
  Can send unicast 802.1X data frames to AP B, forwarded by AP A
    “From DS” or “To DS” set to true (Class 3)
  Can tune radio to Channel 11 (if B > r T)
STA reassociates to AP B
STA
v
c
D

## Slide 6: The Problem Space
Station Velocity
Stationary
Pedestrian
Vehicular
Rate
Scan +
Radio tuning
Scan + Pre-auth via
Old AP

T
c
T
AP authentication & Advertisement over IP
D
RTTassoc
Association not possible
High Speed

## Slide 7: State Machine
Original 802.11 state machine can be used
IEEE 802.1X data frames can be sent in State 1,2
  To DS, From DS =0
  “Unassociated pre-auth”
IEEE 802.1X data frames can be sent in State 3
  To DS or From DS = 1
  “Associated Pre-auth”
Unauthenticated Deauth can be silently discarded by STA

## Slide 8: Pre-Authentication State Machine
No “controlled” and “uncontrolled” ports
  In fact, no “ports” at all!
  Port doesn’t exist until Association/Reassociation exchange
  RADIUS Access-Request contains no NAS-Port attribute
  Accounting START sent after successful Association/Reassociation Response w/NAS-Port
Supplicant initiation only
  Supplicant authenticates to APs that it is likely to roam to
  Since roaming decision made by STA, it also handle auth initiation
  Unsolicited EAP-Request/Identity frames are silently discarded
802.11 state machine governs frame treatment
  802.11-1999 state machine already supports pre-authentication, no changes required
  802.1X “auth complete” an input to 802.11 state machine
  Reverse of 802.1X after Association, where 802.11 events are inputs to 802.1X state machine

## Slide 9: Strawman Threat Model for 802.11
Snooping, modification or injection of data packets
Impersonation of legitimate 802.11 STA or AP
Modification of authentication or control/management messages
Injection of forged authentication or control/management messages
Denial of service, including resource starvation
Disruption of security negotiations
  Capabilities advertisement
  Ciphersuite or authentication negotiation

## Slide 10: 802.11 EAP Method Requirements
Question: “What role does EAP have in 802.11 security?”
Wireless method requirements (from RFC 2284bis):
  Mutual authentication
  Key derivation
  Dictionary attack resistance
  Support for fast reconnect
    Question: is 2.5 round trips “fast”?
  Protected EAP conversation
To be discussed
  Ciphersuite negotiation?
  Key activation?

## Slide 11: Threats Addressed by EAP Reqmts.
Snooping, modification or injection of data packets (802.11 ciphers)
Impersonation of legitimate 802.11 STA or AP (802.11 ciphers)
Modification of authentication or control/management messages
Injection of forged authentication or control/management messages
Denial of service, including resource starvation
Disruption of security negotiations
  Capabilities advertisement
  Ciphersuite or authentication negotiation

## Slide 12: No Mandatory Auth Method: Implications
Interoperability
  No guarantee that STA and AP can successfully authenticate
Configurations without a backend server
  Authenticator can’t just implement the mandatory method; needs to support commonly deployed methods
  Result: AP may need constant code changes to support new auth methods – what EAP was designed to prevent!
  “Pass through” configuration is easier to implement
IBSS authentication
  No guarantee that two STAs can authenticate each other
Effects on 802.1X architecture
  Backend authentication server originally an optional component
  Not really possible to “Colocate AS and AP”
    In EAP, AS and client are assumed to be extensible but AP is not
  Normative discussion of AAA attributes and protocols
    Belongs in a non-normative Appendix, not within the main specification.

## Slide 13: Protection of Management Frames
Protectable
  Association/Reassociation Request/Response, Deauthenticate, Disassociate
Unprotectable
  Beacon, Probe Request/Response
  Would need to protect Beacon with multicast key; would not prevent forgery
  Can protect contents of Beacon, Probe Response later on in order to detect forgery
Handling of unauthenticated management frames
  STA can discard unauthenticated Deauthenticate message
Alternatives
  Custom MIC
    Requires change to key hierarchy
    Low performance
  TKIP/WRAP applied to MPDU
    No change required to key hierarchy
    High performance
    Requires changes to ciphers

## Slide 14: Protection of Control Frames
Similar issues to management frame protection but fewer options
  Control frames are higher bandwidth
  Performance penalty of not reusing TKIP and WRAP ciphersuites is prohibitive
  Custom MIC not a viable option
Conclusion
  For control frame protection, need ciphersuites operating on MPDU

## Slide 15: Threats Addressed by Mgmt/Cntrl Protection
Snooping, modification or injection of data packets
Impersonation of legitimate 802.11 STA or AP
Modification of authentication or control/management messages
Injection of forged authentication or control/management messages
Denial of service, including resource starvation
Disruption of security negotiations
  Capabilities advertisement
  Ciphersuite or authentication negotiation

## Slide 16: Protected Negotiations
Ciphersuite negotiation
  Ciphersuite negotiation needs to occur before ciphersuites are used
  If ciphersuite used to protect management messages, then negotiation needs to occur prior to Association/Reassociation Request/Response
  Alternatives
    Authenticated Association/Reassociation Request/Response
      Too late if Assoc/Reassoc protected by TKIP or WRAP ciphersuite
    4-way handshake
      Early in conversation
      Specific to 802.11
    EAP
      Need to create new EAP method to handle thise
      Requires support for multiple media (PPP, 802.11, etc.)
Authentication negotiation
  Handled by EAP protection method

## Slide 17: Threats Addressed by Protected Negotiation
Snooping, modification or injection of data packets
Impersonation of legitimate 802.11 STA or AP
Modification of authentication or control/management messages
Injection of forged authentication or control/management messages
Denial of service, including resource starvation
Disruption of security negotiations
  Capabilities advertisement
  Ciphersuite or authentication negotiation

## Slide 18: Key Activation
Determines when “FC” WEP bit can be set to true
Alternatives
  4-way handshake
    Enables “FC” WEP bit to be turned on prior to completion of EAP exchange (e.g. to cover Success/Failure frames
  Authenticated Association/Reassociation exchange
    “FC” WEP bit only turned on in “associated” pre-auth
    EAP protection required
    Used to activate keys in 802.11-1999

## Slide 19: Summary
Threat | Mitigation alternatives
Authentication | 802.1X pre-authentication 802.1X post-authentication
Protected capabilities negotiation | 4-way handshake EAP Authenticated Association/Reassociation
Key activation | 4-way handshake Authenticated Association/Reassociation
Management frame authentication | Ciphers operating over MPDU Authenticator Information Element
Control frame authentication | Ciphers operating over MPDU

## Slide 20
Feedback?