## Slide 1: Avoiding scrambler seed transmission errors
Ericsson Microelectronics AB
Isafjordsgatan 16
SE-164 81 Kista, Sweden
+46 8 7575018, mike.lewis@mic.ericsson.se
Mike Lewis
Wireless System Design

## Slide 2: Scrambler seed requirements
Scrambler seed for 802.11a shall “be set to a pseudo random non-zero state”.
  Transmission errors of the seed information cause well-known problems combined with MAC-level FEC.
Solution: provide the receiver with a way to deduce the initial state other than the transmitted information!

## Slide 3: Preconditions for use
At sender: possibility to set OFDM PHY scrambler initial state prior to Tx.
At receiver: possibility to determine initial state used by Rx descrambler in OFDM PHY.
Entirely optional at receiver, maintains current (draft 3.0) MAC FEC frame structure.

## Slide 4: Proposed method: transmit side
Maintain a list of <Address1, seed> pairs for each recipient Address1 (DA / RA / BSSID) to which FEC traffic has been sent.
  Can be a unicast, broadcast or multicast address
When sending FEC traffic, for each MPDU sent, check for a list entry corresponding to Address1.
  If list entry does not exist, initialise it with Address1 and set seed to a pseudo-random non-zero value.
Use value of seed corresponding to Address1 to initialise the OFDM PHY layer scrambler for sending the MPDU.
Update the value of seed, to be the state of the OFDM PHY scrambler after one iteration with initial state set to seed.
  Seed is, as required, a pseudo-random non-zero value.

## Slide 5: Proposed method: receive side
Maintain a list of <Address1, Address2, seed> triplets for each recipient Address1 (DA/RA/BSSID) and sender Address2 (SA/BSSID/TA) for which FEC traffic has been received.
  Address1 can be a unicast, broadcast or multicast address
  Address2 is always an individual address.
If an MPDU is received successfully (after possible error correction)
  Update (or create if it does not exist) an entry in the list corresponding to <Address1, Address2, seed’>. Seed’ is generated by taking the value rx_seed used to initialise the OFDM PHY descrambler and updating it according to the algorithm used to generate seed’ at the transmitter.
This causes seed generation at the receiver to be synchronised with that at the transmitter for all <receiver,transmitter> combinations

## Slide 6: Proposed method: receive side
If an MPDU cannot be received correctly, even after attempted error correction...
  Assume that the cause is scrambler error propagation
  Determine the received scrambler seed value rx_seed used to initialise the 802.11a PHY descrambler.
  Can’t read address fields in corrupted message, so must search...
Perform an intelligent search of the <Address1, Address2, seed> list
  For each entry searched, compensate the received MPDU for the difference in descrambler output when using seed instead of rx_seed in the 802.11a PHY layer.
  See if the compensated MPDU is successfully error-corrected by FEC.
If compensated MPDU is successfully corrected and received
  Update <Address1, Address2, seed’> based on seed value used to successfully decode the message.

## Slide 7: Performance of method
If all <Address1, Address2, seed> values are stored, and a full search is performed, seed errors can always be corrected for if the previous MPDU was successfully received.
Performance can be modelled as a 2-state Markov chain
  Probability of error in current MPDU depends only on whether last MPDU was successfully received or not (seed values synchronised).
Resulting packet error rate is very close to performance of FEC code without scrambler problem.

## Slide 8: Performance of method
PER based on 1000 byte packets, with independent bit errors.
PERFEC : ideal PER with FEC and no scrambler propagation errors
PERMarkov : Steady-state PER with full search method implemented

## Slide 9: Limiting search extent
Only maintain records for FEC frames directed to the receiver
  Only try to correct header part of message while searching: look for matching receive address after compensation / error correction.
  Reduces number of entries for a WSTA to store
    Accept loss of NAV data for a small number of frames
Search through all <Address1,Address2> pairs rarely required
  QSTA will often be receiving data from QAP
  QAP will often be receiving data after granting a TXOP
  Other similar MAC-level information can be used to guide search
Can also search based on minimum non-zero Hamming distance between stored and received seeds.