## Slide 1: Changes to WARP
Srinivas Kandala (Sharp Laboratories)
Adrian P. Stephens (Mobilian Corporation)
srini@sharplabs.com

## Slide 2: Change of the name of the protocol
Tgi has a similarly sounding protocol – WRAP.
Requested Tge to change the protocol name if possible.
  They are changing the name as well.
No real address resolution function is being performed – a misnomer.
Editor’s resolution :
  Change the name to Direct Link Protocol (DLP)

## Slide 3: Problems with WARP
Protocol overhead is too high to discover the capabilities of the target destination.
It is not clear if the power save works.
  There may be significant delay between the time the PS-Poll frame sent by the target destination and the sender actually receiving the notification. There is no guarantee that the target DA can be awake.
  There could be multiple WSTAs wanting to communicate with the target power-saving DA exacerbating the situation.
Elsewhere in the draft it is mentioned that the Direct links are not allowed with the PS devices:
  Unlikely that the data that needs to be sent to a PS would be high enough to justify the establishment of a direct link.

## Slide 4: Summary of the proposed changes
Delete registration, status notification and wake notification.
Modify location discovery, so that the sender can initiate negotiation with the target destination, with the aid of the QAP.
No changes to direct negotiation procedure.
  Extra security framework may be needed. Work in progress in Tgi.

## Slide 5: Protocol after changes
a1: Location Discovery Request frame from WSTA1 to QAP
a2: Location Discovery Request frame forwarded by QAP to WSTA2
a3: Location Discovery Response frame from WSTA2 to QAP
a4: Location Discovery Response frame forwarded by QAP to WSTA1
b1: Direct Communication Request frame from WSTA1 to WSTA2
b2: Direct Communication Response frame from WSTA2 to WSTA1

## Slide 6: Location Discovery
Needed for discovering the destination and if the destination is in PS-mode, it can change its state.
As BSS relay of management frames is not possible, the request and response frames are overloaded to achieve the desired result.

## Slide 7: Termination of Direct Link
WSTA can terminate the direct link by sending a direct link termination request frame.

## Slide 8: Motion
Instruct the editor to incorporate the normative text in doc 02/438r0