## Slide 1
Short Slot Time Option for TGg Updated Version
  Richard van Nee, Woodside Networks
  Sean Coffey, Texas Instruments

## Slide 2
TGg Slot Time Proposal Context
  Strong support for enhancing .11g throughput by introducing the possibility for short slot times
  Key issues were raised regarding the proposal
  New proposed text addressed those issues

## Slide 3
TGg Slot Time
  Current draft of 11g uses pure IEEE 802.11a, except for slot time which is the longer 802.11b slot time
  The longer slot time significantly reduces the maximum throughput compared to 802.11a at 5 GHz
  TGg currently has no migration path toward an 11g-only network that is as fast as 802.11a at 5 GHz

## Slide 4
6
9
12
18
24
36
48
54
Raw Data Rate [Mbps]
Throughput [Mbps]
Throughput .11g versus .11a
  31 Mbps throughput for .11a versus less than 25 Mbps for .11g at 54 Mbps mode
  Note: Throughput estimates without RTS/CTS using 1500 bytes packet length
0
5
10
15
20
25
30
35
  red: 9µs slot time (.11a)
  blue: 20µs slot time (current .11g)

## Slide 5
Short Slot Time Option
  Introduce a Short Slot Time Subfield in Capability Information Field
  The Access Point signals the short slot time mode in the beacon by setting Short Slot Time Subfield to 1
  If a non-short slot time device* associates, the Access Point sets Short Slot Time Subfield to 0
  All .11g STAs change their slot time when a change in the beacon Short Slot Time Subfield is observed
  * non-short slot time device: Legacy 11b device or 11g device with Short Slot Time Subfield = 0 in its association request

## Slide 6
Summary of Key Issues Addressed
  BSS shall revert to 20 s slot time when a non-short slot device associates
  Overlapping BSS: recommended practice to revert back to 20 s slot time in case of overlap with a co-channel long-slot time BSS
  IBSS mode: recommended practice to use 20 s slot time only

## Slide 7
Motion to Amend
  Amend motion to: ‘include the proposed text in document IEEE802.11-02/470r0 in the TGg draft text’