## Slide 1: Proposal for Informative Schemes for Generating Randomness
Tim Moore, Microsoft
Doug Whiting, HiFn
Clint Chaplin, Symbol Technologies

## Slide 2: Randomness Needed
For key generation, randomness is needed in the stations
Current implementations may not have a good source of randomness
Suggest that we add an informative appendix with possible implementations

## Slide 3: Software Solution
Initialize result to empty array
LoopCounter = 0
Wait until ethernet traffic or association
Repeat until global key counter "random enough" or 32 times {
result = PRF-256(0, "Init Counter", Local Mac Address || Time || result || LoopCounter)
LoopCounter++
Repeat 32 times {
If ethernet traffic available then
Take lowest byte of time when ethernet packet is seen
Concatenate the seen time onto result
else
Start 4-way handshake, but only to reception of message 2
Take lowest byte of time of when message 1 is sent
Take lowest byte of time of when message 2 is received
Take lowest byte of RSSI from message 2
Take SNonce from message 2
Concatenate the sent time; receive time, RSSI and SNonce onto result
}
}
Global key counter = result = PRF-256(0, "Init Counter", Local Mac Address || Time || result || LoopCounter)

## Slide 4: Hardware Assist Solution

## Slide 5: Code for Hardware Assist Solution
Initialize result to empty array
Repeat 1024 times {
Read LFSR
result = result | LFSR
Wait a time period
}
Global key counter = PRF-256(0, "Init Counter", result)

## Slide 6: Call for Motion
Move that the editor incorporate into the draft document 02-xxx as an informational appendix.