## Slide 1: Proposal for Informative Schemes for Generating Randomness
Tim Moore, Microsoft
Doug Whiting, HiFn
Clint Chaplin, Symbol Technologies

## Slide 2: Randomness Needed
For key generation, randomness is needed in the stations
Current implementations may not have a good source of randomness
Suggest that we add an informative appendix with possible implementations

## Slide 3: Software Solution
Two clocks cannot be perfectly correlated
Two widely separated clocks have more decorrelation
Take enough samples, can get enough randomness
Attacker could not perfectly match AP clock
Take samples from wired side if available (heavy broadcast traffic on most normal networks), otherwise create traffic on wireless side using first terminal

## Slide 4: Software Solution
Initialize result to empty array
LoopCounter = 0
Wait until ethernet traffic or association
Repeat until global key counter "random enough" or 32 times {
result = PRF-256(0, "Init Counter", Local Mac Address || Time || result || LoopCounter)
LoopCounter++
Repeat 32 times {
If ethernet traffic available then
Take lowest byte of time when ethernet packet is seen
Concatenate the seen time onto result
else
Start 4-way handshake, but only to reception of message 2
Take lowest byte of time of when message 1 is sent
Take lowest byte of time of when message 2 is received
Take lowest byte of RSSI from message 2
Take SNonce from message 2
Concatenate the sent time; receive time, RSSI and SNonce onto result
}
}
Global key counter = result = PRF-256(0, "Init Counter", Local Mac Address || Time || result || LoopCounter)

## Slide 5: Hardware Assist Solution
Three ring oscillators, separated as much as possible.
Mix in another source of randomness, if available
Use Flip-Flops to avoid metastable state
Feed to maximum cycle length LFSR
Read LFSR multiple times, and hash outputs

## Slide 6: Hardware Assist Solution

## Slide 7: Code for Hardware Assist Solution
Initialize result to empty array
Repeat 1024 times {
Read LFSR
result = result | LFSR
Wait a time period
}
Global key counter = PRF-256(0, "Init Counter", result)

## Slide 8: Call for Motion
Move that the editor incorporate into the draft document 02-477 as an informational appendix.