## Slide 1: Mapping password to PSK
Tim Moore, Microsoft
Doug Whiting, HiFn
Jesse Walker, Intel

## Slide 2
Standardize how to generate a 256 bit PSK from an ASCII password
The proposal uses PBKDF2 from PKCS #5 v2.0: Password-based Cryptography Standard, also RFC2898
  PSK = PBKDF2 (Password, ssid, ssidlength,
    4096, 256)
  Salt is the SSID so PSK different for different SSIDs
Used once when password is saved
Document includes example code and test vectors

## Slide 3
DK = T1 || T2 – concatenate to 256 bits
T1 = F (P, S, c, 1) , T2 = F (P, S, c, 2)
F (P, S, c, i) = U1 xor U2 xor  xor Uc
U1 = HMAC-Sha1 (P, S || Int (i)) , U2 = HMAC-Sha1 (P, U1) , … Uc = HMAC-Sha1 (P, Uc-1)
C is 4096

## Slide 4
Motion to incorporate document 545 as an normative annex