## Slide 1: Validating Disassociate and Deauthenticate messages
Tim Moore

## Slide 2: 802.11 state machine

## Slide 3: Synchronization problem
STA or AP can delete state asynchronously
Two options
  Integrity check of disassociate and deauthenticate cannot work under all cases
    Only when keys are available
  Use AKMP
Either case 802.11 state machine needs to check if keys available before accepting disassociate or deauthenticate messages

## Slide 4: New 802.11 state machine

## Slide 5: Integrity check
New format for messages
Add IE to messages containing Integrity check
Use TKIP/WRAP/CCMP

## Slide 6: AKMP
Start 4-way handshake on receiving disassociate or deauthenticate messages
  Change Supplicant and Authenticator state machines to run 4-way handshake on receiving disassociate or deauthenticate
  Authenticator
    Move DeauthenticateRequest from DISCONNECTED state to PTKSTART state
  Supplicant
    Add new state DISCONNECT. Sends EAPOL-Key Request. Timeout on completing 4-way handshake. Timeout goes to DISCONNECTED state