## Slide 1
802.11e features for the enterprise
Mathilde Benveniste
benveniste@ieee.org
Avaya Labs - Research

## Slide 2: Our Objective
Identify 802.11e features for APs and clients appropriate for the enterprise market

## Slide 3: Performance criteria
Enterprise APs must operate with both EDCF and HCF clients
  EDCF clients used in the home will be brought to the office
Achieving greatest throughput, subject to QoS requirements, is the ultimate goal
  Both EDCF and HCF protocols must be designed for the greatest channel use efficiency
  Near-term implementations will be the future legacy population which, because of backward compatibility requirements, must be efficient
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 4: Market Segmentation vs Technology
Small systems
One or a few BSSs; single owner; no channel reuse; no BSA overlap
Residential/Entertainment Center (controlled RF spectrum usage; few traffic streams – some heavy)
    HCF (CFBs and HCF polling)
SOHO (controlled RF spectrum usage; few traffic streams) 
    EDCF is adequate
  Alternatively,
    downlink by HCF (CFBs)
    uplink data by EDCF or polled HCF
    uplink voice by polled HCF
 Enterprise segments in blue
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 5: cont’ed
Large Systems
Many BSSs reuse channels; overlapping BSAs
Enterprise/Campus/Public spaces – single owner (controlled RF spectrum usage; multiple traffic streams; heavy load) 
    downlink by HCF (CFBs)
    uplink data by EDCF or polled HCF
    uplink voice by polled HCF
Office park - independent owners (uncontrolled RF spectrum usage; multiple traffic streams; heavy load) 
    downlink by HCF (CFBs)
    mix of EDCF and polled HCF
Multi-dwelling unit – independent BSS ownership (uncontrolled RF spectrum usage; multiple traffic streams; heavy load)
    downlink by HCF (CFBs)
    mix of EDCF and polled HCF
 Enterprise segments in blue
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 6: Technology interests for the enterprise
AP Mandatory Functions
HCF CFBs
polled HCF
EDCF
HCF-Client Mandatory Functions
TSPEC
EDCF-RR (QoS null frame sent by WSTA and ShortInactivityTimer at the AP, own top-priority TC with PF=0.5)
Response to polling
EDCF-Client Mandatory Functions
TC Differentiation by AIFS and PF
Other TC parameters: MSDULifetime, CWmin, CWmax
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 7: EDCF-RR for HCF clients
EDCF-RR enables statistical multiplexing of traffic
  For example, at least 2 voice calls can be accommodated in place of 1 voice call
EDCF-RR Mechanism*
  TSPEC used to set up session
  ShrtInactivityTimer is used to drop inactive TID from polling list
  TSPEC is not cancelled due to WSTA short-term inactivity
  Receipt of an RR by the AP will cause the return of TID to the polling list
  the RR function will be achieved by an WSTA’s QoS null frame, which will use its own top-priority TC (PF=0.5 and the shortest AIFS)
*For more detailed discussion see 01/409r1, 02/525r1, and 02/594r0
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 8: PF for EDCF clients
PFs are needed for priority differentiation
  TCs can be differentiated better (a different PF for each TC)
  without PFs, differentiation of TCs above BE is not possible in the presence of legacy STAs
PFs reduce delay and jitter for high priority TCs
PFs are easy to implement (see example for values like 0.5, 1, 1.5, and 2) *
The PFs cause no overhead; remain constant over time (PF need not adapt to traffic)
Proposed alternative approach, namely differentiation by CWmax, can increase collisions if there is no contention window adaptation to traffic
*For more detailed discussion see 01/409r0 and 01/409r1
Notes: Page <number>
        <footer>
<header>
<date/time>

## Slide 9: Conclusions
To achieve enterprise performance goals, it is proposed that we:
  Introduce EDCF/RR mechanism in 02/525r1 for polling-list management
  Re-introduce persistence factors in the simplified form proposed in 409r1 for improved EDCF performance