## Slide 1: Interference Cancellation for Downlink MU-MIMO
Date: 2010-03-15
Authors:
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 2: Abstract
Downlink (DL) Multi-user (MU) MIMO is identified as a key technology to improve the overall network performance
In 09/1234r0 we showed that :
  Interference Cancellation (IC) at the STA makes downlink (DL) MU-MIMO more robust
  To support Interference Cancellation in DL MU-MIMO at the STA:
    AP must transmit enough LTFs to enable channel estimation for the total number of spatial streams in the DL
      We call this mode of LTF transmission the ‘Resolvable LTF’ mode
    AP must signal to each STA which spatial streams are meant for it
This document is a review of IC concept in 09/1234r0 with an additional strawpoll at the end
Notes: doc.: IEEE 802.11-yy/xxxxr0

## Slide 3: Outline
Introduction
  Interference Cancellation
  Receive processing
  Sources of CSI Error at AP
Simulation results for 40MHz and reasonable product configurations
  AP with 4Tx; Clients have 2 Rx
  AP with 8Tx; Clients have 3 Rx
Conclusions
Straw poll

## Slide 4: Introduction to Interference Cancellation
In DL MU-MIMO, clients can have more receive (Rx) antennas than the number of spatial streams they receive
  The additional antennas can be used for Interference Cancellation (IC) / Interference Suppression
  Particularly useful when precoding is imperfect due to errors in the CSI available at the AP
This calls for a DL MU-MIMO preamble design that can support IC
  Each client should receive as many LTFs as needed to train the total number of spatial streams in the DL
  Each client should know which spatial streams are meant for it

## Slide 5: Receive MMSE for Interference Suppression
For instance, consider a 4-antenna AP transmitting 1 ss each to 4 STAs each with 2 Rx antennas, the Rx signal at 8 Rx antennas is given by:
The equivalent precoded channel is Hequiv = H8x4W4x4
The first two rows of Hequiv is the channel seen by STA1; H1 = Hequiv(1:2,:)
STA1 can do the following MMSE processing to reduce the interference from other STAs:
where the first element of x1 gives the estimate of the symbol for STA1 and 12 is the noise variance at STA1

## Slide 6: Sources of CSI Errors at AP
Pathloss to the STA or the amount of quantization in the CSI feedback report
  The channel estimation SNR or quantization level is fundamental to the accuracy of CSI
Time variations in the channel
  A non-zero time interval between CSI feedback and DL MU-MIMO transmission causes discrepancies between precoding weights and the actual channel
    Feedback delay of 20 ms results in an error floor of -25 dBc (assuming a coherence time of 800 ms)
Modeled as two independent additive noise sources in the CSI
  CSI Feedback Delay Error Floor {-20, -25, -30} dBc
  Channel Estimation Error Floor (Pathloss dependent)
At high SNRs, CSI feedback errors dominate and at low SNRs, pathloss errors dominate

## Slide 7: Simulations
Determine the gains of using MU-MIMO and Interference Cancellation (IC)
  We plot the 10 percentile and 50 percentile points from the CDF of the aggregate PHY throughput (measured at the AP) as a function of pathloss
  For comparison, we also plot the corresponding sequential beamforming (BF) data quantities
    SVD based transmission with equal MCS per spatial stream
    Data rates averaged across sequential transmissions to the clients

## Slide 8: Results for 4 antenna AP, Four clients each with 2 Rx, full loading

## Slide 9: Simulation Parameters
AP with 4 Tx antennas transmitting at 24 dBm
Noise floor of -89.9 dBm
4 STA with 2 Rx antenna each
-35 dBc of TX distortion
Equal Pathloss to each STA, varied from 70 to 95 dB
Single SS per STA in the MU-MIMO case and 2 ss for Tx BF case
TGac Channel Model D, NLOS
  Results for 200 channel realizations
For MU-MIMO, MMSE precoding done to beamform the 1 ss of each STA to one of its antennas
Two sources of CSI error at AP
  Channel estimation floor at client = -(Total Tx Power – Pathloss + 89.9 dBm (Thermal noise))
  Feedback delay error = {-20, -25 ,-30} dBc

## Slide 10: 4 antenna AP, Four 2 Rx clients, -20 dBc feedback error
MU-MIMO with IC gives best performance
  Interference Cancellation improves performance for a poor CSI accuracy
IC enables full loading
  Compare with slide 22 in Appendix, which shows the 3 ss results
  Performance better with 3 ss in the absence of IC
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC

## Slide 11: 4 antenna AP, Four 2 Rx clients, -25 dBc feedback error
For all pathlosses between 70 and 95, MU-MIMO with IC gives substantial gains
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC

## Slide 12: 4 antenna AP, Four 2 Rx clients, -30 dBc feedback error
For all pathlosses between 70 and 95, MU-MIMO with IC gives best performance
  Gains of IC reduce as CSI accuracy improves
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC

## Slide 13: Results for 8 antenna AP, Three clients each with 3 Rx

## Slide 14: Simulation Parameters
AP with 8 Tx antennas transmitting at 24 dBm
Noise floor of -89.9 dBm
3 STA with 3 Rx antenna each
-35 dBc of TX distortion
Equal Pathloss to each STA, varied from 70 to 95 dB
Two SS per STA in the MU-MIMO case and 3 ss for Tx BF case
TGac Channel Model D, NLOS
  Results for 200 channel realizations
For MU-MIMO, MMSE precoding done to beamform the 2 ss of each STA to two of its antennas
Two sources of CSI error at AP
  Channel estimation floor at client = -(Total Tx Power – Pathloss + 89.9 dBm (Thermal noise))
  Feedback delay error = {-20, -25 ,-30} dBc

## Slide 15: 8 antenna AP, Three 3 Rx clients, -20 dBc feedback error
MU-MIMO with IC gives best performance
  IC improves performance for a poor CSI accuracy

## Slide 16: 8 antenna AP, Three 3 Rx clients, -25 dBc feedback error
For all pathlosses between 70 and 95, MU-MIMO with IC gives best performance

## Slide 17: 8 antenna AP, Three 3 Rx clients, -30 dBc feedback error
Gains of IC reduce here
  Precoding is very good

## Slide 18: Conclusions
IC makes MU-MIMO robust to poor CSI accuracy at the AP
  Significantly improves PHY throughput
  Enables fully loaded MU-MIMO
This calls for a DL MU-MIMO preamble design that can support IC
  AP must transmit enough LTFs to enable an STA to train the total number of spatial streams in the DL
  AP must signal to each STA which spatial streams are meant for it

## Slide 19: Straw Poll
Do you support the Interference Cancellation concept described in this document by inclusion of the following section and text in the Tgac spec framework document:
“4.1 Resolvable LTFs for DL MU-MIMO
In a DL MU-MIMO transmission, LTFs are considered “resolvable” when the AP transmits enough LTFs for an STA to estimate the channel to all spatial streams of every recipient STA. In order to enable interference cancellation at an STA during a DL MU-MIMO transmission, an AP may transmit the preamble using resolvable LTFs. ”
  Yes
  No
  Abstain

## Slide 20: Appendix

## Slide 21: Methodology used to get to Data Rate CDFs
For each spatial stream
  Calculate the post processing SINR on each tone
  Map the post processing SINR to capacity using log(1+SINR)
  Average the capacity across tones to get Cav
  Use Cav to calculate SINReff using Cav = log(1+ SINReff)
  Map the SINReff to a rate using the AWGN rate table
This method is used in other WAN standards, e.g., 3GPP2
Sum the rate across all spatial streams for one channel realization to get to aggregate PHY throughput
Do this for 200 channels to get to the CDF of aggregate PHY throughput

## Slide 22: 4 antenna AP, Three 1x1 clients, -20 dB feedback error
For all pathlosses between 70 and 95, MU-MIMO gives substantial gains
IC curve lies on top of MU-MIMO w/o IC
  In absence of IC, 4 SS MU-MIMO performs worse than 3 SS MU-MIMO
    Compare green curve of this slide with blue curve of slide 10
    Better to transmit at 75% loading in the absence of extra antenna at the STAs
      Scheduler decision
70
75
80
85
90
95
100
200
300
400
500
600
700
800
Pathloss in dB
PHY Rate in Mbps measured at AP
Variation of 10 percentile PHY Rates with pathloss
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC
70
75
80
85
90
95
100
200
300
400
500
600
700
800
Pathloss in dB
PHY Rate in Mbps measured at AP
Variation of 50 percentile PHY Rates with pathloss
Eigen BF TDMA
MU-MIMO w/o IC
MU-MIMO with IC