## Slide 1
Notice: This document has been prepared to assist IEEE 802.19. It is offered as a basis for discussion and is not binding on the contributing individual(s) or organization(s). The material in this document is subject to change in form and content after further study. The contributor(s) reserve(s) the right to add, amend or withdraw material contained herein.
Authors:
Radio Resource Measurement for TVWS application under FCC rules
Date: 2010-03-30

## Slide 2: Motivation
According to FCC rule, all devices to be used for TVWS must have sensing capability.
In the event of successful primary signal detection FCC rule requires immediate evacuation of the channel.
The 802.11 WLAN devices inherently embrace sensing capability for media access purpose.
The sensing capability of the 802.11 WLAN devices should be extended/modified to suite the TVWS domain.

## Slide 3: Summary
  TV signal detection
    We propose to modify the basic measurement report to include TV broadcast signal detection to suite TVWS domain

## Slide 4: Proposed modification on the Map field format for Basic report frame
Proposed Map field format for 802.11af
(IEEE Std 802.11™-2007)

## Slide 5: Proposed text corresponding to the “TV signal” bit in the Map field format
TV signal bit, which shall be set to 1 when TV broadcast signal, is detected operating in the channel during the measurement period.
The algorithm to detect TV broadcast signal shall satisfy regulatory requirements and is outside the scope of this standard. Otherwise, the TV signal bit shall be set to 0.