## Slide 1: Towards carrier-grade 802.11 at Disney theme parks
Date: 2010-03-16
Authors:

## Slide 2: summary
about Disney & Disney Research
deployment scenarios & application examples
  detailed analysis for Magic Kingdom
TVWS opportunity for Magic Kingdom application
  channel availability, link budget
need for frequency division duplex
conclusions

## Slide 3: about Disney
some of our divisions / ventures with interest in carrier-grade 802.11 & TVWS:
  Walt Disney Studio Entertainment
  Disney Consumer Products
  Walt Disney Parks and Resorts
  Disney Cruise Line
  Disney Interactive Media Group
  Disney-ABC Television Group
  ESPN Inc.
  Radio Disney

## Slide 4: about Disney Research
mission
  Invent new technologies for the media & entertainment industry
  Take research results to market: spin-in or spin-out
organization
  Association of research labs: Disney Research Zurich & Pittsburgh, Pixar Research, Walt Disney Animation Studios Research, Walt Disney Imagineering Research, Disney Interactive Media Group Research
areas of research
  AI & Autonomous Agents, Computer Graphics, Computer & Sensor Networks, Computer Vision, Display Technologies, Mobile Computing, Radios & Antennas, Robotics, Video Processing, …

## Slide 5: deployment areas of carrier-grade 802.11

## Slide 6: application examples of carrier-grade 802.11
802.11-enabled handheld
audio and video streaming
real time information
interactive games in queues
real time social interaction
example: Mobile Magic
  disneyparksmobile.com
  m.disneyland.com

## Slide 7: Magic Kingdom
around 50,000 visitors per day
  Source: TEA/ERA. “Theme Park Attendance Report 2008” www.themeit.com [2009]
size around 370m radius (107 acres)
one access point in the middle of the park
  carrier-grade access point

## Slide 8: Magic Kingdom application requirements
long range
  large coverage area (connected toys)
  hard to install infrastructure because of attractions
high capacity
  high user density, especially in proximity of rides
high throughput
  audio and video streaming
good QoS
  interactive games
low-complexity
  affordable in consumer electronics

## Slide 9: Magic Kingdom TVWS
a few channels available in Disneyworld
FCC regulations separate fixed and portable channels
Source: www.showmywhitespace.com

## Slide 10: link budget estimation
Path loss mode: Okumura-Hata, suburban
Thanks to Sid Shetty (shettysid@gmail.com) for contribution to the link budget

## Slide 11: system parameters
modulation parameters
  64-QAM, 5/6, 5MHz bandwidth. 16.25Mbps at 800ns GI
bandwidth
  8 channels x 5 MHz
throughput
  132Mbps data rate, single spatial stream
  528Mbps data rate, four spatial streams
comparison with other technologies
  only one access point as compared to 802.11g or 802.11n that requires infrastructure
  single-cell throughput comparable to WiMAX

## Slide 12: carrier-grade 802.11 frequency division duplex

## Slide 13: evaluation scenario 3 clients per access point

## Slide 14: comparing FDD with 802.11
scenario: two downlink & two uplink streams (high and low priority)
802.11:
single channel
1x12Mb/s
FDD:
dual channel
2x6Mb/s
same thrp.
slightly higher delay

## Slide 15: FDD advantages
potentially more TVWS channels available for 802.11
  example: Magic Kingdom application
802.11 could be deployed in any paired spectrum
  WiMAX
  LTE, including 700 MHz
facilitates regulation for multiple operators
performance
  Simulation shows FDD throughput similar to CSMA
  FDD allows to reserve capacity to the access point for carrier-grade networks

## Slide 16: conclusions
potential use of 802.11 enabled handhelds in Disney theme parks
  mobile and fixed operation
  single TVWS base station to cover the theme park
Magic Kingdom example
  separate uplink and downlink due to FCC regulations
  need FDD
PHY requirements
  PHY changes for low cost implementation (OOB filtering)
MAC requirements
  single transmitter for half duplex: dual channel CCA & NAV
  coordinated dual-radio for full duplex: dual channel CCA & NAV
  modified NAV rules
a step towards carrier-grade 802.11 with FDD
  allows to reserve capacity to the access point
  collision detection instead of collision avoidance
  operation in licensed, paired spectrum

## Slide 17: thank you for your attention! www.disneyresearch.com