## Slide 1: PHY Abstraction for MU-MIMO in TGac
Date: 2010-03-15
Authors:

## Slide 2: Overview
Show calculation complexity problem of MAC SAP throughput evaluation for MU-MIMO
Present one possible PHY abstraction which limits the number of STAs
Show the transmission performances in the presented PHY abstraction

## Slide 3: Introduction
Calculation complexity of PHY / MAC simulation for MU-MIMO may be heavy since MCS code and PER changes corresponding to the combination of STAs
[1] describes modifications to AoA and AoD for MU-MIMO, and suggests single random offset uniformly distributed over 180
Large number of STAs which located over 180 significantly increases the number of STA combinations
Calculation complexity reduction by PHY abstraction may be valuable for TGac

## Slide 4: Example of PHY / MAC simulation
One possible example based on “Black Box” approach [3]
PHY Model
Channel Model
Table
Channel sets
Max PLR, MSDU size,
MAC header size,
Retry limit,
Delay time,
STAs Combination, …
Channel Model Number,
Coherence time, Locations of STAs
Select channel model
Channel sets are generated for NU STA
Calculate PER in the selected MCS code for all the combinations of STAs
Look up table (LUT) consisting of MCS codes and PER
Calculation complexity in MAC simulation becomes large as the LUT size increases

## Slide 5: Number of STA Combinations
Number of STA combinations when the number of STAs with which an AP simultaneously communicate is 1, 2, 3, or 4
LUT size is proportional to the number of STA combinations
The STA number, NU, needs to be large to investigate transmission performances of STAs whose offset angles are distributed over 180,

## Slide 6: PHY Abstraction Approach
Reduce calculation complexity by limiting number of STAs for MU-MIMO
Must investigate the transmission performance since the limited STAs scenario may not be a general case

## Slide 7: PHY Abstraction Method
Limit number of STAs for MU-MIMO
As one example of PHY abstraction in in-home entertainment application, downlink transmission at the AP other than VoIP application [3] are selected
AP
S1
S7
S2
S8
S3
S9
S4
S10
S11
S13
S14
S12
S14
S6
S5
AP
S1
S7
S2
S8
S3
S9
S4
S10
S11
S13
S14
S12
S14
S6
S5

## Slide 8: Simulation Conditions
SINRs in the limited STAs approach and random offset angle approach are compared
Channel model C is used based on following parameters
  8  1 MISO, Coherence time of 800 ms, Noise variance of -100 dBm
  100 channel in delay time, t, of 0 ms and 40 ms are generated for each STA
  Tx weight is calculated using channel at t of 0 ms based on zero forcing
S1
S4
S10
S11
S1
S4
S10
S11
Limited STAs approach
Random offset angle approach
STA1 (0, 5m)
STA4 (45, 9.9m)
STA10 (-45, 14.1m)
STA11 (-63.4, 11.2m)
Offset angle is set to be over 180
STA1 (0 180, 5m)
STA4 (45 180, 9.9m)
STA10 (-45 180, 14.1m)
STA11 (-63.4 180, 11.2m)
Notes: test

## Slide 9: SINR for Two STAs MU-MIMO
CDFs of SINR in MU-MIMO when AP communicates with two STAs using perfect channel state information (CSI) (0 ms) and outdated CSI corresponding to 40 ms
Differences of median values are less than 1.3 dB
t = 0 ms
t = 40 ms

## Slide 10: SINR for Four STAs MU-MIMO
SINRs in limited STA approach is slightly higher than those in random offset angle approach
Difference is very small while number of STA combinations is significantly reduced
t = 0 ms
t = 40 ms

## Slide 11: Results of Performance Evaluation
The impact of limiting number of STAs with fixed offset angles is very small because the spatial correlation is small in TGac channel model.
The presented PHY abstraction is one candidate of PHY abstraction for reduction of the calculation complexity

## Slide 12: Summary
Present PHY abstraction which limits STA number and fix offset angle
Show example of PHY abstraction in in-home entertainment application (STA1, STA4, STA10, STA11)
Confirm that similar distributions of SINR in the limited STA approach and the random offset angle approach
Presented PHY abstraction is valid to reduce the calculation complexity in MAC simulation

## Slide 13
References
[1] 11-09/1274r0 TGac Channel Model Addendum
[2] 11-09/0992r3 Specification Framework for TGac
[3] 11-04/0218r3 Unified “Black Box” PHY Abstraction Methodology
[4] 11-09/0451r11 TGac Functional Requirements and Evaluation Methodology

## Slide 14: Straw poll
Do you think PHY abstraction method for MU-MIMO is needed?
  Yes
  No
  Abstain
Do you agree to include PHY abstraction methods as a recommendation in FR&EM document?
  Yes / No / Abstain