## Slide 1: Mechanism for Inter-system Coexistence
Date: 2010-05-16
Authors:

## Slide 2: Summary
This document presents a coexistence mechanism for the ongoing 802.11ad and the completed 802.15.3c
Two alternative coexistence mechanism are proposed
A simple procedure to manage network discovery between heterogeneous systems is proposed
A ‘common platform’ to bridge negotiation between the heterogeneous systems is proposed

## Slide 3: Abbreviations
CB – coexistence beacon
CCI – co-channel interference
CC – convolutional coding
DEV – device
ED – energy detection
MCS – modulation and coding scheme
RS – Reed Solomon
STA – station

## Slide 4: Presentation Outline
Background
Motivation
The Basics
Proposed Coexistence Mechanism
Plan A Details
Plan B Details
CB Frame Format
Operating Range
Additional Notes
Conclusion

## Slide 5: Background
There are two 60GHz unlicensed wireless system specifications in the IEEE 802
The 802.15.3c has a completed MAC/PHY specification in the 60GHz band
The 802.11ad is currently specifying MAC/PHY for operation in the 60GHz band
It is expected that two systems will have to agree on some mechanism to achieve mutual coexistence (i.e. network discovery)
A mechanism for such purpose was proposed in 10/231r3
Up-to-date, there is no mechanism facilitating cross-802 heterogeneous system coexistence in the 802.11ad effort

## Slide 6: Motivation
Nevertheless, coexistence is still an essential topic
  Detection better than ED is required for CCI mitigation
  Coexistence assurance is needed for the sponsor ballot
Therefore, this proposal proposes a mechanism to facilitate coexistence between 802.15.3c and 802.11ad while minimizing the additional complexity in implementation

## Slide 7: The Basics - Main Idea
Heterogeneous network discovery is participated by both the existing and incoming network
The existing network periodically sends out beacon-like signals for potentially incoming heterogeneous networks
The incoming network scans to detect the existing network before setting up a new network
The scanning and detection are performed through a predefined and pre-agreed common bridge (i.e. PHY specification)

## Slide 8: The Basics - How It Works

## Slide 9: The Basics - Common Platform
Name for the predefined and pre-agreed PHY layer design
  ‘Common platform’
The candidates for the Common Platform:
  2.4/5GHz WLAN – the most robust MCS
  802.15.3c WPAN – the most robust MCS
  Hybrid of both

## Slide 10: The Basics - Operational Procedure
Existing DEV/STA coordinating a network in the current channel
  CB transmitted using the Common Platform periodically
Prospective heterogeneous system DEV/STA enters the channel, performs scan
  Receives CB in the Common Platform
Incoming heterogeneous system DEV/STA subjected to following options:
  Decode and extract information in CB for synchronization
  Try another channel
  Stop communication
Incoming and existing DEV/STA can now coordinate respective networks in the same location
Once incoming DEV/STA starts new network, periodical CB transmission continues

## Slide 11: Proposed Coexistence Mechanism
Two mechanism proposed: Plan A and Plan B
Unified operational procedure with different combinations of Common Platform
Candidates of Common Platform
  Plan A
    2.4/5 GHz WLAN MCS
      OFDM, BPSK, CC rate ½, 5MHz channel spacing
  Plan B
    2.4/5 GHz WLAN MCS and 802.15.3c WPAN MCS
      OFDM, BPSK, CC rate ½, 5MHz channel spacing
      SC, p/2-BPSK, RS (255,239), 2160MHz channel spacing

## Slide 12: Plan A - Procedure

## Slide 13: Plan A - Analysis
802.11ad radios will have dual-radio architecture
  60GHz 802.11ad radio
  2.4/5GHz 802.11 radio – Common Platform
The current situation in 802.11ad is leaning towards zero 802.15.3c/802.11ad coexistence
Instead of zero coexistence, this method gives a possibility for 802.11ad and 802.15.3c to discover each other
Future 60GHz radios may need to implement 802.11 2.4/5GHz radio anyway
Making 802.11 MCS the Common Platform is a reasonable approach
With Plan A as the base for heterogeneous coexistence, Plan B may be an enhancement to further increase the level of coexistence

## Slide 14: What is Plan B
Plan B has similar operational procedure as Plan A, with an additional Common Platform candidate
      The additional Common Platform is the 802.15.3c WPAN Common Signaling Mode (i.e. SC, p/2-BPSK, RS (255,239), 2160MHz channel spacing )

## Slide 15: Plan B - Procedure

## Slide 16: Plan B – Analysis
802.11ad radios may have dual-radio architecture
  60GHz 802.11ad radio
  2.4/5GHz 802.11 radio – Common Platform 1
  60GHz 802.15.3c radio – Common Platform 2
In Plan A, a certain level of coexistence can be facilitated with 802.15.3c system that supports the Common Platform (i.e. 2.4/5GHz WLAN MCS)
In order to further boost the harmony in the 60GHz band environment, Plan B with an additional Common Platform is able to facilitate coexistence with 802.15.3c DEVs that are not supporting the 2.4/5GHz WLAN MCS

## Slide 17: CB Frame Format
The CB frame for facilitating heterogeneous system coexistence can reuse most of the existing beacon frame
Some additional information need to be included in the CB:
  Timing information for the CB
  Operation mode of the existing network
  Coexistence capability of the existing network

## Slide 18: Operating Range
By employing the 2.4/5 GHz WLAN MCS, the operating range is substantially different from that of a 60GHz signal
Transmit power control has to be used to confine the 2.4/5 GHz CB within the intended radio sphere of influence

## Slide 19: Additional Notes
The dual/tri-radio architecture, besides offering a higher capability of coexistence, provides other advantages such as user experience and system optimizations
One example is given in 10/259r2

## Slide 20: Conclusion
This document proposes a method for cross-802 system coexistence – 802.11ad and 802.15.3c
Coexistence between the two systems is important to:
  Mitigate the devastating CCI that causes performance degradation
  Construct the coexistence assurance document

## Slide 21: Straw Poll
Do you support inclusion of coexistence technique Plan A, as described in 10/0485r0 in the TGad draft amendment?
Yes: . No: . Abstain: .
Do you support inclusion of coexistence technique Plan B, as described in 10/0485r0 in the TGad draft amendment?
Yes: . No: . Abstain: .