## Slide 1: Mechanism for Inter-system Coexistence
Date: 2010-05-19
Authors:

## Slide 2: Summary
This document presents a potential coexistence mechanism for the ongoing 802.11ad and the completed 802.15.3c
Two alternative coexistence mechanism are discussed
A simple procedure to manage network discovery between heterogeneous systems is presented
A ‘common platform’ to bridge negotiation between both systems is presented

## Slide 3: Abbreviations
CB – coexistence beacon
CCI – co-channel interference
CC – convolutional coding
DEV – device
ED – energy detection
MCS – modulation and coding scheme
RS – Reed Solomon
STA – station

## Slide 4: Presentation Outline
Background
Motivation
The Basics
Proposed Coexistence Mechanism
Plan A Details
Plan B Details
CB Frame Format
Operating Range
Additional Notes
Conclusion

## Slide 5: Background
There are two 60GHz unlicensed wireless system specifications in the IEEE 802
The 802.15.3c has a completed MAC/PHY specification in the 60GHz band
The 802.11ad is currently specifying MAC/PHY for operation in the 60GHz band
It is hoped that two systems will have to agree on some mechanism to achieve mutual coexistence (i.e. network discovery)
Mechanism for such purpose were proposed
  10/231r3
  10/432r2
  10/498r3

## Slide 6: Motivation
Coexistence is the basic essential requirement
  Detection better than ED is desired for CCI mitigation
  Coexistence assurance is required across 802 systems
Therefore, this proposal explores mechanism that facilitate the coexistence between 802.15.3c and 802.11ad while minimizing the additional complexity in implementation
On top of the proposed coexistence method, this presentation intends to explore the possibilities to further optimize radio resource sharing

## Slide 7: The Basics - Main Idea
Heterogeneous network discovery is participated by both the existing and incoming network
The existing network periodically sends out beacon-like signals for potentially incoming heterogeneous networks
The incoming network scans to detect the existing network before setting up a new network
The scanning and detection are performed through a predefined and pre-agreed common bridge (i.e. PHY specification)

## Slide 8: The Basics - How It Works

## Slide 9: The Basics - Common Platform
Name for the predefined and pre-agreed PHY layer design
  ‘Common platform’
The candidates for the Common Platform:
  2.4/5GHz WLAN – the most robust MCS
  60GHz – the most robust MCS
  Both

## Slide 10: The Basics - Operational Procedure
Existing DEV/STA coordinating a network in the current channel
  CB transmitted using the Common Platform periodically
Prospective heterogeneous system DEV/STA enters the channel, performs scan
  Receives CB in the Common Platform
Incoming heterogeneous system DEV/STA subjected to following options:
  Decode and extract information in CB for synchronization
  Try another channel
  Stop communication
Incoming and existing DEV/STA can now coordinate respective networks in the same location
Once incoming DEV/STA starts new network, periodical CB transmission continues

## Slide 11: Proposed Coexistence Mechanism
Two mechanism proposed: Plan A and Plan B
Unified operational procedure with different combinations of Common Platform
Candidates of Common Platform
  Plan A
    2.4/5 GHz WLAN MCS
      OFDM, BPSK, CC rate ½, 5MHz channel spacing
  Plan B
    2.4/5 GHz WLAN MCS and 802.15.3c WPAN MCS
      OFDM, BPSK, CC rate 1/2, 5MHz channel spacing
      SC, p/2-BPSK, RS (255,239), 2160MHz channel spacing

## Slide 12: Plan A - Procedure

## Slide 13: Plan A - Analysis
802.11ad radios will have dual-radio architecture
  60GHz 802.11ad radio
  2.4/5GHz 802.11 radio – Common Platform
This method gives a possibility for 802.11ad and 802.15.3c to discover each other
802.11ad 60GHz radios (future 802.15.3c radios for that matter) may implement 802.11 2.4/5GHz radio for multiband operation
Making 802.11 MCS the Common Platform is a reasonable approach
With Plan A as the base for heterogeneous coexistence, Plan B may be an enhancement to further increase the level of coexistence

## Slide 14: What is Plan B
Plan B has similar operational procedure as Plan A, with an additional Common Platform candidate
      The additional Common Platform is the 802.15.3c WPAN Common Signaling Mode (i.e. SC, p/2-BPSK, RS (255,239), 2160 MHz channel spacing )

## Slide 15: Plan B - Procedure

## Slide 16: Plan B – Analysis
802.11ad radios may have dual-radio architecture
  60GHz 802.11ad radio
  2.4/5GHz 802.11 radio – Common Platform 1
  60GHz 802.15.3c radio – Common Platform 2
In Plan A, a certain level of coexistence can be facilitated with 802.15.3c system that supports the Common Platform (i.e. 2.4/5GHz WLAN MCS)
In order to further enhance the harmony in the 60GHz band environment, Plan B with an additional Common Platform is able to facilitate coexistence with 802.15.3c DEVs that are not supporting the 2.4/5GHz WLAN MCS
With further signal decoding, synchronization between the two radios may also be achieved for optimized resource sharing

## Slide 17: CB Frame Format
The CB frame is a coexistence frame for facilitating coexistence and it reuses some of the elements in the existing beacon frame
Basic network discovery lies in the preamble of the CB
In order to achieve higher level of synchronization, some additional information may be included in the CB:
  Timing information for the CB
  Operation mode of the existing network
  Coexistence capability of the existing network
  Resource sharing information (CFP sharing)

## Slide 18: Operating Range
By employing the 2.4/5 GHz WLAN MCS, the operating range is substantially different from that of a 60GHz signal
Transmit power control has to be used to confine the 2.4/5 GHz CB within the intended radio sphere of influence

## Slide 19: Additional Notes
The dual/tri-radio architecture, besides offering a higher capability of coexistence, provides other advantages such as resource optimization
There are other proposals in TGad proposing multi-radio (multiband) operation for other purposes
Examples are
  10/432r0
  10/259r2
  10/446r0

## Slide 20: Conclusion
This document discusses a method for cross-802 system coexistence – 802.11ad and 802.15.3c
Coexistence between the two systems can basically mitigate CCI that causes performance degradation, if not achieving higher level of synchronization for optimum radio resource sharing