## Slide 1
[Intra cluster response model and parameter for the enterprise cubicle environments at 60GHz (Part3)]
Date: 2010-5-19
Authors:

## Slide 2: Abstract
Intra cluster channel model is developed by high resolution measurement for the enterprise cubicle environments.
For far location
  The channel model parameter kb and gb for far location are re-measured and confirmed reasonably low compared with the previous our report(372r0)
  This leads to the necessity of a cluster model - 23.4 dB down from LOS component
For near location
  The channel model parameter kb and gb are re-measured and confirmed as reasonable values compared with the previous our report(372r0)
  One ray cluster model is good to represent this environment

## Slide 3: Floor plan of cubicle environments
Desk
160×70
STA
AP height:2.5m
STA height:0.7m
from floor
Impulse responses are measured at each location
STA
Near location
Far location

## Slide 4: Direct and reflection wave paths in cubicle environments
Far location
Near location
Multiple-time-reflected waves on desktop were observed
Reflection wave characteristics from ceiling should be clarified for channel modeling
Direct wave
Reflection wave
Tx

## Slide 5: High resolution measurements for cubicle environment
160cm
70cm
20cm
50cm
15cm
10cm
Measured points (Total: 26)
High resolution measurements have been carried out with 2 lines separated by 30 cm and 13 measurement points per line, 10 cm separated each other on the desk top
Additional measured points on desktop

## Slide 6: Measurement system for cubicle environments
Network
Analyzer
Tx antenna is near the ceiling(AP)
Rx antenna is on the desktop(STA)

## Slide 7: High Resolution Measurement set up forTGad defined enterprise cubicle environment
Parameter | Value
Center frequency | 62.5 GHz
Band width | 3 GHz
Number of frequency points | 801
Frequency step | 3.75 MHz
Antenna type | Conical horn
HPBW of antenna | 30 degree (STA), 90 degree (AP)
Polarization | Vertical(STA), Circular(AP)
Calibration | Direct port connection without antennas

## Slide 8: High resolution measurement results (far location)
Total number of measured response is 26
Reflection waves
Direct waves
23.4dB
kb=7.4dB
30.8dB
Direct path and single ray will be enough as the channel model for cubicle environment (far location)

## Slide 9: Intra-cluster parameters for cubicle environments(far location)
Environments Far location |  | kf [dB] | kb [dB] | gf [ns-1] | gb [ns-1] | lf [ns-1] | lb [ns-1] | Distribution, for forward | Distribution for backward
Cubicle AP-STA | High resolution | 5.1 | 7.4 | 3.1 | 6.0 | 0.55 | 0.53 | Rayleigh | Rayleigh
 | Previous Estimation Doc.10/372r0 | N/A | 22.5 | N/A | 14 | N/A | 0.81 | N/A | Rayleigh
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution
Tx antenna (AP)
HPBW: 90deg
C pol.
Rx antenna (STA)
HPBW: 30deg
V pol.
kb and gb are reasonably low compared with the previous report

## Slide 10: High resolution measurement results (near location)
Total number of measured response is 26
Reflection waves
Direct waves
25.3dB
kb=15.3dB
40.6dB
Direct path and one ray will be enough as the channel model

## Slide 11: Intra-cluster parameters (near location)
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution
Tx antenna (AP)
HPBW: 90deg
C pol.
Rx antenna (STA)
HPBW: 30deg
V pol.
Environments Near location |  | kf [dB] | kb [dB] | gf [ns-1] | gb [ns-1] | lf [ns-1] | lb [ns-1] | Distribution, for forward | Distribution for backward
Cubicle AP-STA | High resolution | 5.4 | 15.3 | 0.80 | 5.5 | 1.6 | 2.2 | Rayleigh | Rayleigh
 | Previous estimation Doc.10/372r0 | N/A | 24.5 | N/A | 0.690 | N/A | 1.13 | N/A | Rayleigh

## Slide 12: Conclusion
Intra cluster channel model is developed by high resolution measurement for the enterprise cubicle environments.
For far location
  The channel model parameter kb and gb for far location are re-measured and confirmed reasonably low compared with the previous our report(372r0)
  This leads to the necessity of a cluster model - 23.4 dB down from LOS component
For near location
  The channel model parameter kb and gb are re-measured and confirmed as reasonable values compared with the previous our report(372r0)
  One ray cluster model is good to represent this environment

## Slide 13
Appendix: Measurement for reflected wave by ceiling
for the cubicle environment (near location)
Reflection wave
Tx
Rx
1m
3m
The reflected waves by ceiling are measured at each grid point (separated by 1m) in the room (Total measured points are 20).
Measurement system
Measurement points
in the room
1m
1m

## Slide 14: Reflection Wave Measurement Set up (from ceiling)
Parameter | Value
Center frequency | 62.5 GHz
Band width | 3 GHz
Number of frequency points | 801
Frequency step | 3.75 MHz
Antenna type | Conical horn
HPBW of antenna | 30degree
Polarization | Vertical
Calibration | Direct port connection without antennas

## Slide 15: Measured impulse response examples
Reflected waves by metal frame, pipe and concrete wall were observed in measured impulse responses
Reflected wave power varies up to 15dB depending on the position
15dB
Metal frame reflection
Pipe reflection
Concrete wall reflection

## Slide 16: Cause of reflected wave power variation
Behind the ceiling
Metal frame
Concrete
Shielded pipe
Cable
The behind the ceiling are metal frames, pipes , and concrete wall
Metal frames cause strongest reflection waves
Incident wave
Plaster board
Concrete wall
Metal frame
60cm
Detail of two reflected waves
Pipe
30cm

## Slide 17: Plaster board penetration loss measurement
Tx
Rx
Snap shot of penetration loss measurement
Penetration loss
Penetration loss is about 0.7～2dB
Plaster board does not reflect strongly

## Slide 18: Reflected wave power
Power difference are about average 12dB in each position
Reflected wave power in cubicle environment depends heavily on the position
12dB down in average

## Slide 19: Impulse responses of AP-STA (AP antenna HPBW:90deg, C pol., STA antenna HPBW:30deg, V pol.)
The strong reflection wave by metal frame is included.
If there is no metal frame, reflection wave power is very small
Near location scenario
Direct waves
Reflection waves
18dB
12dB
No metal
frame

## Slide 20: Consideration of the channel model for the cubicle environment (near location)
There are two situations for reflected waves by ceiling.
Intra cluster channel model including reflection wave by metal frame is required for the simulation of worst case (See slide 19).
On the other hand, reflection wave is very small (30dB lower than direct wave) when there is no metal frame in the ceiling. In this case, channel model may not be required.

## Slide 21: Intra-cluster parameters for cubicle environments (near location)
Environments Near location |  | kf [dB] | kb [dB] | gf [ns-1] | gb [ns-1] | lf [ns-1] | lb [ns-1] | Distribution, for forward | Distribution for backward
Cubicle AP-STA | For worst case※ | 7.2 | 12 | 0.46 | 1.8 | 0.47 | 0.88 | Rayleigh | Rayleigh
 | Previous estimation Doc.10/372r0 | N/A | 24.5 | N/A | 0.690 | N/A | 1.13 | N/A | Rayleigh
t = 0
Time of arrival
kb
kf
Central ray of intra-cluster
Arrival rate, lb
Arrival rate, lf
Ray decay factor, gb
Ray decay factor, gf
Rayleigh distribution
Rayleigh distribution
Tx antenna (AP)
HPBW: 90deg
C pol.
Rx antenna (STA)
HPBW: 30deg
V pol.
※The parameters are extracted from reflected waves by ceiling