## Slide 1: MFQ MMPDU MAC Sequence Numbering
Date: 2010-06-01
Authors:

## Slide 2: Abstract
A proposal for MAC sequence numbering of MMPDUs that are subject to Management Frame QoS (MFQ).

## Slide 3: Purpose of MAC Sequence Number
Duplicate detection
    (original 802.11 use)
    Retry attempts due to failed ACK reception can lead to reception of multiple copies of a single MPDU
    Sequence number allows identification of duplicate frames
    Applicable to MMPDU
Re-ordering at the recipient
    (11e extension)
    When BlockAck is used, frames can be delivered out of order
    MAC Sequence numbers allow recipient to determine correct order for delivery to layer above
    BlockAck not supported for MMPDU
      Tgae sentiment is to not modify this part of the protocol

## Slide 4: 802.11 Baseline MMPDU SEQ NUM
Non-QoS STA
  All SEQ NUM from one counter for all frames (7.1.3.4.1)
QoS STA
  MMPDU SEQ NUM assigned from a SEQ space shared with MCAST QoS MSDUs and all non-QoS Data frames (7.1.3.4.1)
  Other frames use one SEQ NUM counter per TID, RA (7.1.3.4.1)

## Slide 5: 802.11 Baseline Duplicate Detection
Recipient can detect duplicates by storing one SEQ NUM per TA = last received SEQ NUM of the group
  E.g. last RX SEQ NUM of MCAST MSDU, non-QoS Data frame, MMPDU
This originally worked because there can only be one frame of the group from each TA outstanding at any time
  I.e. pre-11e-QoS-baseline had only one TX queue
      Transmissions are always in queue order, with no attempts from later frames until current frame has been completed
  Recipient keeps only the last received SEQ NUM for that TA
  Rejects as duplicate only if RETRY=1 and SEQ NUM + TA is an EXACT MATCH – i.e. NOT a check for “old”

## Slide 6: 802.11 Baseline Behavior Non-QoS STA
Non-QoS STA
  PS-induced missed duplicate
    AP transmits SEQ=N, STA receives SEQ=N
    AP fails to receive ACK for SEQ=N
    TBTT occurs, AP sends Beacon + MCAST
    STA receives MCAST with SEQ=N+1
    AP finishes MCAST, resends SEQ=N with RETRY=1
    STA receives SEQ=N, RETRY=1, compares to SEQ=N+1, does not declare duplicate, does not discard duplicate
    Problem is avoided if SEQ=N retry is completed BEFORE Beacon transmission begins
      Spec seems to mandate this (see 11.1.2.1)

## Slide 7: DCF-Baseline Missed Duplicate
DCF all share one SEQ space
  DATA SEQ=N retransmission interrupted by TBTT
  Recipient replaces Duplicate Cache entry N with MCAST SEQ N+1
  Retransmission of SEQ=N is not detected as duplicate
  Only when PS is used
Data
SEQ=N
AP
STA
ACK
SEQ=N
MCAST
SEQ=N+1
DCF TX
PS-mode MCAST
STA passes Data SEQ=N to next layer
Data
SEQ=N
ACK
SEQ=N
STA passes Data SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!
BCN
TBTT

## Slide 8: 802.11 Baseline Behavior QoS STA
QoS STA
  One SEQ NUM counter per TID per RA, for QoS MSDUs
  One SEQ NUM counter for all MGMT, all MCAST QoS Data, all non-QoS Data
    PS-induced missed duplicate
      Same as previous, except MGMT frame instead of DATA frame
    EDCA-induced missed duplicate
      Same as previous except MGMT frame instead of DATA frame, and this occurs when there are no PS STAs causing PS buffering of MCAST
        MCAST sent as AC_BE
        MGMT sent as AC_VO (shares SEQ NUM space with MCAST)
      AP switches between these queues in between retry attempts
      EDCA protocol requires switching queues based on backoff outcome
        Could always buffer MCAST as though PS is present

## Slide 9: EDCA-Induced Missed Duplicate
AC_BE MCAST frame wins backoff
  AC_BE transmission with different SEQ number occurs before retransmission of AC_VO frame
  Recipient replaces Duplicate Cache entry N with N+1
  Retransmission of SEQ=N is not detected as duplicate
  Happens if PS is not used, and, despite 11.1.2.1
MGMT
SEQ=N
AP
STA
ACK
SEQ=N
MCAST
SEQ=N+1
AC_VO TX
AC_BE TX
STA passes MGMT SEQ=N to next layer
MGMT
SEQ=N
ACK
SEQ=N
AC_VO backoff
STA passes MGMT SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!

## Slide 10: MFQ MMPDU Duplicate Detection
With MFQ, MMPDU transmitter sends MMPDUs through different ACs
Differential AC delivery yields mixed MMPDU attempt re-transmission order
  EDCA-induced missed duplicate rejection is aggravated
    Now it can happen even when PS is being used
Need to split the SEQ NUM space among different MMPDU AC delivery priorities
  Just as was done for MSDUs under 11e-QoS
  This fixes EDCA-induced missed duplicate rejection problem

## Slide 11: MFQ-Aggravated EDCA-Induced Missed Duplicate
AC_BE MGMT frame wins backoff
  AC_BE transmission with different SEQ number occurs before retransmission of AC_VO frame
  Recipient replaces Duplicate Cache entry N with N+1
  Retransmission of SEQ=N is not detected as duplicate
  Happens if PS is not used, and, despite 11.1.2.1
MGMT
SEQ=N
AP
STA
ACK
SEQ=N
MGMT
SEQ=N+1
MGMT
SEQ=N
ACK
SEQ=N
AC_VO TX
AC_VO backoff
AC_BE TX
STA passes MGMT SEQ=N to next layer
STA passes MGMT SEQ=N to next layer
DUPLICATE DELIVERED TO NEXT LAYER!
AGGRAVATED = More choices possible – MCAST or MGMT from various AC, no longer confined to non-PS case
ACK
SEQ=N+1

## Slide 12: MFQ MMPDU Sequence Num Proposal (1)
Assign UCAST MMPDU SEQ NUM per AC
  Recipient needs to determine duplicates despite EDCA
    Assuming no Block Ack for MGMT frames
  Duplicate detection must be per AC, because SEQ NUM space is per AC
    Therefore, recipient needs to know AC and cache last SEQ per {AC, TA} for MGMT frames
Explicit AC signalling using portion of SEQ space
  Use two bits of SEQ number for MGMT frames for AC signalling
    Leaves 2^10 = 1024 total SEQ numbers per AC for MGMT frames
      Maximum required is only 1 bit for SEQ space, since Block Ack for MGMT is not supported
      Comparison to last cached value is for EXACT match, not “older than”
      Frames are always delivered in order within each AC queue

## Slide 13: MFQ MMPDU Seq_control field
Reserved bits used by MSDUs to signal FRAG
  Not used by MMPDUs
AC is signalled with 2 bits from SEQ portion
SEQ space is reduced to 10 bits
  But only 1 bit of SEQ is really needed
    Cache contains last received frame SEQ for this TA, AC for MGMT
    Block Ack is not used for MGMT frames, so only EXACT match matters
    RETRY FAIL sequence suggests more than 1 bit is needed, 2? 3?
Reserved
AC
SEQ
SEQ_CONTROL field
Bits
B0
B3
B4
B5
B6
B15
4
2
10

## Slide 14: MFQ MMPDU Sequence Num Proposal (2)
MCAST MMPDU SEQ NUM – no change
  Legacy (i.e. non-TGAE STA) can receive MCAST MMPDU
  Should not cause duplicate detection problems for legacy STA
  Therefore, cannot change SEQ numbering for MCAST MMPDU
  Therefore, all MCAST MMPDU must be sent from same queue
    I.e. to avoid EDCA-aggravated missed duplicate detection
  MCAST MMPDU SEQ space still shared with MCAST QoS and all non-QoS MSDUs
    All of these frames should be sent with one AC to avoid EDCA-induced missed duplicate detection
Therefore, for MFQ, MCAST MMPDU shall be sent AC_BE (non-PS case)

## Slide 15: References