## Slide 1: VHT-LTF sequence for 80 MHz
Date: 2010-07-12
Authors:

## Slide 2: Abstract
The spec framework document specifies the tone allocation for 80 MHz transmissions (number and location of pilot, guard and DC tones) [1]. This document proposes a VHT-LTF frequency domain sequence for 80 MHz transmissions and the phase rotations to be used in each 20 MHz sub-band. The proposal minimizes the peak-to-average power ratio during VHT-LTFs assuming pilot tracking during VHT-LTFs as suggested in [2].

## Slide 3: VHT LTF sequence structure
Let us assume that the VHT-LTF sequence is constructed by
  using all 11n40 tones on both 40 MHz subchannels, with filling of missing tones and applying a phase rotation on each 20MHz subchannel
  Missing tones
    interp40NullL(3 tones), interp80ExtraL (4 tones), interp80ExtraR (4 tones) , interp40NullR(3 tones)
  [c1 c2 c3 c4] is the phase rotation pattern consisting of {+/-1,+/-j} values

## Slide 4: Search for the optimal VHT-LTF sequence
Assuming the VHT-LTF structure of previous slide, to minimize the
PAPR, we need to optimize
  Missing tone values
  20 MHz phase rotations, [c1 c2 c3 c4]
In [2], during VHT-LTFs, pilot tones are multiplied by an R value, while other tones are multiplied by a P value
  Optimization needs to consider the impact of different P and R values

## Slide 5: Search for the optimal VHT-LTF sequence(cont’d)
VHT-LTF sequence optimization done by finding a sequence that minimizes the maximal PAPR over all possible P and R values, i.e.,
  where S are LTF sequences for all possible missing tone values and 20MHz phase rotations
It turns out that PAPR only depends on product of P and R values
  {P,R}={ej,1} and {-ej,-1} give same sequence rotated by 180 degrees

## Slide 6: Optimal VHT-LTF sequence
The parameters which result in the optimal VHT-LTF
  Phase rotation [c1 c2 c3 c4] = [1 -1 -1 -1]
  [interp40NullL, interp80ExtraL, interp80ExtraR, interp40NullR] = [1 -1 1, 1 -1 1 -1, 1 -1 -1 1, 1 -1 1]
Optimal VHT-LTF pattern (excluding phase rotation per 20 MHz subchannel) is
  where the 4 rows correspond to the four 20 MHz subchannels
P x R values | 1 | -1 |  | 
PAPR (4x os) | 5.11dB | 5.17dB | 5.19dB | 5.21dB
Table: PAPR of the optimal VHT-LTF sequence for different values of P and R

## Slide 7: Phase rotations in legacy portion for 80 MHz
  For simplicity, recommend re-using the optimal VHT-LTF phase rotation in the legacy and VHT portions of the packet for 80 MHz
    Rotation of [1 -1 -1 -1] (optimal for VHT-LTFs) gives 3~4 dB lower PAPR than without rotation ([1 1 1 1]) in the legacy portion
Phase Rotations per 20 MHz band | PAPR (2x oversampled) |  | 
 | L-STF | L-LTF | L-SIG
[c1 c2 c3 c4] = [1 1 1 1] | 8.1dB | 9.2dB | 12dB
[c1 c2 c3 c4] = [1 -1 -1 -1] | 4.3dB | 5.4dB | 9.4dB

## Slide 8: Conclusions
Proposed a VHT-LTF sequence for 80 MHz and phase rotations per 20 MHz sub-band
  Minimizes the PAPR during VHT-LTFs
Recommend re-using the optimal VHT-LTF phase rotations for other portions (both legacy and VHT) of the PPDU in 80 MHz transmissions

## Slide 9: Strawpoll 1
Do you accept the VHT-LTF sequence specified on slide 6 of this document (without phase rotations) as the base VHT-LTF sequence for 80 MHz and agree to add the following text to the spec framework document?
“In a 80 MHz transmission, the VHT-LTF sequence to be transmitted (on subcarriers -122 to 122) shall be:
”
  Y
  N
  A

## Slide 10: Strawpoll 2
Do you accept the (per 20 MHz) phase rotations specified on slide 6 of this document for VHT-LTFs in 80 MHz transmissions and agree to add the following text to the spec framework document ?
In the VHT-LTF sequence of an 80 MHz VHT PPDU, subcarrier k, where
, shall be multiplied by the following function of k, prior to transmission:
  Y
  N
  A

## Slide 11: Strawpoll 3
Do you agree to extend the phase rotation on VHT 80 MHz LTFs to the 80 MHz legacy preamble, VHT preamble and data portion and add the following text to the spec frame work document?
“In all elements of an 80 MHz VHT PPDU , i.e., the L-STF, L-LTF, L-SIG, VHT-SIG-A, VHT-LTFs, VHT-SIG-B and the Data, the same function of k shall be used to multiply subcarrier k, prior to transmission”
  Y
  N
  A

## Slide 12: References
[1] 09/0992r11, “Proposed Specification Framework for Tgac”
[2] 10/0771r0, “Phase Tracking during VHT-LTF.ppt”