## Slide 1: 11ac Auto-Detection: Further Results
Date: 2010-07-14
Authors:

## Slide 2: Proposed VHT-SIG-A Format
Scheme | OFDM Symbol #1 | OFDM Symbol #2
Proposed (10-0750) | BPSK | S-QPSK
10-0459 | BPSK | QBPSK
10-0628 | BPSK | BPSK and QBPSK on different tones

## Slide 3: Motivation for Proposed Scheme
Better detection of VHT-SIG-A bits in multipath
  Overall 0.5-1dB SNR gain
  Nearly same performance as L-SIG
Better solution than previous proposals
  Compared to 10-0459
    Better protection of VHT-SIG-A
    Lower 11n false detection in devices using both HT-SIG symbols
  Compared to 10-0628
    Better protection of VHT-SIG-A
Better modulation than BPSK
  Compelling case to adopt S-QPSK for VHT-SIG-B and Data Payload

## Slide 4: Simulation Conditions
20 MHz Channel
Channel Model: DNLOS
  Channel profiles are not normalized
Channel Estimation (non-ideal)
SISO System
Consider Three Scenarios:
  AC packets are sent to AC Receiver
    Check miss detection rate and packet error rate of VHT-SIG-A;
  Legacy packets are sent to AC Receiver
    Check false detection rate of BPSK modulated date symbols (worst case for BPSK+SQPSK scheme)
  SQPSK used for VHT-SIG-B
    Check Packet Error Rate

## Slide 5: AC packets to AC Receivers

## Slide 6: VHT-SIG-B Performance
Assuming VHT-SIG-B carries 26 information bits and thus occupies 1 OFDM symbol
with 1/2 –Rate coding; Channel Model D

## Slide 7: 11ac Payload with S-QPSK
3/4–Rate coding; 400 bit payload; Channel Model D

## Slide 8: Conclusions
We propose that the second VHT-SIG-A symbol be modulated using S-QPSK
This approach has two main advantages
  VHT-SIG-A error rate improves in multipath channels
    We show 0.5-1dB gain in Channel D (42 information bits)
    Will be even higher for longer VHT-SIG-A lengths (if more bits are required)
  Lower false alarm rate for 11n receivers
S-QPSK can also be used in 11ac for
  VHT-SIG-B
    We show >2dB gain in Channel D
  Data Payload
    Even higher gains with higher rate coding

## Slide 9: Strawpoll
Do you agree that S-QPSK modulation be evaluated further for use in VHT-SIG-A, VHT-SIG-B and data portions of the 11a packet?