## Slide 1: Phase Rotations for VHT 80 MHz
Date: 2010-07-14
Authors:

## Slide 2: Abstract
In 10/0802r0, we proposed for 80 MHz, a VHT-LTF sequence and the phase rotations to be used in each 20 MHz sub-band
  The proposal minimizes the peak-to-average power ratio during VHT-LTFs
    Assuming pilot tracking during VHT-LTFs as suggested in [3]
Other contributions on this topic
  10/0791r1 discussed potential issues when using a phase rotation which is not [1 j] for an 11n 40 MHz device
  10/0795r0 showed the performance of various phase rotations for legacy section
In a subsequent motion in TGac, the 80 MHz VHT-LTF base sequence (without phase rotations) was adopted
This document attempts to converge on the phase rotation values, only for VHT section of the PPDU
  Further discussions might be needed for consensus on rotations in legacy section

## Slide 3: Optimal VHT-LTF sequence
Parameters which result in the optimal VHT-LTF as shown in 10/0802r0
  Phase rotation [c1 c2 c3 c4] = [1 -1 -1 -1]
  [interp40NullL, interp80ExtraL, interp80ExtraR, interp40NullR] = [1 -1 1, 1 -1 1 -1, 1 -1 -1 1, 1 -1 1]
Optimal VHT-LTF pattern (excluding phase rotation per 20 MHz subchannel) is
  where the 4 rows correspond to the four 20 MHz subchannels
P x R values | 1 | -1 |  | 
PAPR (4x os) | 5.11dB | 5.17dB | 5.19dB | 5.21dB
Table: PAPR of the optimal VHT-LTF sequence for different values of P and R

## Slide 4: Conclusions
TGac has already adopted a 80 MHz frequency domain sequence for VHT-LTF
Recommend adopting the phase rotation of [1 -1 -1 -1] in the VHT section of the PPDU for 80 MHz transmissions
  Results in the minimum PAPR for the VHT-LTFs

## Slide 5: Strawpoll 1
Do you accept the (per 20 MHz) phase rotations specified on slide 6 of 10/0802r0 for all VHT sections of the PPDU in 80 MHz transmissions and agree to add the following text to the spec framework document ?
“ In the VHT section of an 80 MHz VHT-mixed format PPDU, subcarrier k, where , shall be multiplied by the following function of k, prior to transmission:
  ”
  Y
  N
  A

## Slide 6: References
[1] 10/0802r0, “VHT-LTF sequence for 80 MHz”
[2] 09/0992r11, “Proposed Specification Framework for Tgac”
[3] 10/0771r0, “Phase Tracking during VHT-LTF”
[4] 10/0795r0, “PAPR reduction of Legacy portion of VHT PLCP Preamble”
[5] 10/791r1, “Phase Rotation for the 80 MHz 802.11ac Mixed Mode Packet”