## Slide 1: Replies to Q&A following 10/0788r2
Date: 2010-07-14
Authors:

## Slide 2: Abstract
This presentation provides answers to the Q&A session in the PM1 TGaa meeting on Tuesday during the July 2010 San Diego IEEE plenary

## Slide 3: Answers to Q&A (1)
Should the “question” for data frame reception be incorporated as a separate frame or within a more robust header of the same?
  Yes. In making the mechanism consistent with the existing standard(s), the BAR in Block ACK essentially is a similar “question”, so the proposal should modify the MRG BAR and not modify the data frame header.
Should the “question” be asked before or after data tx?
  Afterwards, as it is done in 11n Block ACK and 11aa MRG
Specification of leader selection mechanism in 11aa?
  We agree to the commenter that an “out of scope of 11aa” note is required
Scalability of existing MRG-BA with the number of group members
  Although it is true that not all group members need to be addressed in the MRG BAR, once only a subset is addressed:
    this subset needs to be determined (leader-selection for several leaders)
    for the non-addressed group members, no feedback (not even implicit) is obtained

## Slide 4: Answers to Q&A (2)
Problem that the leader may roam or otherwise “leave”
  Since leader selection is out of scope, it shall not be a pre-requisite in the standard that the “weakest” receiver in a group has to be the leader.
  “weakest within the group” does not imply that this station has a very bad reception and will thus roam / de-associate
  When the leader leaves unexpectedly, this results in no more positive ACKs being received, but it does not break anything. It would decrease efficiency, but not reliability
Frequency of update of the leader role
  Since the selection algorithm shall not be specified, also the frequency shall not be specified.
  But: The minimum granularity for probing group members for signal strength is the block size. After each block, it shall be possible to switch between MRG BA and aggregate BA
Does this assume that the leader always uses the smallest AID?
  No. The bitmap offset may start anywhere. The bitmap itself can be made a circular map or not be used at all, since only 1 station needs to be addressed

## Slide 5: Answers to Q&A (3)
Timing requirements to cancel ACK by NACK
  Requirements are less strict than for MRG BA, where NO overlap is tolerable. In this scheme, though, overlap is desired and the amount of overlap is controllable and rather uncritical.
  Example:
    OFDM 20MHz: aSlotTime = 9us, thus SIFS tolerance ±900ns, SIFS duration <16us, airPropagationTime for 3km: 10us.
    Length of shortest 802.11 OFDM frame (ACK, 11 symbols): 44us >> 10us+900ns
  Or: Define NACK to be longer than ACK
Timing requirements concerning the hardware
  Immediate Block-ACK and consequently MRG Block-ACK have to be sent immediately after the corresponding BAR, so the requirements w.r.t the hardware processing time are the same

## Slide 6: Answers to Q&A (4)
Overlay-FEC: Are upper layer protocols available?
  Yes. RTP-FEC defines an extension header / payload type to RTP, where RTP packets either carry (systematic) data or parity e.g., cf. RFC2733:
    “FEC Packet: The forward error correction algorithms at the transmitter take the media packets as an input. They output both the media packets that they are passed, and new packets called FEC packets. The FEC packets are formatted according to the rules specified in this document.”
Requirement for Deep Stateful Packet Inspection for Overlay-FEC and thus increased AP complexity
  Packet classification at the AP is one possibility.
  But we may also rely on pre-classified packets using SCS and 802.1

## Slide 7: Exemplary Leader Selection Results
802.11a DLS test result
Simple 4 STA scenario with arbitrary but slow movement of STAs
Simple dynamic leader selection (DLS) implemented
  Probe STAs every 100ms, average over 3 RSSI values and set the weakest according to this as the leader
Measurement parameter | Fixed Leader | DLS
SW ACK loss | 0.894134 | 0.992322
HW ACK loss | 0.883892 | 0.967472
SEQ loss at STA1 | 0.000137 | 
SEQ loss at STA2 | 0.000168 | 
SEQ loss at STA3 | 0.000246 | 
SEQ loss at STA4 | 0.000138 | 

## Slide 8: Straw poll
Does TGaa regard the issues raised to be covered and all open questions answered?
Yes:
No:
Abstain:

## Slide 9: References
doc.: IEEE 802.11-10/0788r2
doc.: IEEE 802.11-10/0768r2
doc.: IEEE 802.11-09/1150r2
doc.: IEEE 802.11-09/0290r1