## Slide 1: Replies to Q&A following 10/0788r2
Date: 2011-03-07
Authors:

## Slide 2: Abstract
This presentation aims to provide revised answers to the Q&A session in the PM1 TGaa meeting on Tuesday during the July 2010 San Diego IEEE plenary

## Slide 3: Definitions
JAR: Jamming-Ack-Request, cf. BAR
JA: Jamming-Ack, cf. BA
weak STA: STA which may be about to roam to another AP of the same ESS
LAF: Leader announcement frame

## Slide 4: Answers to Q&A, revisited (1)
Should the JAR be self-contained or incorporated into each/some data frame(s) (e.g. by means of a preamble extension)?
  The proposal should extend the GCR BAR and thus make the JAR self-contained, for two main reasons:
    Implementation complexity is reduced when JAR-JA is kept similar to BAR-BA.
    Compatibility issues with legacy STA are avoided.
Should the JAR be issued before or after data tx?
  In analogy to GCR BAR-BA: each JA shall be directly preceded by a JAR
Specification of (one/some/any) leader selection mechanism for JAR-JA?
  Similarly to rate adaptation, leader selection is out of scope of 802.11aa
Scalability of existing GCR BAR-BA with the number of group members
  GCR BAR-BA may address a subset of the group, thus collecting partial feedback.
  This implies the following:
    this subset needs to be determined (which is assumed out of scope of 802.11aa)
    for the group members outside this subset, no feedback is obtained
  Unsolicited retries may help reduce BAR-BA overhead, but do not generate feedback
  Hence, JAR-JA is an additional mechanism that has the following properties
    It has limited feedback overhead
    but still gathers feedback (implicitly) from all members of the group

## Slide 5: Answers to Q&A, revisited (2)
Problem that the Leader receiver may roam or otherwise disappear
  We have previously shown (cf. 10/0768r2) that the JAR-JA protocol performs best when the Leader receiver experiences the lowest SNR within the group (i.e. the “weakest” receiver)
  Since leader selection is out of scope, this shall not be standardized in 802.11aa
  “weakest” within the group does not necessarily imply that this station is indeed a weak STA
  Still, the Leader may disappear (e.g. due to power-loss):
  When the leader leaves unexpectedly, this results in absence of positive ACKs and thus possibly unnecessary retransmissions.
  The leader disappearing unnoticed is presumably a rare event. The effect is limited to a temporary decrease in overall throughput until the AP detects the missing of the Leader
  The GCR AP could have multiple STA as potential Leaders or test if the Leader is “alive” immediately before JAR-JA.
  We do not limit the scheme to BSSs and we do not tie any STA to the current AP.
Frequency of update of the Leader role
  Since the Leader selection is out of scope, also its frequency shall not be specified. The update frequency is a parameter that is dependent on the fading scenario.
  Yet, it may be necessary to switch the Leader after each JAR-JA exchange.

## Slide 6: Answers to Q&A, revisited (3)
Is it assumed that the leader always uses the smallest AID?
  No. The bitmap offset may start anywhere. The bitmap itself can be made a circular map or not be used at all, since only 1 station needs to be addressed
Timing requirements to cancel positive feedback
  We have shown that cancellation is not timing critical. As long as there is an overlap, positive feedback is cancelled with a predictable probability
  Example:
    OFDM 20MHz: aSlotTime = 9us, SIFS tolerance ±0.9us airPropagationTime for 3km: 10us.
    Even short frames can be cancelled: 6 Mbps 11a ACK: 11 OFDM symbols 44us >> 10us+0.9us
Hardware implementation complexity
  GCR BA is sent immediately after the corresponding BAR, so with respect to this aspect, the implementation complexity stays the same for JAR-JA
  If Leader role can be switched on a per JAR-JA basis, a STA needs to determine for each JAR if it is the Leader.

## Slide 7: Answers to Q&A, revisited (4)
Overlay-FEC: Are upper layer protocols available?
  Yes. RTP-FEC defines an extension header / payload type to RTP, where RTP packets either carry (systematic) data or parity e.g., cf. RFC2733:
    “FEC Packet: The forward error correction algorithms at the transmitter take the media packets as an input. They output both the media packets that they are passed, and new packets called FEC packets. The FEC packets are formatted according to the rules specified in this document.”
Requirement for Deep Stateful Packet Inspection for Overlay-FEC and thus increased AP complexity
  Packet classification at the AP is one possibility.
  But we may also rely on pre-classified packets using SCS and 802.1

## Slide 8: Leader Management
Leader may be selected by received SNR
  AP probes STAs via GCR BAR-BAs
    When exactly / period: out of scope
    At least when the current designated Leader leaves
  Could rely on 802.11k, 802.11v?
Leader announcement
  A LAF may introduce more protocol overhead than signaling the Leader role within the JAR-JA exchange
  A LAF lends itself to reduce JAR processing complexity at the group member STAs. Additionally, the indoor environment is typically slow fading
  Drawback of LAF: Compensating the disappearance of the leader will take more time, thus throughput is degraded for a longer period.

## Slide 9: Straw poll
Does TGaa regard the issues raised to be covered and all open questions answered?
Yes: 1
No: 1
Abstain: 7

## Slide 10: References
doc.: IEEE 802.11-10/0788r2
doc.: IEEE 802.11-10/0768r2
doc.: IEEE 802.11-09/1150r2
doc.: IEEE 802.11-09/0290r1