## Slide 1: Achievable gains in AP Discovery
Date: 2010-07-15
Authors:

## Slide 2: Abstract
Based on the ongoing discussion in FIA SG, there requests were risen to elaborate how all phases being part of an initial link set-up could be shortened.
This document presents some initial toughs on improving AP discovery. Assumptions for the calculation of the duration of AP discovery are added and resulting numbers revised.
Attention: References to IEEE 802.11 refer to REVmb D4.0 (before the renumbering of clauses as part of the revision process)

## Slide 3: AP Discovery
Passive scanning
Active scanning
No Assumptions (scan all channels), find all APs
2.4 GHz
5 GHz
Reduce number of channels (to 1) where APs are known to operate
Enablement at 5GHz via 2.4 GHz
2.4 GHz
5 GHz
2.4 GHz
5 GHz
1100 ms
Expected Mean of time spent in scanning for
2300 ms
102 ms
n/a
17 ms
n/a
100 ms
100 ms
Return after 1st AP Responses (scan 1 channel)
50ms
50ms
2 ms
n/a
2.4 GHz
5 GHz
50ms
50ms
2 ms
2 + ε ms
No Assumptions (scan all channels), stop after 1st APs is found
2.4 GHz
5 GHz
550 ms
1150 ms
22 ms
n/a
Amendment required
11k may work,
But not for initial link set-up
Amendment required
Amendment required
Amendment required
Attn.: 1 additional scan (active or passive) afterwards for joining the BSS.
Assume active scanning: today: 17ms  tomorrow 2ms

## Slide 4: Stop Scanning after 1st AP is found
Passive scanning
  Allows such behavior: “shall listen to each channel scanned for no longer than a maximum duration defined by the MaxChannelTime“ [11REVmb-D4, Cls 11.1.3.1]
  Realization is vendor specific. Currently, there is not option to the MLME-SCAN.request primitive forcing this behavior
Active scanning:
  Not possible right now: “…. [scan until] ProbeTimer reaches MaxChannelTime, process all received probe responses“ [11REVmb-D4, Cls 11.1.3.2.2]

## Slide 5: Scan only a channel where an AP operates
Moving from one BSS to another (note: not scope of FIA SG, but mentioned for completeness)
  11k neighbor report can provide information on which channels APs operate
Initial link-set up
  Not possible right now (STA is not within a BSS in order to query a neighbor report)

## Slide 6: Enablement at 5GHz via 2.4 GHz
Currently, a STA has to receive a Beacon before operation ….
  Upon receipt of an MLME-JOIN.request primitive, the STA shall use the synchronization procedure described in 11.1.3.4
  STA is required to receive a Beacon in order to obtain (Cls 11.1.3.4 § 1):
    channel synchronization information (FH PHY only)
    TSF timer value
Rules for operation under spectrum management (802.11REVmb-D4, Cls. 11.9.0a, DFS)
  Receive Beacon or Probe Response (with Spectrum Management Bit in Capabilities set to 1)
  OR: STA can determine that it is in a regulatory domain that does not require DFS
  OR: STA can ensure that it will meet regulatory requirements even if DFS is not employed
Legislation does not affect idea of enablement to shorten AP discovery time since STA has to receive beacon during JOIN phase
Notes: Note: the parameters of MLME-JOIN.request contain a “probe delay” which applies if “active scanning” is used (Cls. 10.3.3.1.2). As the call of the primitive is in order to “This primitive requests synchronization with a BSS“ (Cls. 10.3.3.1.1), the only permissible approach is defined in 11.1.3.4 reception of a beacon (and not a probe response). This looks like is has been an error while amanding the baseline. Correct or request clarification.
Note: Fig. 11-3 is also missleading or wrong. It shows that MaxChannelTime measurement starts after MinChannelTime end. According to section (f) above the figure, there is only one timer which is not reset. Hence, the durations should overlap.

## Slide 7: Details on calculation of Expected Mean values

## Slide 8: Parameters
Number of channels: 11 for 2.4 GHz; 23 for 5 GHz
Beacon interval: 100 ms
Idle channel
Do not account for time to switch RF from one channel to another
Parameters for active scanning [1]:
  ProbeDelay = 0.1 ms
  MinChannelTime = 0.67 ms
  MaxChannelTime = 15 ms

## Slide 9: Passive Scanning
Time to find all APs an all channels (n):
  N * TBTT = n * 100ms
Time (expected mean) to find first AP by scanning all channels (until AP found)
  Find AP on
    1st channel: 50 ms (= ½ TBTT)
    2nd channel: 100 ms (=TBTT) + 50 ms (= ½ TBTT)
    3rd channel: 2* TBTT + ½ TBTT
    Nth channel: n*TBTT + ½ TBTT
  Expected mean = 1/n SUM_n ( n * TBTT + ½ TBTT) = TBTT (n-1)/2 + TBTT/2 = N/2 * TBTT

## Slide 10: Active Scanning
The time spent in active scanning highly depends on the number of channels where at least one AP operates on.
  Channel idle / no AP operating on that channel  wait for MinChannelTime and go to next channel
  If at least one AP responds within MinChannelTime, wait until MaxChannelTime expires (and catch al responses within that time span) and move on
Assumption: One AP
  Scan all channels, find all APs: (n-1) * MinChannelTime + MaxChannelTime + n*ProbeDelay + n * time for ProbeReq. Frame transmission
  Scan all channels, stop after 1st AP found: (n-1)/2 * MinChannelTime + MaxChannelTime + n/2 * ProbeDelay + n/2 * time for ProbeReq Frame transmission
Assumption: at least one AP on every channel
  Scan all channels, find all APs: n* MaxChannelTime + n*ProbeDelay + n * time for ProbeReq. Frame transmission
  Scan all channels, stop after 1st AP found: MaxChannelTime + ProbeDelay + time for ProbeReqFrame
Assumption: at least one AP on channel 1, 6, 11; no AP on others
  Scan all channels, find all APs: (n-3) * MinChannelTime +3 * MaxChannelTime + n*ProbeDelay + n * time for ProbeReq. Frame transmission
  Scan all channels, stop after 1st AP found: (3-1)/2 * MinChannelTime + MaxChannelTime + 3/2 ProbeDelay + 3/2 * time for ProbeReq
Use average of the resulting duration coming from the three assumptions per scenario

## Slide 11: References
[1] M. Ryong Jeong, F. Watanabe and T. Kawahara, ”Fast Active Scan for Measurement and Handoff,” DoCoMo USA Labs, Contribution to IEEE802, May 2003.