## Slide 1: Smart Grid and Key Lengths
Date: 2010-08-09
Authors:

## Slide 2: Abstract
This submission reviews security in IEEE 802.11 with respect to the Draft NIST IR-7628. The primary concern is cryptographic modules and key lengths. Also this submission reviews a level of effort to extend key lengths in IEEE 802.11.

## Slide 3: Security within IEEE 802.11
IEEE 802.11i RSN
  Assumes key of sufficient strength derived by 802.1X/EAP– authentication, key establishment, (some) key derivation outside scope of 802.11i.
  4-Way Handshake
    Key derivation using HMAC-SHA1 of 384-bit PTK
    Key confirmation using HMAC-SHA1 with 128-bit KCK
  Group Key Handshake
    NIST AES key wrap with 128-bit KEK
  CTR with CBC-MAC Protocol (CCMP) with 128-bit TK
IEEE 802.11r – Not reviewed
IEEE 802.11w – Not reviewed
IEEE 802.11s draft – Not reviewed

## Slide 4: IEEE 802.11i
CTR with CBC-MAC Protocol (CCMP)
  128 bit key, and 64 bit MIC
  From NISTIR 7628 volume 2,
    Table 6-4 lists CCM with AES-128, AES-192 & AES-256 from now and beyond 2030
    Does not mention MIC size!
HMAC-SHA1
  128-bit key used for both key derivation and key confirmation
  SP800-57 states that HMAC-SHA1 is acceptable as a key derivation function to provide up to 128-bits of key
AES Key Wrap
  A 128-bit key is used to wrap a 128-bit key

## Slide 5: IEEE 802.11i and Draft NIST IR-7628
Using HMAC-SHA1 to derive a 128-bit key for CCMP (with a 64-bit MIC) should be OK until 2030 under certain assumptions
  the PMK used in the 4-way HS to derive the key for CCMP (the TK) has sufficient entropy
From Draft NIST IR-7628, section 6.2.1.2
  “Cryptographic modules (both software and hardware) that can support increased key sizes and maintain needed performance should be preferred over those that cannot be changed in case a bit-strength reducing vulnerability is found in the cryptographic algorithm.”
  “Over sizing cryptographic design (including but not limited to key size) to not only meet but exceed current security requirements may be prudent to avoid or delay the need for later upgrade.”
Over-sizing cryptographic design requires more than just using a larger key with CCMP
  HMAC-SHA1 is not acceptable for key derivation of 192- or 256-bits.
  An x-bit key cannot wrap a y-bit key if x < y

## Slide 6: If we wanted to increase the key length, what would be needed?
New assumption on the PMK derived from 802.1X/EAP
  PMK will have comparable strength to be used with new cryptographic parameter set
Definition of new AKM(s)
  New key derivation method to expand a PMK of sufficient entropy into a longer PTK
  New key confirmation method and increased length of KCK
  New key wrapping algorithm and/or increased length of KEK
Definition of new Ciphersuite(s)
  New cipher mode to perform authenticated encryption that uses a longer TK
Language governing gratuitous mixing-and-matching of AKMs and Ciphersuites

## Slide 7: References
  Draft NISTIR v1.0 vol 1 – July 2010
    http://collaborate.nist.gov/twiki-sggrid/pub/SmartGrid/NISTIR7628v1July2010/draft-nistir-7628_vol1_final.pdf
  Draft NISTIR v1.0 vol 2 – July 2010
    http://collaborate.nist.gov/twiki-sggrid/pub/SmartGrid/NISTIR7628v1July2010/draft-nistir-7628_vol2_final.pdf
  Draft NISTIR v1.0 vol 3 – July 2010
    http://collaborate.nist.gov/twiki-sggrid/pub/SmartGrid/NISTIR7628v1July2010/draft-nistir-7628_vol3_final.pdf
  SP800-56A, SP800-57, SP800-97
    http://csrc.nist.gov/publications/PubsSPs.html